## Slide 1: F281x Boot-SCIA Flash Programming
Jeff Stafford
Application Report

## Slide 2: Step 1 Transfer CFKA to Unsecured RAM LOAD Addresses
Boot-ROM code controls 28x CPU
Boot-ROM SCI-A code transfers CKFA to LOAD addresses in unsecured RAM
Program Counter set to CKFA entry point when transfer is complete
RS-232
PC or ICT
SCI
Boot-ROM
Unsecured RAM
Entry
Point
28x CPU
CKFA

## Slide 3: Step 2 CKFA Unlocks CSM and Transfers to RAM RUN Addresses
CKFA in unsecured RAM controls 28x CPU
CKFA unlocks CSM
CKFA copies itself from LOAD addresses to RUN addresses in secured RAM
RS-232
PC or ICT
SCI
Boot-ROM
28x CPU
Secured RAM
Unsecured RAM

## Slide 4: Step 3 CKFA Transfers AppCode to RAM Buffer #1
CKFA in secured RAM controls 28x CPU
CKFA uses SCI-A to transfer 4KW of AppCode to RAM Buffer #1
RS-232
PC or ICT
SCI
28x CPU
Boot-ROM
Secured RAM
RAM Buffer #2
RAM Buffer #1
AppCode

## Slide 5: Step 4 CKFA Starts Programming Flash
CKFA in secured RAM controls 28x CPU
CKFA programs flash with RAM Buffer #1 contents
CKFA transfers next 4KW of AppCode to RAM Buffer #2
RS-232
PC or ICT
SCI
28x CPU
Boot-ROM
Secured RAM
RAM Buffer #2
RAM Buffer #1
AppCode
Flash

## Slide 6: Step 5 Flash Programming Completed
Device is reset, setting program counter = 0x3F7FF6
AppCode in flash controls 28x CPU
All RAM available for AppCode use
At 57600 bps, 64 KW program time = 24 sec
RS-232
PC or ICT
SCI
28x CPU
Boot-ROM
Secured RAM
RAM Buffer #2
RAM Buffer #1
Flash
Entry
Point
0x3F7ff6

## Slide 7: Emulated ICT Flash Programming
CKFA and AppCode Transfer to Emulated ICT RAM by RS-232
CKFA Transfer to Target RAM by Boot-ROM Controlled SCI
AppCode Transfer to Target Flash by CKFA Controlled SCI
At 1.875 Mbps, 64 KW program time = 1.4 sec
RS-232
PC
SCIA
28x CPU
Boot-ROM
RAM
(CKFA)
RAM Buffer #2
RAM Buffer #1
CKFA and AppCode
Flash (AppCode)
SCIA
28x CPU
Boot-ROM
Internal RAM (CKFA)
Flash
Emulated ICT (281x eZdsp)
F281x Target
External
RAM
(AppCode)
CKFA and AppCode
RAM
(ICT)
SCIB

## Slide 8: Emulated ICT - HW
Emulated ICT (EICT)
PC RS-232 Interface
CCS JTAG Interface
F281x Target
EICT - Target Direct SCI Connection
Hardware:
(2) F2812 eZdsps From Spectrum Digital
RS-232 Interface from Link Research
JTAG Emulator from Spectrum Digital
Software:
PC = HyperTerminal
EICT = Application Report EICT SW
Target = Application Report CKFA SW