## Slide 1: Connect the hardware
Notes: For this experiment we will be using channel 3 on the precision labs hardware. First, set the jumpers as shown here. Next, install the OPA320_Goodfilter2 coupon card into the channel 3 socket. This is the amplifier that will not have an antialiasing filter. Connect the PSI to the PLABS board using the SMA cable, and connect the PHI to the PLABS channel 3 connector. Finally, connect the USB cables to the computer. Pause and connect the hardware.

## Slide 2: Measured vs Expected Results
fsamp = 10kHz |  |  |  |  |  |  |  |  | 
Device |  |  |  | Expected |  | Example Measurements |  | Your Measurements | 
 | Device | fin (kHz) | Vin (V) | fmeas (kHz) | Vadc (Vpp) | fmeas (kHz) | Vadc (Vpp) | fmeas (kHz) | Vadc (Vpp)
1 | OPA320 Good filter2 | 0.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.748 |  | 
2 | OPA320 Good filter2 | 10.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.729 |  | 
3 | Sallen-Key | 0.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.711 |  | 
4 | Sallen-Key | 10.1 | 2.9 | 0.1 | 11.6m | 0.1 | 12m |  | 
5 | Sallen-Key (test design) | 5.1 | 0.02 | 4.9 | 0.0 | -na- | 2m |  | 
6 | Sallen-Key (test design) | 5.1 | 2.9 | 4.9 | 44.4m | 4.9 | 45m |  | 
Your results should show the same trend as the expected result but the specific values will differ.
Notes: This table summarizes the calculated, simulated, and measured results for this experiment. Your measured results should be close to the example measurement, but you may see some difference. Remember, to translate Sigma to an RMS noise voltage you multiply by the LSB bit width. Comparing the total simulated noise to the example measurement shows that the two numbers compare very well. Remember, there are many factors that impact noise, so you should not expect the results to match exactly. Pause now and fill in your measurements.