## Slide 1: Aliasing and Anti-aliasing Hands-on Experiment TIPL 4301-L TI Precision Labs – ADCs
by Art Kay
Notes: Hello and welcome to the TI Precision labs hands-on experiment covering aliasing and anti-aliasing filters. In this experiment we will use a hand calculation and software tool to predict the alias frequencies. We will also use software to design an anti-aliasing filter, and TINA SPICE to confirm the filters operation. Finally, we will measure the effects of aliasing and the anti-aliasing filter.

## Slide 2: Required/Recommended Equipment
Calculation
  Simple calculation using Nyquist theorem
  Verification using Analog Engineer’s Calculator
  Anti-Aliasing filter hand calculations
Simulation
  Design of Anti-Aliasing filter using FilterProTM
  Simulation of Anti-Aliasing filter using OPA320 Model
Measurement
  PLABS-SAR-EVM-PDK
  http://www.ti.com/tool/plabs-sar-evm-pdk
  Download EVM software and purchase EVM
Notes: For this lab we will use the Analog Engineer’s Calculator and hand calculations to predict where alias signals appear given the input signal frequency and the sampling rate. Next we will confirm the effectiveness of a second order anti-aliasing filter using hand calculations. We will then design the anti-aliasing filter using an active filter design program called FilterPro. Next we will confirm the active filter’s performance using TINA SPICE. Finally we will measure the aliasing and operation of the anti-aliasing filter.

## Slide 3: Fill in the Alias frequencies Given fs and fin
Signal Amplitude:
Vin = 2.9Vpp
Vcm = 1.5V
Normal Operation:
fin = 0.1kHz
Alias Operation:
fin = 10.1kHz
Sampling rate:
fs = 10ksps
Fill in all the alias frequencies in the diagrams.
Notes: In this experiment we will use the OPA320 Good Filter2 amplifier configuration with the ADS7042. The ADS7042 sampling rate will be set to 10ksps. The Nyquist frequency is half the sampling rate, or 5kHz in this example. Thus, any input signal with a frequency higher than 5kHz will generate alias signals and signals below 5kHz will not generate aliases. The goal for this example is to predict the measured frequency for a 10.1kHz and 0.1kHz input frequency. First we will use a software tool to do this calculation, then we will show the underlying algorithm.

## Slide 4: Analog Engineers Calculator: find Alias frequencies
http://www.ti.com/tool/analog-engineer-calc
Notes: The Analog Engineer’s Calculator has a tool that lets you find the alias signals given the input frequency and the sampling rate. The frequency range from 0Hz to the Nyquist frequency is called the first Nyquist zone. The frequency range from the Nyquist frequency to the sampling rate is called the second Nyquist zone. The first and second Nyquist zones are repeated an infinite number of times. For example, the third and forth Nyquist zone are copies of the first and second. This tool let’s you select the number of Nyquist zones that we will observe.
For this example, the input frequency is 10.1kHz and the sampling rate is 10kHz. This produces aliases at 0.1kHz, 9.9kHz, 10.1kHz, and so forth up to 29.9kHz. Note that there is really an infinite number of aliases and adding more Nyquist zones will reveal more aliases. Again, we are mainly interested in the first Nyquist zone and normally the other zones are hidden. The calculator can be downloaded using the link below, and the software can be selected by choosing “Alias Calculations” under “Data Converters” and choosing the “Alias Frequencies” tab.

## Slide 5: Solutions: Normal Operation vs. Aliased Signal
You see the same FFT results for both a 0.1kHz and 10.1kHz input signal.
Notes: Here is the answer to the two different problems that were given earlier. These problems were both solved using the software we just introduced. For the first problem, the input signal is 0.1kHz, the Nyquist rate is 5kHz, and the sampling rate is 10kHz. Since this input signal is less then the Nyquist frequency we don’t see any aliases in the first Nyquist zone. In the second problem we apply 10.1kHz to a system with the same sampling rate. In this case the signal is above the Nyquist frequency and it produces an alias in the first Nyquist zone at 0.1kHz. Remember the EVM GUI will only display the first Nyquist zone. So if you compare the measured results for the two examples, the FFTs will look identical. That is, for both the 0.1kHz and 10.1kHz signals the FFT measurement will show 0.1kHz. Now let’s look at the math behind the software calculator.

## Slide 6: Hand Calculation to Find Alias Frequencies
Equation
Where
k = -N…-2, -1, 0, 1, 2 …N
N = Nyquist Zones
fs = sampling rate
fin = input frequency
Example
Notes: The alias frequencies can be calculated using the simple equation shown. Where fs is the sampling rate, and fin is the input frequency. Also, k is an integer from –N to N where N is the number of Nyquist zones. To find the alias you take the absolute value k times fs plus fin. On the right you can see the example we discussed earlier solved using this method. In the hands on experiment, we will apply a 0.1kHz and 10.1kHz input signal and compare the FFT results to the theoretically expected results. Before we do this, let’s design an antialiasing filter to minimize the amplitude of the alias.

## Slide 7: Design an Anti-aliasing Filter: find Cutoff
System Requirements
fs = 10kHz, fNyquist = 5kHz
Vin@Nyquist = 20mVpp, FSR = 3V
Resolution = 12 bits
Filter Specifications:
2nd Order Filter, find fc
Goal:
Find fc to attenuate the 20mVpp alias at the Nyquist frequency to less then half an LSB.
Nyquist Frequency
fc = 100Hz
G ≈ -70dB
fc = 800Hz
G ≈ -30dB
fc = 25Hz
G ≈ -90dB
Notes: Any signal above the Nyquist frequency can produce an alias. To avoid aliases you would not intentionally apply a signal greater than the Nyquist frequency; however, you may have an unwanted noise signal at this frequency. In this design example, we will assume that the largest input signal at the Nyquist frequency is 20mVpp. In fact, this signal could range from 0V to the ADC full scale range, but we are assuming that we will not see a signal larger than 20mVpp at the Nyquist. This 20mV level was selected based on the system specifications, and can be adjusted depending on the expected amplitude of noise signals beyond the Nyquist frequency. In general, the antialiasing filter needs to reduce the amplitude of the noise signal to a level that the ADC can no lolger detect; that is, we want to reduce it to less than half of an LSB. In this example we want to use a simple second order filter, so the design goal is to find a cutoff frequency that will get the proper attenuation. For example, you can see with the cutoff at 100Hz the attenuation is about 70dB. [click] If we increase the cutoff frequency to 800Hz you see that the attenuation decreases to 30dB. [click] on the other hand, decreasing the cutoff to 25Hz gives 90dB of attenuation. For best rejection of the alias signal you need to move the cutoff frequency lower; however, this reduces the usable frequency range for the system. In the next slide we will consider the math involved in selecting the best cutoff frequency to give us the required attenuation.

## Slide 8: Design an Anti-aliasing Filter: find Cutoff
System Requirements
fs = 10kHz, fNyquist = 5kHz
Vin@Nyquist = 20mVpp, FSR = 3V
Resolution = 12 bits
Filter Specifications:
2nd Order Filter, find fc
Goal:
Find fc to attenuate the 20mV alias at the Nyquist frequency to less then half an LSB.
Find the required attenuation
Find fc for G = 18.31mV/V at f = fNyquist = 5kHz
Not a closed form equation!
Notes: First, remember that we need to attenuate the alias signal to less than one half of an LSB. Solving this for a 12 bit ADC with a 3V full scale range gives 366uV for half of one LSB. The required gain can be calculated by dividing half an LSB by the amplitude of the alias signal. In this case the gain is 18.31mV/V or -34.7dB. The gain equation for a second order Bessel transfer function is given. We need to solve this equation to get a gain of 18.31mV/V at a frequency of 5kHz. Unfortunately, this equation doesn’t have a simple closed form solution and needs to be solved numerically. This will be true for most filter problems. In the next slide we introduce a software tool to solve this problem.

## Slide 9: Calculator: Find Antialiasing Filter Cutoff
Notes: This software tool finds the cutoff frequency for an antialiasing filter given the filter type, filter order, Nyquist frequency, input alias signal amplitude, ADC full scale range, and ADC number of bits. For this example, the software calculated a 534Hz cutoff frequency will produce a -34.75dB attenuation at the Nyquist frequency. This attenuation will reduce the 20mV alias signal to one half LSB. Thus, the filter will attenuate the 20mV signal to a point where the ADC can no longer detect it.
Using this approach we fixed the order of the filter to two, and adjusted the cutoff frequency to achieve the desired attenuation. Another approach is to fix the cutoff frequency and adjust the filter order to achieve the desired attenuation. Let’s take a look at that.

## Slide 10: Design an Anti-aliasing Filter: find Order
System Requirements
fs = 10kHz, fNyquist = 5kHz
Vin@Nyquist = 20mV, FSR = 3V
Resolution = 12 bits
Filter Specifications:
fc= 1kHz, find Order
Goal:
Find the order to to attenuate the 20mV alias at the Nyquist frequency to less then half an LSB. From previous design Gain is -34.7dB.
fn = 1kHz
Nyquist
G = -34.7dB
1st order
fc = 500Hz
2nd order
3rd order
Notes: Here we will solve the same problem as before, but the cutoff frequency will be fixed at 500Hz and we will find the filter order needed to achieve the desired attenuation. From the previous problem we saw that the target attenuation was -34.7dB. From this graph you can see that a first order filter doesn’t meet that attenuation goal. [click] The second order filter meets this attenuation target exactly, so this is what we would use in the design. [click] Using a higher order filter would provide even better attenuation, but this would add additional complexity and cost to the circuit. On the next slide we will take a quick look at a software tool that finds the antialiasing filter order given a fixed cutoff frequency.

## Slide 11: Calculator: Find Antialiasing Filter Order
Notes: This tab on the Anti-Alias filter designer finds the filter order given the filter type, Nyquist frequency, cutoff frequency, input alias signal amplitude, ADC full scale range, and ADC number of bits. For this example, the software calculated 2nd order filter will produce a -34.75dB attenuation at the Nyquist frequency. The two tabs provide two different ways to solve the same problem. For example, if your design needs to be limited in cost and complexity to a second order filter you can use the tab that solves for the cutoff frequency. On the other hand, if you can use a more complex filter, but need a specific cutoff frequency you can use the tab that solves for filter order.
For this example, we know that filter type, filter order, and filter cutoff frequency. In the next slide we will introduce a software tool that will select filter component values to realize the filter. Pause and run the Analog Engineer’s Calculator anti-alias filter design software.

## Slide 12: Designing the Antialiasing filter
Download FilterPro v3.1
http://www.ti.com/filterpro-dt
Active filter design software.
Run from
Texas Instruments > FilterPro Desktop
Notes: FilterPro is a free active filter design program from Texas Instruments. This software can be downloaded using the provided link. We will use this software to find componants to realize our 2nd order 500Hz Bessel filter. Once you have downloaded and installed the software it can be run under “All Programs > Texas Instruments > FilterPro Desktop”.

## Slide 13: Designing the Antialiasing filter
Select “Lowpass” filter.
Enter gain, cutoff frequency, maximum ripple.
Notes: The first screen you will see in FilterPro is to select the Filter Type. In this case we want a low pass filer. Press “Next” and we can enter the Filter Specifications. In this case we want a gain of 1, and a cutoff frequency of 500Hz. The ripple specification isn’t really pertinent as we are using a Bessel filter and Bessel filters don’t have ripple. Finally, check the filter order as “set fixed”, and select two for a second order filter. Press next to continue.

## Slide 14: Designing the Antialiasing filter
Choose “Bessel” type for maximally flat response.
Choose “Sallen-Key” topology for non-inverting functionality.
www.ti.com/lit/pdf/sloa049
Notes: Now we will choose “Bessel” for the filter response type. Bessel has a maximally flat response and linear phase. Bessel and Butterworth are two commonly used filter types for antialiasing applications. For more details on filter responses use the link to the document at the bottom of the page. Press next to continue. In step 4 we will choose the filter topology. In our example we need a non-inverting configuration so we will use the “Sallen Key filter”. The “Multiple Feedback Filter” on the other hand, is an inverting topology. The link at the bottom of the page will also cover details on the differences between the various filter topologies. Press next to continue.

## Slide 15: Designing the Antialiasing filter
The default tolerance is “exact”. Change according to your design.
Click on the component value “150nF” and change to “10nF”.
Notes: Now we have a schematic with values. However, by default the values are exact values and we really need standard resistor and capacitor values. Using the pull-down menus we can change the resistors to 1% resistors and the capacitors to 5% capacitors. Furthermore, we can edit the component values and all the components will scale accordingly. In this example we change the 150nF capacitor to 10nF and all other components scale to the appropriate standard value. This is a useful feature as a 150nF capacitor is not available as a C0G type, but 10nF will work for C0G.

## Slide 16: Designing the Antialiasing filter
Final circuit with properly scaled component values. Note AC response and group delay below.
Notes: Here we see the final circuit with it’s associate graphs. This output doesn’t take into account the non-ideality of the amplifier. For this reason, it is always recommended to simulate the circuit in TINA SPICE for final confirmations. Pause and run the FilterPro Software.

## Slide 17: Add an Antialiasing Sallen-Key Filter
Click here to open TINA file.
Notes: This slide shows the TINA SPICE frequency response for the filter that we designed using FilterPro. Note that the cutoff frequency is at 500Hz as expected. You can also see that the role off is at 40dB/decade which is what you would expect for a second order filter. Finally, we show the results for a transient simulation for a 2.9Vpp signal at 10.1kHz. 2.9V is used as it is nearly the ADC full scale range. The reason 2.9V is used rather than 3V is to avoid the non-linear region of the amplifier, and to avoid overdriving the ADC. The output of the transient response is 11.6mVpp. This is what you would expect based on the attenuation at 10.1kHz. The equation shown here is another way you can calculate the expected output at 10.1kHz. Note that the transient simulation and hand calculation match. This same approach can be used for other signal frequencies and amplitudes. Later we will fill in a table for several different amplitudes and frequencies. You might have noticed that the output signal appears to be inverted even though circuit is a non-inverting topology. This “inversion” is actually a phase shift introduced by the second order filter.

## Slide 18: OPA320_Goodfilter2 vs. Sallen-Key Filter
Notes: At this point we are ready to start the hands-on experiment. We will be comparing two different circuits. The first circuit that we will look at is called “OPA320 Goodfilter2”. In this case, the filter at the output of the OPA320 is not an antialiasing filter. This filter is designed to minimize transients from ADC charge kickback that occurs during conversion. We will discuss the design of this filter in detail in a later Precision Labs video. For now, it is important to note that this filter cutoff frequency is 9.1MHz and so it will not work as an antialiasing filter as the Nyquist frequency is 5kHz.
The next circuit that we will look at is a Sallen-Key filter. This is the circuit we designed using the Analog Engineer’s Calculator and Filter Pro. The cutoff here is 500Hz and the Nyquist frequency is 5kHz, so this circuit will attenuate any alias signals by at least 35dB. We will measure the effectiveness of this filter in the hands on experiment. Let’s get started.

## Slide 19: Connect the hardware
Notes: For this experiment we will be using channel 3 on the precision labs hardware. First, set the jumpers as shown here. Next, install the OPA320_Goodfilter2 coupon card into the channel 3 socket. This is the amplifier that will not have an antialiasing filter. Connect the PSI to the PLABS board using the SMA cable, and connect the PHI to the PLABS channel 3 connector. Finally, connect the USB cables to the computer. Pause and connect the hardware.

## Slide 20: Start & Setup the Plabs-Power Scaling EVM Software
3. Set Sampling to 10ksps.
1. Select “Plabs-Power Scaling” from “start>All Programs”
4. Press here to expand PSI controls
2. Set number of samples to 16,384.
Notes: Now let’s start the software by selecting the “Plabs-Power-Scaling-EVM” icon from the “Start > All Programs” menu. Once the software is running you should notice the green “HW connected” message at the bottom of the software. [click] Next, change the number of samples to 16,384. [click] Next, change the sampling rate to 10ksps. [click] Finally press here to expand the controls for the PSI hardware. Pause and get the EVM software started.

## Slide 21: Time domain for 0.1kHz and 10.1kHz look the same
finput = 0.1kHz
Vin = 2.9V
Offset = 0V
finput = 10.1kHz
Vin = 2.9V
Offset = 0V
100 Samples
tsample = 1/fsample = 1/10kHz = 0.1ms
Tperiod = Nsample∙tsample∙ = 100 ∙0.1ms=10ms
f = 1/ Tperiod = 1/10ms = 100Hz
Notes: Now we can apply a 0.1kHz and 10.1kHz signal to the ADC and look at the response. These are the signals that we used in the alias calculator earlier. Based on our earlier results, we expect to see a 0.1kHz signal for both input frequencies. The 10.1kHz input signal should product a 0.1kHz alias signal.
First, enter the input frequency of 0.1kHz, set the amplitude to 2.9V, and set the offset to 0V. Press “update” and turn on the output. Press capture and you should see the output signal. Left click and drag on the time domain display to zoom in on the signal so that 200 samples are visible. [click] The horizontal axis can be converted to time. The time for each point is equal to one divided by the sampling rate. For this example 1/10kHz is equal to 0.1ms /sample. The number of samples between the two peaks of the input signal is 100 samples. The 100 sample period multiplied by 0.1ms/sample gives a period of 0.01s for the digitized signal. Taking the reciprocal of the period we get the expected 100Hz.
Next, enter the input frequency of 10.1kHz, set the amplitude to 2.9V, and set the offset to 0V. Press “update” and turn on the output. Press capture and you should see the output signal. Left click and drag on the time domain display to zoom in on the signal so that 200 samples are visible. Notice that the period of the 10.1kHz signal is the same as the 0.1kHz. This is because the 10.1kHz signal actually produces a 0.1kHz alias frequency.

## Slide 22: Time domain for 0.1kHz and 10.1kHz look the same
Vpp = 2.867 - 0.119 = 2.748V
Vpp = 2.852 - 0.123 = 2.729V
fin=0.1kHz
fmeas = 0.1kHz
fin=10.1kHz
fmeas = 0.1kHz
Notes: Here we compute the peak to peak amplitude of the digitized waveforms. Both waveforms are about the same amplitude and close to the applied signal. The difference between the applied signal and the digitized signal is due to system inaccuracies and loading of the signal generator. Now let’s take a look at the frequency domain.

## Slide 23: Frequency domain for 0.1Hz and 10.1kHz the same
fMeas = 0.1kHz
finput = 0.1kHz
finput = 10.1kHz
fMeas = 0.1kHz
Notes: Here we show the frequency domain response for the 0.1kHz and 10.1kHz input signals. As you might expect both signals have essentially the same frequency domain result. In both cases the measured fundamental is at 0.1kHz. Clearly the 10.1kHz signal aliases to 0.1kHz. Pause and capture the time domain and frequency domain signals for both 0.1kHz and 10.1kHz signals.

## Slide 24: Install the Sallen Key Filter
Notes: Now let’s do the same experiment with the Sallen Key filter. The only change needed for the hardware is to change the coupon board from OPA320_Goodfilter2 to the Sallen key filter. Pause and install the Sallen Key filter.

## Slide 25: Antialiasing filter with 0.1kHz and 10.1kHz Input
finput = 0.1kHz
Vin = 2.9V
Offset = 0V
finput = 10.1kHz
Vin = 2.9V
Offset = 0V
Notes: Here we apply a 0.1kHz and 10.1kHz 2.9V sine wave to the input of the Sallen Key filter. Recall that this filter has a cutoff of 500Hz so the 10.1kHz signal should be significantly attenuated. After capturing the signal you can see that the 0.1kHz signal is passed through the filter and the 10.1kHz signal is no longer visible. To zoom in on the 10.1kHz signal, change the “Y Scale fit” to “Auto Mode”.

## Slide 26: Zoom in on Alias
Vpp = 1.502 – 1.490 = 0.012V
Notes: Once you change the “Y Scale fit” to “Auto Mode” you can see that the alias signal is still present. The peak-to-peak values can be calculated by subtracting the maximum and minimum voltages. In this example the peak to peak is about 12mV which is very close to the predicted 11.6mV from simulation. Pause and apply the 0.1kHz and 10.1kHz 2.9V signals to the Sallen Key filter.

## Slide 27: Measured vs Expected Results
fsamp = 10kHz |  |  |  |  |  |  |  |  | 
Device |  |  |  | Expected |  | Example Measurements |  | Your Measurements | 
 | Device | fin (kHz) | Vin (V) | fmeas (kHz) | Vadc (Vpp) | fmeas (kHz) | Vadc (Vpp) | fmeas (kHz) | Vadc (Vpp)
1 | OPA320 Good filter2 | 0.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.748 |  | 
2 | OPA320 Good filter2 | 10.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.729 |  | 
3 | Sallen-Key | 0.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.711 |  | 
4 | Sallen-Key | 10.1 | 2.9 | 0.1 | 11.6m | 0.1 | 12m |  | 
5 | Sallen-Key (test design) | 5.1 | 0.02 | 4.9 | 0.0 |  |  |  | 
6 | Sallen-Key (test design) | 5.1 | 2.9 | 4.9 | 44.4m |  |  |  | 
Your results should show the same trend as the expected result but the specific values will differ.
Notes: This table summarizes the results of different anti aliasing experiments. We have completed the first four experiments. In the first experiment a 0.1kHz 2.9Vpp signal is applied. The captured data shown in example measurements approximately matches the input signal. Here the differences are due to loading of the PSI signal. The exact value of your measured results may differ somewhat but it should be close to the example shown. In the second experiment the 10.1kHz signal produces an alias signal at 0.1kHz. In the third and forth experiment the Sallen-Key filter is used to minimize the alias. Using simulation we predicted that the alias would be attenuated to about 11.6mV, and which compares well to the 12mV example measurement. Again, your results should be similar to this. In the last two experiments we will verify the design of the anti-aliasing filter.

## Slide 28: Check Antialiasing Filter Near Nyquist (Vin = 20mV)
Vpp = 1.495 – 1.493 = 2mV
finput = 5.1kHz
Vin = 0.02V
Offset = 0V
Notes: Recall that we designed the filter to attenuate a 20mV input signal at the Nyquist frequency to an amplitude of less than one half LSB. let’s test the antialiasing filter just beyond the Nyquist frequency at 5.1kHz. The attenuation at this frequency is -36.1dB, so the expected output for the 20mV input signal 313uV. The plots here show the time domain and frequency domain output. We expect the 20mV signal to be completely attenuated. Looking at the time domain signal we see about three codes of noise, or 2mVpp. You can’t really see anything that looks like a sinusoidal signal in this noise. Nevertheless, if you look at the spectral analysis you can see a small component at 4.9kHz, and this is where you would expect to see an alias of the 5.1kHz input signal. For all practical purposes, however, this signal is very small and difficult to distinguish from the noise floor. Thus, the filter is working as expected. Let’s confirm the attenuation by applying a full scale signal.

## Slide 29: Check Antialiasing Filter Near Nyquist (Vin = 2.9V)
Vpp = 1.517 – 1.472 = 0.045V
finput = 5.1kHz
Vin = 2.9V
Offset = 0V
Notes: Here we use the same configuration but change the input signal amplitude to 2.9V. The attenuation at 5.1kHz is 36.1dB so the expected output can be computed to be 45.4mV. Applying the signal and measuring the peak to peak output shows that the filter attenuates as expected at 5.1kHz.

## Slide 30: Measured vs Expected Results
fsamp = 10kHz |  |  |  |  |  |  |  |  | 
Device |  |  |  | Expected |  | Example Measurements |  | Your Measurements | 
 | Device | fin (kHz) | Vin (V) | fmeas (kHz) | Vadc (Vpp) | fmeas (kHz) | Vadc (Vpp) | fmeas (kHz) | Vadc (Vpp)
1 | OPA320 Good filter2 | 0.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.748 |  | 
2 | OPA320 Good filter2 | 10.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.729 |  | 
3 | Sallen-Key | 0.1 | 2.9 | 0.1 | 2.9 | 0.1 | 2.711 |  | 
4 | Sallen-Key | 10.1 | 2.9 | 0.1 | 11.6m | 0.1 | 12m |  | 
5 | Sallen-Key (test design) | 5.1 | 0.02 | 4.9 | 0.0 | -na- | 2m |  | 
6 | Sallen-Key (test design) | 5.1 | 2.9 | 4.9 | 44.4m | 4.9 | 45m |  | 
Your results should show the same trend as the expected result but the specific values will differ.
Notes: Now we can fill in the results for the final two experiments. Note that the measured results for the filter closely match the expected results. Pause now and make measurements for the final two tests.

## Slide 31
Thanks for your time!
Notes: That concludes the hands-on experiment. I hope this was useful to you. Thanks for your time.