## Slide 1: Amplifier Settling and Charge Bucket Filter Design TIPL 4405-L TI Precision Labs – ADCs
by Art Kay, Dale Li
Notes: Hello and welcome to the TI Precision labs hands-on experiment covering Amplifier Settling and Charge Bucket Filter Design. In this experiment we will use the Analog Engineer’s Calculator and simulation to predict ADC settling. We will look at several examples, some that are properly designed and others that are have poor settling. For each example, we will simulate the settling and measure the AC performance.

## Slide 2: Required/Recommended Equipment
Calculation
  Determine initial values for RC charge bucket circuit and bandwidth using Analog Engineer’s Calculator
Simulation
  Optimize RC charge bucket circuit using TINA SPICE
  Confirm final settling error is less than half of one LSB.
Measurement
  Verify THD and SNR for good and bad charge bucket filter design.
  PLABS-SAR-EVM-PDK
  http://www.ti.com/tool/plabs-sar-evm-pdk
  Download EVM software and purchase EVM
Notes: In the last precision labs lecture we described in detail the steps involved in selectign the SAR ADC amplifier and associated filter. For this lab we will quickly review and summarize this procedure. We will use the Analog Engineer’s Calculator to find the bandwidth and initial values for the RC circuit. Next we will optimized the circuit using TINA SPICE. Finally, we will measure the performance of the properly designed circuit as well as poorly designed circuits.

## Slide 3: Find amplifier and RC circuit
Amplifier:
5V, Rail-to-Rail I/O with Zero Crossover Distortion Required
Find bandwidth using Analog Engineer’s Calculator
Use parametric search to find device.
Verify model Open Loop Gain and Open Loop Output Impedance
RC Charge Bucket Circuit:
Use Analog Engineer’s Calculator for initial values
Use TINA Simulation to Optimize
Notes: First let’s quickly review the design problem that we covered in the lecture. The goal here is to choose an amplifier and find values for the filter. For the amplifier we want to get rail-to-rail input and output without crossover distortion. We can get the bandwidth of the amplifier from the analog engineers calculator and use parametric search to find a good amplifier choice. Finally, we need to test the amplifier model to verify that the output impedance and open loop gain curve are correctly modeled.
For the charge bucket filter we need to use the initial values from the analog engineer’s calculator as a starting point in TINA SPICE to optimize component values. We will use parameter stepping to find the RC value that gives the best settling.

## Slide 4: Find the Op Amp Bandwidth and RC Charge Bucket
1. Enter the information from the ADS8860 Data Sheet.
2. Results will be used in the simulation
Notes: Let’s review the operation of the Analog Engineer’s Calculator. First, find the “ADC SAR Drive” calculator under converters. Next select “Single Ended #2” and enter the resolution, internal sample and hold capacitor Csh, resolution, full scale range, and acquisition time. Note that all this information can normally be found in the ADC’s data sheet. Press ok and the range of Rfilt and Cfilt is displayed. In this case the resistance range is from 4.1ohms to 32.5 ohms and the nominal filter capacitance is 1.1nF. Also the amplifier’s gain bandwidth product is given to be 17.8MHz. Based on the gain bandwidth product and the fact that we need a rail to rail amplifier without crossover distortion we used parametric search to choose the OPA320 for this example.
Pause now and try this example on the Analog Engineer’s Calculator.

## Slide 5: Op Amp Model: Open Loop Gain
Notes: Now let’s confirm that the OPA320 op amp model is accurate. Specifically we will check the open loop gain and output impedance models. Both of these parameters are very important in ADC settling. This slide shows the standard test circuit for open loop gain testing. The Tera Farad and Tera Henry components are used so that the simulation has a closed loop DC operating point but is open loop for AC. Pause now and run the example TINA file “Aol opa320.tsc”. Compare the results to the data sheet specification.

## Slide 6: Op Amp Model: Open Loop Output Impedance
Notes: Another important curve is the open loop output impedance. This curve is ideally flat and low for fastest ADC settling. The circuit used for this test is similar to the open loop gain test, as the feedback loop is broken for AC but is shorted for DC operation. The main difference is that the current generator signal source is applied to the output of the amplifier. Pause now and run the example TINA file “Zo opa320.tsc”. Compare the results to the data sheet specification.

## Slide 7: Find the Op Amp Bandwidth and RC Charge Bucket
Notes: Now that we have verified that the amplifier model is accurate we can use simulation to adjust the RC charge bucket filter for optimal settling. Here we will use parameter stepping to sweep the resistor value from 4.1 ohms to 32.5 ohms. The capacitor value will be held constant at 1.1nF. Note that the two “resistors” are actually voltage controlled resistors. This scheme was used as parameter stepping can only control one object at a time. The voltage source value is equal to the resistance of Rfilt1 and Rfilt2. The objective of the parameter stepping will be to get an error signal that is less than one half LSB at the end of the acquisition cycle. In this example, one half of an LSB is 38.15uV. Let’s look at the simulation results.

## Slide 8: Parameter Step Rfilt
Notes: Here we see three different iterations of the parameter stepping for this example. In the first iteration we sweep the resistor according to the range from the Analog Engineer’s Calculator. That is, we sweep the resistance from 4.1 ohms to 32.5 ohms. We used the three best settling results from this simulation to set the range for the next simulation. Typically these results will contain an over dampened and under dampened response. In this case the boundary is adjusted in the second iteration from 19.9 to 26.3 ohms. Again, we use the best three settling results to set the new boundary. However, in the case of the third iteration, we use standard value resistors in the parameter step table. The result of the third iteration gives the optimal resistor value for best settling. Pause and run the parameter step simulations.

## Slide 9: Connect the hardware
Notes: For this experiment we will be using channel 2 on the precision labs hardware. First, set the jumpers as shown here. Connect the PSI to the PLABS board using the SMA cable, and connect the PHI to the PLABS channel 2 connector. Finally, connect the USB cables to the computer. Throughout this experiment we will test different amplifiers. Always be careful to install this amplifier right side up with the label at the bottom of the coupon card. For now you can leave the amplifier socket empty. Pause and connect the hardware.

## Slide 10: Record results as we progress through Experiment
Device |  |  |  |  | Simulated Settling Error ½LSB=38uV | Example Measurements |  | Your Measurements | 
 | Device | Samp.Rate | Voffset (V) | Vin (V) | Verror (V) | SNR (dB) | THD (dB) | SNR (dB) | THD (dB)
 | ADS8860 Data Sheet |  |  |  |  | 93 | -108 |  | 
1 | OPA320 Good filter1 | 1M | 2.5 | 4.9 | 28uV | 93.3 | -108.8 |  | 
2 | OPA320 Bad filter | 1M | 2.5 | 4.9 | -41mV | 82.5 | -73.4 |  | 
3 | OPA333 Low Bandwidth | 1M | 2.5 | 4.9 | -91mV | 54.1 | -55.9 |  | 
4 | OPA316 Crossover | 1M | 1.8 | 3.6 | 36.7mV | 86.1 | -85.0 |  | 
5 | OPA316 Crossover | 500k | 1.8 | 3.6 | 47uV | 90.3 | -102.4 |  | 
Notes: Throughout the experiment we will use different devices and apply different input signal amplitudes at different sampling rates. Also, we will simulate and measure the performance of the different circuits. Print out this table and use it to record your measured results as you step through the experiments.

## Slide 11: Start & Setup the Plabs-Power Scaling EVM Software
2. The green “HW Connected” and teal “PSI Controls” indicate good hardware communication.
1. Select “Plabs-SAR-EVM” from “start>All Programs”
Notes: Now let’s start the software by selecting the “Plabs-SAR-EVM” icon from the “Start > All Programs” menu. Once the software is running you should notice the green “HW connected” message at the bottom of the software. Also if the PSI controls are colored teal the hardware communications is working. Pause and get the EVM software started.

## Slide 12: 1: OPA320_Good Filter1
Error Target = 38µV
Simulate Error = 28µV
Note RC circuit is from optimization.
Notes: The circuit shown here is uses the values that we found in the parameter step optimization. Remember the goal was to get settling error less than the 38uV error target at the end of the acquisition period. The settling error for this design is about 28uV which meets the goal. Since the settling error meets the goal we expect the system performance to be equal to the ADC data sheet specification. For reference, let’s call this design OPA320 Good Filter 1. Pause now and run the ADC input settling simulation.

## Slide 13: 1: OPA320_Good Filter1
 | SNR (dB) | THD (dB)
ADS8860 Spec. | 93 | -108
Good Filter 1 | 93.3 | -108.8
Press “Capture”
Record AC performance
2. Amplitude = 4.9V
Offset = 2.5V
Frequency = 2kHz
Install OPA320_Good filter 1 coupon card in socket.
Notes: Now let’s measure the performance of good filter 1. First install the “OPA320 Good filter 1” coupon board in the channel 2 socket. Be careful to properly align the pins and make sure the device is right side up. Second, set up the PSI: the Amplitude is set to 4.9V, offset is set to 2.5V, and frequency is set to 2kHz. Press the power button to enable the output. Third, press “capture”. The FFT results will be displayed under “Spectral Analysis”. Forth record the AC performance and compare to the expected data sheet performance for the ADS8860. The ADS8860 specified SNR is 93dB and the THD is -108dB. The measured AC performance of this circuit actually exceeds the data sheet specifications. This proves that the amplifier and associated filter are properly designed. Pause now and test performance of good filter 1.

## Slide 14: 2: OPA320 Bad Filter
Error Target = 38µV
Simulate Error = -41mV
Optimal values:
R = 24.9Ω
C = 1.1nF
Bad Filter Values:
R = 100Ω
C = 1.1nF
Notes: In this experiment we will intentionally choose the wrong values for the RC charge bucket circuit to see how the performance is effected. Here we use 100 ohm resistors rather than the 24.9 ohm resistor value determined during our TINA SPICE optimization. You can see the simulation result shows that the settling error is -41mV which is more than one thousand times larger than the error target of 38uV. For reference, let’s call this design OPA320 Bad Filter. You can verify the simulated performance later using the included file.

## Slide 15: 2: OPA320 Bad Filter
 | SNR (dB) | THD (dB)
ADS8860 | 93 | -108
Bad Filter | 82.5 | -73.4
2. Amplitude = 4.9V
Offset = 2.5V
Frequency = 2kHz
Install OPA320_Bad Filter coupon card in socket.
Press “Capture”
Record AC performance
Notes: Now let’s measure the performance of the “OPA320 Bad Filter” circuit that we just simulated. First install “OPA320 Bad Filter” coupon board in the channel 2 socket. Be careful to properly align the pins and make sure the device is right side up. Second, set up the PSI: the Amplitude is set to 4.9V, offset is set to 2.5V, and frequency is set to 2kHz. Press the power button to enable the output. Third, press “capture”. The FFT results will be displayed under “Spectral Analysis”. Forth record the AC performance and compare to the expected data sheet performance for the ADS8860. The ADS8860 specified SNR is 93dB and the THD is -108dB. The measured AC performance of this circuit is very poor compared to the data sheet specifications. For this example measurement we measured 82.5dB for SNR and -73.4dB for THD. Also, you can see significant noise and harmonics in the spectral analysis FFT results display. This emphasizes the importance of using the parameter stepping optimization we covered earlier to select the optimal RC charge bucket circuit . Pause now and test performance of the “OPA320 Bad Filter” circuit.

## Slide 16: 3: OPA333 Low Bandwidth
Bandwidth Required:
Gain Bandwidth= 17.8MHz
OPA333 Bandwidth:
Gain Bandwidth= 350kHz
Error Target = 38µV
Simulate Error = -88mV
Notes: In this experiment we will intentionally choose an amplifier with insufficient bandwidth to drive the SAR ADC. Here we use an OPA333 op amp with a bandwidth of 350kHz. Remember, the bandwidth requirement from the calculator was 17.8MHz. You can see the simulation result shows a settling error of -88mV which is more than one thousand times larger than the error target of 38uV. For reference, let’s call this design OPA333 Low Bandwidth. You can verify the simulated performance later using the included file.

## Slide 17: 3: OPA333 Low Bandwidth
 | SNR (dB) | THD (dB)
ADS8860 | 93 | -108
Low Bandwidth | 54.1 | -55.9
2. Amplitude = 4.9V
Offset = 2.5V
Frequency = 2kHz
Install OPA333_Low Bandwidth coupon card in socket.
Press “Capture”
Record AC performance
Notes: Now let’s measure the performance of the “OPA333 Low Bandwidth” circuit that we just simulated. First install the “OPA333 Low Bandwidth” coupon board in the channel 2 socket. Second, set up the PSI: the Amplitude is set to 4.9V, offset is set to 2.5V, and frequency is set to 2kHz. Press the power button to enable the output. These settings are the same as in the last experiment. Third, press “capture”. The FFT results will be displayed under “Spectral Analysis”. Forth record the AC performance and compare to the expected data sheet performance for the ADS8860. The ADS8860 specified SNR is 93dB and the THD is -108dB. The measured AC performance of this circuit is very poor compared to the data sheet specifications. For this example measurement we measured 54.1dB for SNR and –55.9dB for THD. Also, you can see significant noise and harmonics in the spectral analysis FFT results display. This experiment emphasizes the importance of using an amplifier with sufficient bandwidth. Pause now and test performance of the “OPA333 Low Bandwidth” circuit.

## Slide 18: 4: OPA316 Crossover, fs = 1Msps
Bandwidth Required:
Gain Bandwidth= 17.8MHz
OPA316 Bandwidth:
Gain Bandwidth= 10MHz
Error Target = 38µV
Simulate Error = 35mV
Notes: In this experiment we will look at another amplifier that has insufficient bandwidth to drive the SAR ADC. Here we use an OPA316 op amp with a bandwidth of 10MHz. Remember, the bandwidth requirement from the calculator was 17.8MHz, so the 10MHz bandwidth of the amplifier is close but not sufficient for this sampling rate. You can see the simulation result shows that the settling error of 35mV which is substantially larger than the error target of 38uV. Note that this amplifier has input crossover distortion, and a hands-on experiment covering the effects of crossover distortion is covered in a different video. For reference, let’s call this design “OPA316 Crossover”. You can verify the simulated performance later using the included file.

## Slide 19: 4: OPA316 Crossover, fs = 1Msps
 | SNR (dB) | THD (dB)
ADS8860 | 93 | -108
Crossover 1Msps | 86.1 | -85.0
Note that the sampling rate is 1Msps
2. Amplitude = 3.6V
Offset = 1.8V
Frequency = 2kHz
Install OPA316_Crossover coupon card in socket.
Press “Capture”
Record AC performance
Notes: Now let’s measure the performance of the “OPA316 Crossover” circuit that we just simulated. First install the “OPA316 Crossover” coupon board in the channel 2 socket. Second, set up the PSI: the Amplitude is set to 3.6V, offset is set to 1.8V, and frequency is set to 2kHz. Press the power button to enable the output. These settings are different from the last experiment. In this case we reduced the amplitude of the input signal to avoid the crossover distortion region. We will discuss this more later. Third, notice that he default sampling rate is set to 1Msps. Forth, press “capture”. The FFT results will be displayed under “Spectral Analysis”. Finally, record the AC performance and compare to the expected data sheet performance for the ADS8860. The measured AC performance of this circuit is very poor compared to the data sheet specifications. For this example measurement we measured 86.1dB for SNR and –85.0dB for THD. Also, you can see significant noise and harmonics in the spectral analysis FFT results display. This experiment emphasizes the importance of an amplifier with sufficient bandwidth. In the next experiment we will reduce the sampling rate and see how performance is effected. For now let’s pause and test performance of the “OPA316 Crossover” circuit.

## Slide 20: Input signal range to avoid crossover distortion
Crossover happens at 3.8V for OPA316
Hands-on Experiment - Crossover Distortion
Notes: If you switch to the time domain display you can see that the maximum voltage of the input signal is 3.5V. The input signal amplitude was selected to avoid the crossover distortion region which is at 3.8V. Thus, any AC performance limitation we are seeing is not from crossover distortion. If you aren’t familiar with crossover distortion, please watch the crossover distortion experiment given in the link below.

## Slide 21: Changing the Sampling Rate to 500kHz
Notes: Reducing the sampling rate will cause the acquisition time of the SAR ADC to increase. This will make it easier for the data converter to achieve good settling which allows lower bandwidth amplifiers to achieve good settling. For the next experiment we will reduce the ADC sampling rate to 500kHz. This slide shows how to calculate the new acquisition time based on the reduced sampling rate. First, note that the period of the entire conversion cycle is one divided by the sampling rate. In this example, one divided by 500kHz is equal to 2us. Next, note that the maximum conversion time is a fixed value. For this example it is 710ns. Finally, note that the acquisition time can be calculated by subtracting the maximum conversion rate from the entire period. In this example 2us minus 710ns is equal to an acquisition period of 1.29us. Remember that the acquisition time for the 1MHz sampling rate was 290ns, so decreasing the sampling rate to 500kHz significantly increases the acquisition time.

## Slide 22: Changing the Sampling Rate to 500kHz
Bandwidth Required:
Gain Bandwidth= 4MHz
OPA316 Bandwidth:
Gain Bandwidth= 10MHz
Acquisition time (tacq) from last slide.
Notes: Now let’s use the acquisition time that we just calculated in the Analog Engineer’s Calculator. The resolution, sample and hold capacitor and full scale range are the same as before. After pressing the ok button, you can see that the Gain Bandwidth requirement is now 4MHz. Since the OPA316 has a gain bandwidth of 10MHz we should be able to get good results with this device. Let’s simulate the performance.

## Slide 23: 5: OPA316 Crossover, fs = 500ksps
Bandwidth Required:
Gain Bandwidth= 4MHz
OPA316 Bandwidth:
Gain Bandwidth= 10MHz
Error Target = 38µV
Simulate Error = 47µV
Notes: Here we have the same circuit we looked at in the last experiment. The only difference is that we adjusted the sampling rate to 500ksps. With this new sampling rate the amplifier bandwidth should be sufficient for good settling. Sure enough, after the simulation you can see the settling error is about 47uV which is comparable to the error target of 38uV. You can verify the simulated performance later using the included simulation file.

## Slide 24: OPA316 Crossover, fs = 500ksps
 | SNR (dB) | THD (dB)
ADS8860 | 93 | -108
Crossover 1Msps | 86.1 | -85.0
Crossover 500ksps | 90.3 | -102
Set sampling rate to 500ksps
2. Amplitude = 3.6V
Offset = 1.8V
Frequency = 2kHz
No device change needed.
Press “Capture”
Record AC performance
Notes: Now let’s measure the performance of the “OPA316 Crossover” circuit that we just simulated. First no change is required on the hardware. We are still using the “OPA316 Crossover” coupon board in the channel 2 socket. Second, set up the PSI: the Amplitude is set to 3.6V, offset is set to 1.8V, and frequency is set to 2kHz. These settings are the same as the last experiment. Press the power button to enable the output. Third, sett the sampling rate to 500ksps. This lower sampling rate should allow for better performance. Forth, press “capture”. The FFT results will be displayed under “Spectral Analysis”. Finally, record the AC performance and compare to the expected data sheet performance for the ADS8860. The measured AC performance of this circuit is close to the data sheet specifications. For this example measurement we measured 90.3dB for SNR and –102dB for THD. You can see significant improvement in AC performance compared to the same circuit with a 1Msps sample rate. Thus, it is possible to use lower bandwidth amplifiers and get good performance if you reduce the sampling rate. Pause now and test performance of the “OPA316 Crossover” circuit with a 500ksps sampling rate.

## Slide 25: Settling can be improved
Notes: You may have noticed that although the error settled to the target in the last experiment, the settling had a lot of overshoot and ringing. Ideally, for best performance and a robust design the settling waveform should have minimal overshoot and ringing. The top graph shows the settling of the previous circuit which wasn’t optimized. Using a SPICE parameter stepping optimization you can find better values for the RC charge bucket circuit. The bottom graph shows the final optimized transient response. Notice that the settling waveform has no overshoot and settles to a very small error of 40nV. Again, for the best performance and a robust design over temperature an process variation use the optimized RC charge bucket values.

## Slide 26: Measured vs Expected Results
Device |  |  |  |  | Simulated Settling Error ½LSB=38uV | Example Measurements |  | Your Measurements | 
 | Device | Samp.Rate | Voffset (V) | Vin (V) | Verror (V) | SNR (dB) | THD (dB) | SNR (dB) | THD (dB)
 | ADS8860 Data Sheet |  |  |  |  | 93 | -108 |  | 
1 | OPA320 Good filter1 | 1M | 2.5 | 4.9 | 28uV | 93.3 | -108.8 |  | 
2 | OPA320 Bad filter | 1M | 2.5 | 4.9 | -41mV | 82.5 | -73.4 |  | 
3 | OPA333 Low Bandwidth | 1M | 2.5 | 4.9 | -91mV | 54.1 | -55.9 |  | 
4 | OPA316 Crossover | 1M | 1.8 | 3.6 | 36.7mV | 86.1 | -85.0 |  | 
5 | OPA316 Crossover | 500k | 1.8 | 3.6 | 47uV | 90.3 | -102.4 |  | 
Your results should show the same trend as the expected result but the specific values will differ.
Notes: This table summarized the results for all the experiments and simulations. For simulations the settling error should be less than half of one LSB, or 38uV. If you look at the results, the only simulations that are close to the error target are for experiment 1 and 5. All the other experiments have errors in the millivolts which is substantially larger than the target. Notice that the measured AC performance in the example measurement is very good in cases where the settling error is small. Remember that the ADS8860 data sheet performance is 93dB for SNR and -108dB for THD. If you look at experiments 1 and 5 the circuit approaches this performance. Comparing the performance for the other experiments shows significant performance degradation. Thus, the settling results in the simulations correlate well to the measured AC performance. The conclusion of this experiment is that it is important to select amplifiers with the sufficient bandwidth and also choose the optimal RC charge bucket component values for best settling and AC performance.

## Slide 27
Thanks for your time!
Notes: That concludes the hands-on experiment. I hope this was useful to you. Thanks for your time.