## Slide 1: Designing in emerging applications: Ultrasonic sensing and capacitive touch
Presenters:
Leo Estevez – MSP430 Applications
Dennis Lehman – MSP430 Applications

## Slide 2: Ultrasonic Liquid Level Sensing
Presenter: Leo Estevez – MSP430 Applications

## Slide 3: Agenda
TI’s Solution
Test fixtures
Transducers
Adverse operating conditions
Additional applications and demo

## Slide 4: Technology/Cost comparisons
In liquid sensors are prone to corrosion/mechanical failure and can’t work with arbitrary containers. (drink dispensers, coffee machines, etc.)
The additional cost of a transducer can be 50 cents(in high volumes).
  The transducer can often be fit directly into the chassis of the tank or machine and doesn’t require modification to the container itself.
Ultrasonic level sensing enables resolutions(~20 microns) which could enable feedback for flow control while dispensing fluid from a container(or to a container).
Average current consumption is <20uA per measurement per second.

## Slide 5: TI’s ultrasonic sensing solution (MSP43FR604x)
Notes: TI's ultrasonic sensing subsystem (see Figure 1-1) comprises a programmable pulse generator (PPG) and a high-speed sigma delta analog to digital converter with a programmable gain amplifier (PGA) that can autonomously excite and capture ultrasonic waveforms for subsequent processing by the integrated LEA.
This ultrasonic subsystem first excites the “upstream” transducer connected to CH0_OUT while capturing the waveform from a “downstream” transducer connected to CH0_IN. The ultrasonic subsystem subsequently excites the “downstream” transducer connected to CH1_OUT while capturing the waveform from the “upstream” transducer connected to CH1_IN. These waveforms are then processed by the LEA to determine the difference between the upstream and downstream time of flight.

## Slide 6: ADC based correlation vs. TDC zero crossing
TDC
Zero-Crossing
(Amplitude
Dependent)
ADC Based
Correlation
(Amplitude
Independent)
6
Peak value = 15729.26
Peak index = 332
Crossing threshold
value = 3460.44
Above value = 3479.74
Above index = 290
Below value = 3410.58
Below index = 289
Perform full correlation of input with binary transmit pattern
Compute Hilbert transform
Find envelope peak value and index
Calculate threshold using the peak value
Interpolate to find threshold crossing.
Stop timer when threshold exceeded.
Find subsequent zero crossings.
Notes: The ADC based correlation approach implemented with TI’s solution correlates frequency information in the received signal with the transmitted binary pattern and subsequently determines the intersection between a threshold and the envelope of that correlated signal. This approach is insensitive to amplitude variations which are commonly seen under adverse operating conditions.

## Slide 7: Ultrasonic configuration
MSP430FR6043
http://www.ti.com/lit/an/slaa951a/slaa951a.pdf
Notes: For single transducer applications such as level sensing through air, we are using the EVM-FR6043 with an external opamp and driver. We have connected the upstream and downstream transducer connections on the EVM in order to transmit and receive via the same transducer.

## Slide 8: OpenSCAD test fixtures
http://www.openscad.org/
175kHz
200kHz
500kHz
Notes: Three different test fixtures are used in these experiments where the TRANSDUCER_RADIUS is adjusted to fit the transducer and the CYLINDER_LENGTH is adjusted to extend a collimating cylinder for one of the transducers. The OpenSCAD parametric script used to generate these test fixtures can be found in the liquid level sensing app note.

## Slide 9: Tradeoffs in transducers
Frequency | 3.3V Excitation Range | 8 Pulse Standard Deviation | Minimum Distance
175kHz | > 100 cm | 100-500 ns | 3.5 cm
200kHz | 20 cm | 50-400 ns | 1.5 cm
500kHz | 15 cm | 10-300 ns | 1 cm
The standard deviation in measurements
Increases with distance.
Increasing excitation voltage and/or a
collimating waveguide can extend range.
The attenuation of the ultrasonic wave
Increases with frequency and can vary based on the gas mixture.
Notes: For high resolution and close range applications, 500kHz transducers are preferred. For longer range applications, larger lower frequency transducers are preferred. For mid range applications, 200kHz transducer can provide a low cost compromise between long range transducers and higher accuracy transducers. 200kHz and 500kHz transducers are typically less expensive because they are mass produced for the residential gas metering industry.

## Slide 10: 500kHz @12cm
0.2us * 343m/s = 68.6um
(34.3um one way)

## Slide 11: 200kHz @10cm
0.4us * 343m/s = 137.2um
(68.6um one way)

## Slide 12: 175kHz @10cm
0.13us * 343m/s = 44.6 um
(22.3um one way)

## Slide 13: 200kHz foam experiments
No Foam
Some Foam
More Foam
Notes: The strength of the reflected signal decreases as there is an increase in the amount of foam in the cup. Although this can make high resolution level sensing measurements difficult, the amplitude of the signal might also be used to determine how much foam is in the cup.

## Slide 14: 200kHz condensation effects
Notes: Hot steam condensation can also have a negative effect on the accuracy of measurements. As can be seen from this experiment with steaming hot water, the combination of condensation and higher temperatures can significantly weaken the signal.

## Slide 15: 175kHz condensation effects
4us * 343m/s = 1.37mm
(0.68 mm one way)
Notes: 175kHz transducers also gave reduced signal strength with higher standard deviations although the amount of attenuation seen was much lower.

## Slide 16: Additional applications/demo
www.ti.com/tool/evm430-fr6043
(Technical Documents)

## Slide 17: Automated tools make capacitive sensor design quick and easy
Presenter: Dennis Lehman – MSP430 Applications

## Slide 18: Agenda
CapTIvateTM Technology
Automating Sensor Designs
CapTIvate Design Center
OpenSCAD Demo

## Slide 19
Notes: MSP430 Family of 16bit FRAM MCUs with CapTIvate Capacitive Touch Technology

## Slide 20: Agenda
CapTIvateTM Technology
Automating Sensor Designs
CapTIvate Design Center
OpenSCAD Demo

## Slide 21: CapTIvate Technology Guide highlights
https://ti.com/captivatetechguide
  MSP430 CapTIvate MCU selection
  CapTIvate Technology
  Sensor design guidelines
  CapTIvate Design Center GUI
  Development Tools
  Getting Started Workshop
  Video
    Tune capacitive sensors in 5mins or less
Notes: The CapTIvate Technology Guide provides everything you need to start creating a capacitive touch sensor application. The chapters shown in this slide are the most relevant when first starting out. The MSP430 MCU selection chapter compare the family variants and describe many of the MSP430 features. The Technology chapter provides a basic understanding of CapTIvate and how capacitive touch works. Probably the most important is the Design Guide chapter which provides recommended best practices for such things as PCB sensor layout. The CapTIvate Design Center GUI describes how to create and tune your sensors. The Development Tools chapter provides an overview of the available CapTIvate Evaluation modules and panels with links to the respective product page where you can purchase these tools. The Workshop chapter steps a new user through the process of creating a sensor project with the CapTIvate Design Center and how to effectively tune PCB sensors. There is an on-line video showing this complete process in under 5 mins.

## Slide 22: CapTIvate tools
Notes: A quick look at some of the available tools

## Slide 23: Agenda
CapTIvateTM Technology
Automating Sensor Designs
CapTIvate Design Center
OpenSCAD Demo

## Slide 24: Automating PCB sensor design
CapTIvate Tech Guide – Design Guide Chapter
SLAA891- OpenSCAD auto-generates electrode patterns in seconds
Scripts for sliders, curved sliders, wheels and touchpads provided by TI
Notes: SLAA891 describes how to use OpenSCAD to automate the design of complex type of capacitive sensors such as sliders, wheels and trackpads.

## Slide 25: Automating PCB sensor design
OpenSCAD
  https://www.openscad.org
Open Source (free)
2D/3D CAD
Programming script controls sensor design
Notes: OpenSCAD is a free, open source 2D/3D CAD programming tool that creates 2D and 3D objects using scripting code the defines an object’s shape and size. TI has created several scripts to automate slider, wheel and TrackPad sensors. This means all a user has to do is pick which sensor they want to create, modify a couple of parameters such as size or number of electrodes and instantly generate a 2D pattern that can be easily exported in a standard .dxf file format. This .dxf file can be imported into a variety of PCB CAD tools and used to create the copper patterns for the PCBA.

## Slide 26: Automating PCB sensor design
Scripts can be customized by user
Requires only a few parameters to define a sensor design
Notes: The scripts are easy to customize if a user wants more control of the sensor design output.

## Slide 27: OpenSCAD design process
Live Demo at end of presentation
Notes: The OpenSCAD sensor design workflow is quite simple.
Modify the script parameters to meet your design requirements
Render the 2D object
Export to .dxf
Import .dxf into PCB CAD tool
Convert primitives to copper

## Slide 28: Agenda
CapTIvateTM Technology
Automating Sensor Designs
CapTIvate Design Center
OpenSCAD Demo

## Slide 29: CapTIvate Design Center GUI
Select MCU
Notes: The CapTIvate Design Center is the recommended starting point for every design. Here you choose the MCU and define your sensors

## Slide 30: CapTIvate Design Center GUI
Select and configure keypad sensor
Notes: Defining a sensor is simple. You choose the type and select the number of elements (electrodes) and choose self or mutual capacitance.

## Slide 31: CapTIvate Design Center GUI
Repeat for all sensors
Notes: Here is an example of the CAPTIVATE-BSWP EVM panel sensors. All of the CapTIvate EVM panels were first created using this design center.

## Slide 32: CapTIvate Design Center GUI
Notes: Now that all the sensors have been defined the next step is to assign a sensor to the MCU’s CAPT-IO pins. Using the Auto-Assign button will allow the GUI to determine the optimal pin connections between the selected MCU and the sensors the user has created. It is possible to do this step manually, but only if the user is experienced with CapTIvate.

## Slide 33: CapTIvate Design Center GUI
Configuration MCU connections to sensors
Generate MSP430 starter project firmware
Generates 100% of the code to get started. (no need to write code)
Notes: After the sensor connections have been defined the next step is to generate a starter project based on the selected MCU and sensors. This starter project generates 100% of all the necessary code to get started.

## Slide 34: CapTIvate Design Center GUI
Build and program MSP430
Notes: The last step is to import the generated firmware project into either Code Composer Studio or IAR IDE, build and program the target MSP430.

## Slide 35: CapTIvate Design Center GUI
Enable communications
View sensor data
Notes: Communication between the MSP430 and design center GUI flows through the CapTIvate programmer and can use either a UART or I2C interface. Select either BULK_I2C or UART interface then select connected.

## Slide 36: CapTIvate Design Center GUI
View sensor output
Notes: Double mouse click on any sensor icon will bring up its sensor view window. This is the window where the sensor’s measurements are displayed in real-time. If you touch the sensor you will see the BARs change in value

## Slide 37: CapTIvate Design Center GUI
Tune sensor’s sensitivity and thresholds
Detachable
Notes: The tuning process involves selected an appropriate sensitivity and threshold. More details about tuning a sensor is available in the CapTIvate technology guide, either on-line or in the design center’s menu > topics.

## Slide 38: CapTIvate Design Center GUI
Generate final code
Notes: Once the sensors have been tuned the last step is to generate a final version of the project. This time select Update existing project. This generates only the updated user configuration files and not an entire project.

## Slide 39: Agenda
CapTIvateTM Technology
Automating Sensor Designs
CapTIvate Design Center
OpenSCAD Demo

## Slide 40: Design Touchpad using OpenSCAD
Touchpad is a 2D sensor
Remote Controls, headphones, earbuds
Use OpenSCAD to generate diamond patterns
OpenSCAD Demos
Notes: This demo will show the steps to generate a TrackPad sensor.

## Slide 41
SLYP712