## Slide 1: Maximize density, power, and reliability with TI GaN and C2000™ real-time MCUs
GaN: Yichi Zhang
C2000: John Kim

## Slide 2: Overview
Introduction of GaN and C2000 real-time MCUs which enable efficient power conversion and fast control
Example of TI GaN and C2000 real-time MCUs in wide variety of applications
  Totem pole PFC
  900V bidirectional energy storage system with 99% efficiency
  1.25kW 3-phase inverter with 99% efficiency

## Slide 3: GaN + C2000: Efficient power and control
Both LMG341x GaN & C2000 enable high MHz operation, for high power density
  GaN FETs have inherently lower switching and conduction losses, to switch at high frequencies and increase power density
  C2000 MCUs offer precision sensing, powerful processing and premium actuation capabilities engineered specifically for high frequency power control applications
TI GaN with integrated gate drive and protection. Enables fastest GaN switching in the market, for high efficiency and reliability .
C2000 is a platform of scalable, ultra-low latency, real-time controllers designed power electronics that demand high power density, high switching frequencies, perfectly paired with GaN and SiC technologies
Notes: Olivier – could you sanitize what I have for the C2000 messaging?
OA – edited last bullet

## Slide 4: TI GaN + C2000: Delivering efficient power solution
TI-GAN
Integrated driver delivers 2X switching speed and half the losses of discrete GaN
Built-in protection designed for operation under extreme conditions
Simple interface signal for closed loop connection with C2000 real-time MCUs
C2000 real-time MCUs
12-/16-bit ADCs with up to 3.5MSPS for high speed and accurate voltage and current sensing
Powerful 32-bit Floating point DSP enabling multi-phase and multi-level control topologies
Highly flexible, High resolution 150ps PWM enables high frequency converter design
1MHz CrM PFC
with 99% Efficiency
Power Density: 250 W/in3 (15.2 W/cm3)
Versus
Silicon: 55 W/in3 (3.4 W/cm3)
Notes: Same messaging taken from previous slide, but put into a visual format

## Slide 5: Applications for GaN & C2000 real-time MCUs
DC/DC
Converters
Renewable Energy
Motor Control
C2000™
32-bit MCUs
Automotive & EV/HEV
Energy Delivery
Digital Power
Industrial Drives
Motor Control
Solar Power
Telecom / Server
AC/DC Rectifiers
E-bike
Charging Infrastructure
Appliance
Pumps
On-Board Charging (OBC)
Servo Drive
Robotics
Automation
AC Drives
Wind Power
Uninterruptable
Power Supplies
DC-DC
Notes: Few applications removed that didn’t apply to GaN
5

## Slide 6
C2000 real-time MCUs
Highly accurate sensing
12-/16-bit ADCs, up to 24 channels
ADC post processing, and externally accessible DACs
Sense
Control
Highly flexible, High-resolution PWMs:
Up to 32 outputs
Position Manager, Sigma-Delta Filter Module, trip zones
Leading innovation:
Config. Logic Block for peripheral customization, Fast Serial Interface for high-speed communication, ERAD for enhanced diagnostics and profiling
Expertise and support:
Software libraries, reference designs, and functional safety-compliant devices.
Process
High performance processing
Floating-point DSP C28x™ core + parallel multi-core architecture + instructions set optimized for control math, up to 925 MIPS
CAN, CAN-FD, LIN, UART, SPI, I2C, PMBus, USB, 10/100 Ethernet MAC, EtherCAT®, XEMIF
Interface
C2000™ real-time MCUs overview
Scalable, ultra-low latency, real-time controller platform designed for efficiency in power electronics, such as high power density, high switching frequencies, GaN and SiC technologies
Up to 1.5 MB Flash,
256 kB RAM (ECC protected)
QFN, QFP, BGA packages
-40 to 125C
temperature range
1.2-V core, 3.3-V I/O design
Q100 automotive qualified options
Over 750 million units shipped for industrial and automotive applications with compatible software
25 years expertise in
real-time control systems
Notes: we build real-time controller with optimized power efficiency and density in mind, based on unique and innovative features and years of power control system level expertize to help you design faster

## Slide 7: GaN: Key advantages over silicon FET
Low CG,QG gate capacitance/charge (1 nC-Ω vs Si 4 nC-Ω)
faster turn-on and turn-off, higher switching speed
reduced gate drive losses
Low COSS,QOSS output capacitance/charge (5 nC-Ω vs Si 25 nC-Ω)
faster switching, high switching frequencies
reduced switching losses
Zero QRR No ‘body diode’
No reverse recovery losses
Reduces ringing on switch node and EMI
Low RDSON (5 mΩ-cm2 vs Si >10 mΩ-cm2)
lower conduction losses
Drain
Gate
Source
CG
QG
COSS
QOSS
QRR

## Slide 8: TI GaN: Efficient and reliable GaN
Highest switching speed in the industry enabling 50% lower losses in 65W to >10kW applications
Twice the Speed, Half the Losses
Lifetime Reliability
Robust self-protected solutions with >30M device reliability hours
and >3GWHr of power conversion to date
Low Cost and Integrated
TI Owned process and manufacturing of GaN FET with integrated driver and protection in a low inductance package

## Slide 9
Example of TI C2000 + GaN: CCM PFC

## Slide 10: CCM PFC: topologies
Dual-boost PFC
Totem-pole PFC
  Good EMI performance
  Distributed heat
  Moderate efficiency
  Low power density
  Requires 6 power switches and 2 inductors
  High power density
  High efficiency
  Distributed heat
  Requires 4 power switches and 1 inductor
SJ Mosfet has large reverse recovery loss
  can’t survive in a half bridge configuration
GaN FET with 0 Qrr is ideal for totem pole PFC

## Slide 11: Why choose TI GaN in totem-pole PFC?
GaN has >50% lower switching energy compared to SiC
GaN has zero reverse recovery losses
TI GaN switches at up to 100 V/ns – resulting in 5.5x reduction in losses compared to SiC and 2.7x compared to discrete GaN
TI GaN has the best cost parity to Si MOSFETs
146

## Slide 12: 1-kW CCM PFC: power loss comparison

## Slide 13: Higher switching frequency
42.5mm
23.24mm
Inductor volume 43952mm3
100-kHz CCM PFC inductor
(1000 W)
63mm
35mm
Inductor volume 138915mm3
40-kHz CCM PFC inductor
(1000 W)
3.2x reduction in inductor volume

## Slide 14: Path to 99% efficiency with GaN: control
Adaptive Dead Time (A.D.T)
  Dead time calculated based on operating condition to minimize the third quadrant loss and improve efficiency
  C2000 real-time MCUs with Hi-res PWM deadband and compute power can enable adaptive dead time implementation.
Td =
Optimal Td
Turn-on too soon
Turn-on too late

## Slide 15: Path to 99% efficiency with GaN: control
Phase shedding
  Shed phase in lighter load application to reduce switching loss and improve efficiency
  Phases need to be added/dropped quickly for safe operation and optimal efficiency
  Decision based on current reference in voltage loop
  C2000TM Real-Time Controllers enable to implement flexible phase shedding

## Slide 16
Tools & Resources
Target Applications
Energy storage system
Onboard charger
Industrial power supply
Features
GaN-based 3 phase interleaved totem pole bidirectional PFC
Rated Power : 3.3 kW (at 230 Vrms)
Peak efficiency : 98.7 % (at 230 Vrms)
Total Harmonic Distortion (THD) < 2% (at low line)
PWM switching frequency : 100 kHz
PFC mode specification: 120/230 Vac_in, 380 Vdc_out
Inverter mode specification : 380 Vdc_in, 120/230 Vac_out
Soft starting for totem-pole bridge
Phase shedding and adaptive dead time control for higher efficiency
F28004x CPU + CLA (co-processor) support
Benefits
High power density design while maintaining OEM specified form factor
Further system integration through latest TI-GaN gate drivers
Enables superior control and implementation of advanced control schemes brought by high performance C2000 MCU
Enables simple adaptation of software through powerSUITE™ support
Bi-Directional 3Ph Interleaved Totem-Pole CCM PFC/Inverter Reference Design TIDM-02008
TIDM-02008 Tools Folder
Test Data/Design Guide
Design Files: Schematics, BOM, Design Files
Key TI Devices: TMS320F280049, TMS320F28075, LMG3410R070, UCC27714, OPA2376, SN74LVC1G3157, ISO7831, TLV713
Notes: OA – added slide

## Slide 17: TIDM-02008: Measured efficiency and THD
Notes: OA – adjusted title

## Slide 18: TIDM-02008 test results
Steady State 230-Vac IN, 380V DC OUT, 3.3kW, iTHD 2.69%

## Slide 19: TIDM-02008 CPU/CLA utilization
The maximum ISR loading numbers were captured
  ISR1 : Inner current loop, grid synchronization (PLL), etc
  ISR2 : Outer voltage loop, relay on/off, OVP,UVP,OCP, etc
*Advanced options : A.D.T, Phase Shedding, NL voltage loop, SFRA
 | ISR1 (100 kHz) | ISR2 (10 kHz)
CPU utilization (*Advanced options: All Off) | 53% | 6 %
CPU utilization (Advanced options: All On) | 65% | 9%
 | ISR1 (100 kHz) | ISR2 (10 kHz)
CLA utilization (Advanced options: All Off) | 57 % | 9 %
CLA utilization (Advanced options: All On) | 79% | 12 %

## Slide 20
Example of TI C2000 + GaN: 900V bidirectional energy storage system with 99% efficiency

## Slide 21: 900V-5kW bidirectional ACDC converter with TI-GaN
DC voltage up to 1400V, AC voltage up to 480V L-L
Peak efficiency of 99.2%
Convection cooled with no fan
Scalable multi-level solution for >5kW
Total harmonic distortion (THD) < 3%
Surface-mount devices to reduce manufacturing cost
LMG3410R050, 600V, 50mΩ GaN FET with integrated Driver & Protection
Leverages TI C2000 controller: TMS320F28379D
Design Features
Design Benefits
Typical Operating conditions | IGBT | SiC | TI-GaN
Frequency (kHz) | 20 | 100 | 140
Open frame Power Density (W/in3) | 73 | 170 | 211
Efficiency (%) | 98.3 | 98.9 | 99.2
3X power density improvement over IGBT and 1.25X over SiC
470 mm x 162 mm x 51 mm
Notes: OA – added device name for C2000 (this is for Fortress)
OA – target availability needs to be updated (1Q20) – removed for now

## Slide 22: Topology comparison at 99% efficiency
Chart: Inverter relative volume breakdown
| SiC HB | SiC T type | ANPC PWM3 | FC4L (TI-GaN)
EMI | 3.189 | 1.732 | 1.732 | 1.275
Inductor | 62.9 | 19.648 | 19.648 | 5.14
AC capacitor | 3.11 | 3.168 | 3.168 | 3.003
DC capacitor | 4.545 | 6.92 | 6.92 | 4.185
Heatsink | 5.213 | 5.976 | 9.122 | 12.338
Chart: Inverter relative cost breakdown
| SiC HB | SiC T type | ANPC PWM3 | FC4L (TI-GaN)
Device | 18.9 | 36.9 | 72 | 72
Isolated supplies | 5.17 | 6.6 | 6.6 | 10.2
Analog isolators | 2.29 | 4.59 | 4.59 | 16.05
Digital isolators | 5.76 | 11.52 | 12.6 | 12.6
DC film capacitor | 4.24 | 3.23 | 2.62 | 5.78
Electrolytic | 0 | 3.07 | 3.07 | 0
Inductor | 225.4 | 86.16 | 69.24 | 16.87
CMC | 5.2 | 4.94 | 5 | 4.87
Y cap | 1.73 | 1.73 | 1.73 | 1.73
X cap2 | 4 | 4.12 | 4.05 | 3.92
Heatsink | 1.77 | 3.21 | 4.9 | 4.97

## Slide 23: Results
99 % efficiency 3 kW to 5 kW natural convection cooling
CH1: Fly capacitor 532 V
CH2: Fly capacitor 266 V
CH3: Grid voltage 270 V
CH4: Grid current 6 A
3.8ns
480 V
464 V
472 V

## Slide 24
Example of TI C2000 + GaN: 1.25kW 3-phase inverter with 99% efficiency

## Slide 25: TIDA-00915: 1.2kW 3Φ integrated drive
Ultra-small form factor with power density of 150W/in3
  50ºC ambient conditions up to 1.25kW
  85ºC ambient conditions up to 550W
Peak efficiency > 99%
Natural convection cooling with 10mm heatsink
Built-in short-circuit and over temperature protection
450V Max DC Operation
Solution Features
Applications
Integrated motor drives
Robotics
Servo drivers

## Slide 26: Traditional external drive systems with silicon
AC Motor 6
Encoder cable
(Length 10m and more)
Angle Sensor 6
(Encoder, Resolver)
Power Interface Cable
Length of 10m+ for each motor!
Position Interface 6
Robot Controller Cabinet Multi-Axis Inverter
3-Phase Inverter 1
3-Phase Inverter 2
3-Phase Inverter 6
Position Interface 1
Position Interface 2
AC Motor 1
Angle Sensor 1
Digital or analog communication (encoded angle) require high immunity against fast transient bursts, high-voltage surge and ESD.
Manipulator
High dv/dt

## Slide 27: Integrated motor drive with GaN + C2000 MCUs
AC Motor 6
Angle Sensor 6 (Encoder, Resolver)
3-Phase Inverter 1
AC Motor 1
Angle Sensor 1
Manipulator
Position Interface 6
Position Interface 1
Position Interface 2
Position 1
Position 2
Position 6
3-Phase Inverter 6
3-Phase Inverter 2
Cost savings:
Reduce power and communication cabling
Free up floor and cabinet space
High Performance :
Higher dv/dt, less switching power loss
Improve EMC immunity on communication cables

## Slide 28: TIDA-00915: Natural convection cooling
Heatsink: 10mm fin height
Peak efficiency > 99.2%

## Slide 29
Backup

## Slide 30: C2000 MCU ideal for high switching frequency control
C2000 MCU DNA | Scalable MCU architecture from high to low end power stages with high frequency control & processing capabilities | Ideal For WBG (GaN/SiC) Switching/control/system
32-bit -28xCPU Up to 200MHz | Industry’s leading real time control CPU Single/double floating point precision Tightly integrated accelerators & control peripherals | Efficient low latency, precision control algorithms Widely adopted in Motor drive/Solar inverters/Automotive power stages
CLA/TMU/NLPID Up to 200MHz | Industry’s low latency event/algorithm processing engine Executes in floating point precision and in parallel to the CPU Fast trigonometric and non-linear algorithm processing engine | Enabling multi-phase & multi-level control topologies Ideal for low latency non-linear control
PWM/Capture engine | Industry’s proven best in class and flexible PWM generation Up to 200/MHz PWM clock with protection Up to 150ps pulse width resolution with high resolution dead band Tightly integrated with the Analog sub-system | Multi-phase & multi-level control topologies Protects shoot-through/short circuit Efficient switching of GaN/SiC power stage Glueless interface to TI Gate Driver family
Analog sub-system | Up to x4 high-precision, just-in time 12/16bit ADCs Flexible Analog comparator & DAC subsystems Pre-processing blocks to minimize latency in sensing | Enables fast current/voltage sensing scheme Enables customizable Peak-current mode control Minimizes data analog preconditioning/latency
Delta Sigma- SDFM | Up to 8 programmable Delta sigma filters, with digital comparators | Enables isolated current/voltage sensing
CLB Configurable Logic | Configurable logic to add customizable protection Custom peripheral events using Analog and digital triggers | Enables power stage protection Develop advanced switching topologies
Fast Serial interface | Supports low cost fast serial interface up to 200Mbps | Enables isolated current sensing with low latency. Allows distributed power stage architectures
Communication ports | Connectivity ports 50MHz SPI, CAN/CANFD/Ethernet/Ethercat | Enables External host links for monitoring/control
Red- Unique to C2000 MCU only
Green – Showcased in TIDesigns/examples

## Slide 31
SLYP720