## Slide 1: MMWAVE-SDK deep dive Easy evaluation and development of mmWave systems with software development kit
Nitin Sakhuja - Industrial mmWave Radar Applications

## Slide 2: MMWAVE-SDK deep dive
TI's MMWAVE-SDK (MilliMeter Wave Software Development Kit) is a unified software platform for the TI mmWave Sensing Portfolio, providing easy setup and fast out-of-the-box access to evaluation and development.
This training provides an overview of the MMWAVE-SDK 3.x architecture and the various building blocks such as Data Processing Units (DPUs) and Data Processing Chains(DPCs). It also provides a deeper look into the components with software execution flows accompanied with source code references from the MMWAVE-SDK Out of Box Demo point cloud processing chain.
We also present some example applications where the Out of box point cloud detection chain is extended to develop more complex mmWave applications such as Long Range People Detection and Tracking Demo, Traffic Monitoring Demo and Area Scanner Demo.
What you’ll learn:
TI MMWAVE-SDK architecture and it’s various building blocks such as DPCs and DPUs
Understand DPM, DPC and DPU execution flows e.g. initialization and runtime operation using source code references
Developing custom components to extend the out of box processing chain and available examples.

## Slide 3: Agenda
MMWAVE-SDK
  Architecture overview
  Data path design
Data path deep dive
  Initialization
  Configuration
  Execution (Runtime view)
DPUs and DPCs in MMWAVE-SDK 3.x
  DPUs: Range, Static-Clutter removal, Doppler, CFAR-CA and AoA
  DPCs: HWA and DSP based object detection chains
Software development and debugging
  Development resources
  MMWAVE-SDK debugging
Extending SDK architecture for advanced applications
  Considerations for developing custom DPUs and DPCs
  Custom DPUs and DPCs in Industrial Toolbox
  Demo: Long Range People Tracking and, Traffic Monitoring
  Demo: Area Scanner and, Automated Doors and Gates
Notes: Slide 5: This slide is for the 5 slide abstract ONLY

## Slide 4: MMWAVE-SDK - Architecture Overview

## Slide 5: mmWave signal processing
RF Front-End
ADC
ADC Data
xWR64xx
xWR68xx
Pre- Processing
(Interference Mitigation)
1st Dim FFT
(Range)
2nd Dim FFT
(Velocity)
Detection
(CFAR)
3rd Dim FFT
(Angle Arrival)
Point Cloud
[Range, Velocity, Angle]
Clustering
Tracking
Object Classification
Objects
xWR64xx: Radar Accelerator used for this processing
xWR68xx/18xx: Radar Accelerator / C674x DSP used for this processing
Out-of-Box Demo
Notes: Before getting into the SDK architecture, it is important to have a quick look at the FMCW Radar signal processing chain and how it maps to the processing blocks available on TI mmWave devices.
The RF front-end receives the RX radar signal which is mixed with the TX signal to generate the beat frequency signal and delivered to the ADC. The ADC converts the analog signal to digital samples which are pre-processed.
Successive FFTs are computed on the digitized samples for range, velocity and angle of arrival calculation. The FFTs operations and detection processing can be performed either using the Radar Hardware accelerator or the C674x DSP available on these devices.

## Slide 6: mmWave SDK contents
Building blocks
  RTOS, Drivers, and RadarSS firmware
  Scalable data processing blocks and chains to work on HWA or DSP
  Layered / API based Radar analog front end (AFE) programming
  Pre-built software blocks and chains for basic FMCW Radar signal processing
  Catalog of mmWave signal processing algorithms optimized for C674x DSPs including tracker
  Package for high-security (HS) devices to enable programming encryption keys and encrypt/authenticate program binaries
Demonstrations and examples
  TI RTOS based
  Out of box demo with easy configurability via TI Cloud-based or offline GUI
  Representation of point cloud and benchmarking data from demo via GUI
Documentation
  Associated tools: Code Composer Studio, TI-RTOS, Uniflash
  Available at http://www.ti.com/tool/MMWAVE-SDK

## Slide 7: mmWave SDK architecture
Datapath Processing Chain
TI mmWave Application Demo
Analog front-end
Processor (DSP and R4) and peripherals
BSS Firmware
Boot ROM
mmWave Link
mmWave Library
RTOS Drivers + OSAL
IPC
mmWave API
TI-RTOS
OS, Drivers, Algorithms
mmWave APIs
Point Cloud
DataPath Interface
Range
Doppler
CFAR
AoA
DataPath EDMA
Datapath Manager
Main highlights:
Foundational components for SOC enablement – RTOS, Drivers, mmWaveLink, mmWaveLib
RF Front-end completely abstracted using mmWaveLink
mmWave API simplifies device integration of mmWaveLink
Data path layer is an abstraction over existing driver APIs in the data flow
Separation of data processing units and chain from the application
Simpler application that does the instantiation of the Datapath layer
Notes: Main highlights:
Basic SOC enablement using bottommost layer – RTOS, Drivers, mmWaveLink, mmWaveLib
mmWave API simplifies device integration of mmWaveLink
Data path layer is an abstraction over existing driver APIs in the data flow
Separation of data processing units and chain from the application
Simpler application that does the instantiation of the modules

## Slide 8: MMWAVE-SDK – Datapath Design

## Slide 9: Datapath Layer Design
DPM: Datapath manager
  Foundation layer that enables the "scalability" aspect of the architecture.
DPIF: Standard Interface points in the Detection chain are defined
  Input ADC data, Radar Cube, Detection Matrix, Point cloud
DPUs: Data Translating function(s) from one interface point to the other are called “Data Processing Units”
  Range Processing (ADC data to Radar Cube)
  Doppler Processing (Radar Cube to Detection Matrix)
  CFAR and AoA (Detection Matrix to Point Cloud)
DPC: Data Processing Chain
  Chain of “data processing units” is called a data processing Chain. Ex: Detection DPC (ADC to Point Cloud).
  This conforms to the DPM dictated API definition
Datapath Processing Chain (DPC)
Range DPU
Doppler DPU
CFAR DPU
AoA DPU
DataPath Interface (DPIF)
DataPath EDMA (DPEDMA)
DataPath Manager (DPM)
mmWave Application
StaticClutter Removal DPU

## Slide 10: Scalable SW Chain
TI mmWave Sensor Portfolio
Scalable Software Processing Chain
DPIF
DPUs
DPC
Notes: Each of the mmWave device offers different processing nodes to realize the mmwave processing. xWR14xx has HWA engine, xWR16xx has DSP C674x core, xWR68xx and xWR18xx has HWA+DSP(C674x). For devices with multiple processing nodes, the mmWave detection processing chain can exploit them as needed for performance and scalable reasons. Shown here is an example of detection processing chain that uses various data processing units (DPUs) to perform the typical mmwave processing upto the point cloud. The mmwave data representation in mmWave device memory forms an interface layer between the various DPUs. Each DPU can be realized independently using HWA or DSP processing node - the choice is either driven by usecase or availability of that processing node on a given mmWave device.

## Slide 11: Typical call flow (1/2)
DPM
MSS Application
DPUs
Drivers
DPC
DPM Init
DPC Init
DPU#1 Init
DPU#2 Init
DPU#n Init
HWA/EDMA Init
DPM Ioctl (Config#1)
DPC Ioctl (Config#1)
DPU#1 Config
DPU#2 Config
DPU#n Config
DPM Ioctl (Config#2)
DPC Ioctl (Config#2)
DPU#1 Config
DPU#2 Config
DPU#n Config
EDMA/HWA Config
EDMA/HWA Config
DPM Report Callback
(NOTIFY_DPC_IOCTL)
DPM Report Callback
(NOTIFY_DPC_IOCTL)
Config#1 and Config#2 are shown as examples here on how a config can be split into multiple shorrter structures as needed by a DPC. It is not mandatory to split into two. On the contrary, config can be split into even more smaller structures.

## Slide 12: Typical call flow (2/2)
DPM
MSS Application
DPUs
Drivers
DPC
DPM Start
DPC Start
DPU#1 Process
DPU#2 Process
DPU#n Process
H/W Frame Event
H/W Chirp Events
<point cloud results>
DPM Report
(NOTIFY_DPC_STARTED)
DPM Stop
DPC Stop
DPM Report
(NOTIFY_DPC_STOPPED)

## Slide 13: Data path deep dive

## Slide 14: DPM: Datapath Manager
Modular SW Architecture which provides an abstraction between the “Datapath Processing Chain” and the customer application.
  Main task context which encapsulates the execution of DPC and DPUs
  Application code instantiates DPM at start-up and registers a DPC.
Provides a well-defined API
  Exposed to the application to interface with the DPM
  Exposed to the “Data processing chain” developers to be able to write their own code.
Messaging mechanism
  Send/Receive Configuration
  Extends to Multiple-Thread/Core
  Synchronized execution (No critical section required)
  Response Mechanism with error code passing
Reporting mechanism which allows applications to be notified about the status of the DPM/Datapath Processing Chain.
Core Layer
Datapath Chain Management
Message
Application Developers
Data Processing Chain
Developers
Datapath Manager
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer can call the DPM APIs from both MSS and DSS and control the configuration and execution of the corresponding "data processing chain“ running on that core. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 15: DPM Initialization
Application code creates and initializes a DPM instance using the DPM_init function
Application also creates a DPM task
Source: MMWAVE-SDK HTML documentation
C:\ti\mmwave_sdk_03_xx_xx_xx\docs\mmwave_sdk_module_documentation.html

## Slide 16: DPM Initialization
Application code creates and initializes a DPM instance using the DPM_init function
Application also creates a DPM task
1
2
3
Pointer to DPC

## Slide 17: DPC: Data Processing Chain
DPC_xxx_APIs
DPC_xxx_execute
DPC_xxx_ioctl
DPC_xxx_start
DPC_xxx_stop
DPC_xxx_deinit
DPC_xxx_Callbacks
DPC_xxx_cbChirpAvailable
DPC_xxx_cbFrameStart
DPC_xxx_init
DPC_xxx_injectData
All external DPC APIs starts with DPC_. DPC unique name follows next (follows coding guidelines).
  DPC_ObjectDetection_Init
External Mandatory APIs follows the prototype defined by the “Datapath Manager”
DPCs have flexibility in defining their own content within the individual structure
DPC that is split between MSS and DSS will expose two set of APIs - one for MSS and one for DSS. Depending on the functionality split between the two domains, not all APIs need to be implemented on the two domains
For more details, refer to docs folder in each of the DPCs

## Slide 18: DPC Initialization
Application registers the DPC with DPM during DPM creation.
Application calls DPM init which calls the DPC’s registered init function
Application calls DPM_ioctl with different message types
DPM_ioctl invokes the DPC’s registered ioctl function with:
  Pre-start common config message (common to all sub-frames) and
  Sub-frame specific Pre-start config messages.
DPC handles the messages in the ioctl function and performs the corresponding configuration.
Source: MMWAVE-SDK HTML documentation
C:\ti\mmwave_sdk_03_xx_xx_xx\docs\mmwave_sdk_module_documentation.html

## Slide 19: DPC Initialization
Application registers the DPC with DPM during DPM creation.
Application calls DPM init which calls the DPC’s registered init function
Application calls DPM_ioctl with different message types
DPM_ioctl internally invokes the DPC’s registered ioctl function and passes the message to it
DPC handles the message in the ioctl function and performs the corresponding configuration
Refer to the call flow below
1
2
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 20: DPC Configuration
Application registers the DPC with DPM during DPM creation.
Application calls DPM init which calls the DPC’s registered init function
Application calls DPM_ioctl with different message types (i.e. commands)
DPM_ioctl internally invokes the DPC’s registered ioctl function and passes the message to it
DPC handles the message in the ioctl function and performs the corresponding configuration
Refer to the call flow below
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 21: DPC Configuration (continued)
Application registers the DPC with DPM during DPM creation.
Application calls DPM init which calls the DPC’s registered init function
Application calls DPM_ioctl with different message types
DPM_ioctl internally invokes the DPC’s registered ioctl function and passes the message to it
DPC handles the message in the ioctl function and performs the corresponding configuration
Refer to the call flow below
5
6
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 22: DPU: Data Processing Units
DPU_xxx_init
DPU_xxx_InitParams_t
errCode
DPU_xxx_config
DPU_xxx_Config_t
H/W Resources (EDMA, HWA, I/O buffer pointers, Scratch buffer pointers)
Frame/Sub-frame DPU Static Config (Ex: Num ADC Samples, Chirps/Frame, ADCBuf Config, Data Interface Desc)
Frame/Sub-frame DPU Dynamic Config (Ex: DC Range Calibration)
DPU_xxx_process
Handle
DPU_Handle
DPU_xxx_OutParams_t
errCode
errCode
DPU_Handle
DPU_xxx_control
DPU_Handle
cmd
args
argSize
errCode
DPU_xxx_deinit
DPU_handle
errCode
DPU_xxx_Stats_t
DPU optional specific Params (Ex: isLastChirp)
All external DPU APIs start with the prefix DPU_. DPU unique name follows next..Ex: DPU_RangeProcHWA_init
Standard external APIs:
  Init: one time initialization of DPU
  Config: complete configuration of the DPU: hardware resources, static and dynamic (if supported by DPU)
    static config: config that is static during ongoing frames
    dynamic config: config that can be changed from frame to frame but only when process is not ongoing - ideally interframe time after DPC has exported the results for the frame
  Process: the actual processing function of the DPU
  Control: ioctl interface that allows higher layer to switch dynamic configuration during interframe time
  De-init: de-initialization of DPU
All memory allocations for I/O buffers and scratch buffers are outside the DPU since mmWave applications rely on memory overlay technique for optimization and that is best handled at application level
All H/W resources must be allocated by application and passed to the DPU. This helps in keeping DPU platform agnostic as well as allows application to share the resources across DPU when DPU processing doesn't overlap in time.
DPUs are OS agnostic and use OSAL APIs for needed OS services.
For more details, refer to docs folder in each of the DPUs

## Slide 23: DPU Initialization
Recall from DPC Configuration…
Application calls DPM init which calls the DPC’s registered init function
DPC_init calls the various DPU init functions in sequence, to create separate DPU instances for the number of sub-frames configured.
Refer to the call flow below
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 24: DPU Configuration
Recall from DPC Configuration…
Application calls DPM_ioctl with different message types
DPM_ioctl internally invokes the DPC’s registered ioctl function and passes the message to it
DPC performs DPU configuration when handling the PRE_START_CFG command
  The PRE_START_CFG handler calls wrapper functions for each DPU, e.g. DPC_ObjDet_rangeConfig
  The wrapper allocates the resources required for the DPU and calls the corresponding DPU config function e.g. DPU_RangeProcHWA_config.
Refer to the call flow below
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 25: DPIF: Datapath Interface
Radar Cube
Detection Matrix
Point cloud
Property
Complex/Real
numADCSamples
Buffer Pointer
Property
Layout – RADAR CUBE RANGE DOPPLER RX TX (1)
Input ADC data
Buffer Pointer
Property
Layout – DET MATRIX RANGE DOPPLER (1)
Property
Buffer Pointer
Format – XYZV, RAEV
Float
RX interleaved/non-interleaved
Point Cloud SideInfo
Property
noiseVal
snr

## Slide 26: Datapath Execution – Runtime View
At sensor start: Application calls DPM_start which calls the DPC’s pre-registered start function DPC_ObjectDetection_start.
  The mmw demo does this in the sensorStart CLI command handler function.
At every frame interrupt: The DPC’s pre-registered frame start call back function, DPC_ObjectDetection_frameStart is invoked.
  Recall from DPC_init: The DPC’s frameStart callback is registered with the DPM during DPC initialization
This invokes the DPC’s registered execute function, e.g. DPC_ObjectDetection_execute
  Under the hood: The Frame Start handler calls DPM_notifyExecute which posts the semaphore for DPM_execute
  DPM_execute then calls the DPC’s pre-registered execute function.
DPC_ObjectDetection_execute performs the frame processing and populates the output in DPC_ObjectDetection_ExecuteResult structure and returns.
Application reads the output structure and sends it over UART. This completes the frame processing.
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 27: Datapath Execution – Runtime View
At sensor start: Application calls DPM_start which calls the DPC’s pre-registered start function DPC_ObjectDetection_start.
  The mmw demo does this in the sensorStart CLI command handler function.
At every frame interrupt: The DPC’s pre-registered frame start call back function, DPC_ObjectDetection_frameStart is invoked.
  Recall from DPC_init: The DPC’s frameStart callback is registered with the DPM during DPC initialization
This invokes the DPC’s registered execute function, e.g. DPC_ObjectDetection_execute
  Under the hood: The Frame Start handler calls DPM_notifyExecute which posts the semaphore for DPM_execute
  DPM_execute then calls the DPC’s pre-registered execute function.
DPC_ObjectDetection_execute performs the frame processing and populates the output in DPC_ObjectDetection_ExecuteResult structure and returns.
Application reads the output structure and sends it over UART. This completes the frame processing.
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 28: Datapath Execution – Runtime View
At sensor start: Application calls DPM_start which calls the DPC’s pre-registered start function DPC_ObjectDetection_start.
  The mmw demo does this in the sensorStart CLI command handler function.
At every frame interrupt: The DPC’s pre-registered frame start call back function, DPC_ObjectDetection_frameStart is invoked.
  Recall from DPC_init: The DPC’s frameStart callback is registered with the DPM during DPC initialization
This invokes the DPC’s registered execute function, e.g. DPC_ObjectDetection_execute
  Under the hood: The Frame Start handler calls DPM_notifyExecute which posts the semaphore for DPM_execute
  DPM_execute then calls the DPC’s pre-registered execute function.
DPC_ObjectDetection_execute performs the frame processing and populates the output in DPC_ObjectDetection_ExecuteResult structure and returns.
Application reads the output structure and sends it over UART. This completes the frame processing.
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 29: Datapath Execution – Runtime View
At sensor start: Application calls DPM_start which calls the DPC’s pre-registered start function DPC_ObjectDetection_start.
  The mmw demo does this in the sensorStart CLI command handler function.
At every frame interrupt: The DPC’s pre-registered frame start call back function, DPC_ObjectDetection_frameStart is invoked.
  Recall from DPC_init: The DPC’s frameStart callback is registered with the DPM during DPC initialization
This invokes the DPC’s registered execute function, e.g. DPC_ObjectDetection_execute
  Under the hood: The Frame Start handler calls DPM_notifyExecute which posts the semaphore for DPM_execute
  DPM_execute then calls the DPC’s pre-registered execute function.
DPC_ObjectDetection_execute performs the frame processing and populates the output in DPC_ObjectDetection_ExecuteResult structure and returns.
Application reads the output structure and sends it over UART. This completes the frame processing.
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 30: Datapath Execution – Runtime View
At sensor start: Application calls DPM_start which calls the DPC’s pre-registered start function DPC_ObjectDetection_start.
  The mmw demo does this in the sensorStart CLI command handler function.
At every frame interrupt: The DPC’s pre-registered frame start call back function, DPC_ObjectDetection_frameStart is invoked.
  Recall from DPC_init: The DPC’s frameStart callback is registered with the DPM during DPC initialization
This invokes the DPC’s registered execute function, e.g. DPC_ObjectDetection_execute
  Under the hood: The Frame Start handler calls DPM_notifyExecute which posts the semaphore for DPM_execute
  DPM_execute then calls the DPC’s pre-registered execute function.
DPC_ObjectDetection_execute performs the frame processing and populates the output in DPC_ObjectDetection_ExecuteResult structure and returns.
Application reads the output structure and sends it over UART. This completes the frame processing.
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 31: DPUs and DPCs in SDK 3.x

## Slide 32: RangeProc DPU
Purpose: (1D FFT+ DC Range Calib) processing during active frame.
  Takes ADCBuf as input
    interleaved or nonInterleaved format
    Single chirp or multichirp (DSP mode only)
    Either direct access (HWA mode only) or via EDMA
  Produces RadarCube in L3 in user requested format (fixed set of formats described in data interface).
  Performs FFT using HWA or DSP based on configuration.
  Performs DC range calibration either inline (DSP mode) or at the end of all chirps (HWA mode).
Supported architecture
  R4F, C674x
  Different files for HWA based and S/W based implementation

## Slide 33: Static Clutter DPU
Purpose: (Clutter Removal) processing during inter frame.
  Takes non-transposed formatted 1DOUT Radarcube as input
  Updates the RadarCube in L3 (keeping the same format)
  S/W based only
Supported architecture
  R4F, C674x

## Slide 34: Doppler DPU
Purpose: (2D FFT + Energy Sum) processing during inter frame.
  Takes non-transposed formatted 1DOUT Radarcube as input
  Produces Detection Matrix in L3 in fixed format
  Performs FFT and Energy Sum using H/W(HWA)
    S/W(DSP) based implementation would be added in the SDK in future.
Supported architecture
  R4F, C674x

## Slide 35: CFAR-CA DPU
Purpose: (CFAR-CA +peak grouping) processing during inter frame.
  User can choose between various CFAR-CA implementation: CFAR-CA, CFAR-CASO, CFAR-CAGO
  Fixed Point implementation
  2 pass implementation: first pass (optional) in Doppler direction and then second pass in Range direction
  Performs CFAR and PeakGrouping using H/W(HWA)
    S/W(DSP) based implementation would be added in SDK in future
  Takes Detection Matrix as input
  Produces bitmask of peaks and SNR information for AoA.
Supported architecture
  R4F, C674x

## Slide 36: AoA DPU
Purpose: (Range/Phase/Doppler compensation + Near field correction + Max Velocity enhancement + AoA + FoV filter) processing during inter frame.
  Takes non-transposed formatted 1DOUT Radarcube, detection matrix and peak bitmask as input
  Produces Point Cloud
  Performs any FFT ops using H/W(HWA)
    S/W(DSP) based implementation will be added in SDK in future
  All other processing operations are done using S/W.
    For R4F based implementation, near field and max velocity algos will not be offered
  All the processing ops other than AoA FFT is optional and driven by user input
Supported architecture
  R4F, C674x

## Slide 37: xWR64xx OOB Demo Chain (DPC)
R4F
Detection Processing Chain (DPC) for xWR64xx Out of Box demo.
Demonstrates Radar Signal Processing using Cortex R4F + HWA
Also runs on xWR68xx (C674x DSP not used)
×
×
×
×
×
Denotes Unused Datapath
Notes: Each of the mmWave device offers different processing nodes to realize the mmwave processing. xWR14xx has HWA engine, xWR16xx has DSP C674x core, xWR68xx and xWR18xx has HWA+DSP(C674x). For devices with multiple processing nodes, the mmWave detection processing chain can exploit them as needed for performance and scalable reasons. Shown here is an example of detection processing chain that uses various data processing units (DPUs) to perform the typical mmwave processing upto the point cloud. The mmwave data representation in mmWave device memory forms an interface layer between the various DPUs. Each DPU can be realized independently using HWA or DSP processing node - the choice is either driven by usecase or availability of that processing node on a given mmWave device.

## Slide 38: xWR68xx OOB Demo Chain (DPC)
Detection Processing Chain (DPC) for xWR68xx Out of Box demo.
Demonstrates Radar Signal Processing using Cortex R4F + HWA + C674x DSP
DSP provides higher performance and frees up R4F for other processing (e.g. Object Tracking)
R4F
DSP
×
×
×
×
×
Denotes Unused Datapath
Notes: Each of the mmWave device offers different processing nodes to realize the mmwave processing. xWR14xx has HWA engine, xWR16xx has DSP C674x core, xWR68xx and xWR18xx has HWA+DSP(C674x). For devices with multiple processing nodes, the mmWave detection processing chain can exploit them as needed for performance and scalable reasons. Shown here is an example of detection processing chain that uses various data processing units (DPUs) to perform the typical mmwave processing upto the point cloud. The mmwave data representation in mmWave device memory forms an interface layer between the various DPUs. Each DPU can be realized independently using HWA or DSP processing node - the choice is either driven by usecase or availability of that processing node on a given mmWave device.

## Slide 39: 68xx OOB Demo - Application View
mmWave Device
mmWave application (MSS)
Object Detection DPC
RadarSS Firmware
mmWave Front End
mmWave API
DPM
Input/output over UART to external
TLV format
External Processor/Controlling entity
CLI
mmWave Sensor Data
(point cloud)
Notes: Simplified application
  Owns interaction with external entity via peripherals
  Employs mmWave API layer in isolation mode to control the front end
  Instantiates DPM in local domin mode to control the DPC
  Owns the DPC and h/w resources needed by it
  Converts DPC output into TLV format before shipping it out to external entity

## Slide 40: Software Development and Debugging

## Slide 41: Software Development Resources
Software Development Resources: The following resources are key to learning about software development for TI processors.
  BIOS users guide: Installed as part of MMWAVE-SDK, it is available in the TI install directory e.g. C:\ti\bios_6_73_01_01\docs\Bios_User_Guide.pdf.
    This is the one of the best resources for learning about SYSBIOS and software development for TI processors.
  Linker command files: Understanding these is fundamental to developing applications for TI RTOS (SYSBIOS). Refer to the following resources:
    TI Linker Command File Primer
    Advanced Linker Techniques for Convenient and Efficient Memory Usage
Other helpful resources
  Getting Started with Code Composer Studio v7
  Debugging Common Application Issues with TI-RTOS
  TI-RTOS Workshop
  Introduction to C6000 Architecture
  C6000 Cache - Overview (7 of 15)
  Using C6000 EDMA3 - Part 1 (13 of 15)
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 42: MMWAVE-SDK Debugging
Pre-requisites: The user should be familiar with general CCS debugging techniques e.g. running code in CCS, putting breakpoints, observing the values of variables and memories etc. Following resources can be used to ramp-up on these topics if needed.
  Getting Started with Code Composer Studio v7
  Debugging Common Application Issues with TI-RTOS
In addition to the above, the user must be familiar with basic procedures for running an MMWAVE application in CCS debug mode. This is explained in the mmWave Industrial Toolbox at the following page:
  Using CCS Debug for Development
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 43: MMWAVE-SDK Debugging
Rebuilding SDK code for debug:
  All MMWAVE-SDK code (drivers, OOB demo application and DPU libs) is built with –O3 optimization, which does not allow single step debugging in the corresponding components.
  In order to enable step debugging in CCS, the –O3 optimization options needs to be removed (or changed to a lower level)
    Remove the –O3 flag in the SDK common makefile from R4F_CFLAGS and/or C674_CFLAGS directives to change build options for ARM and/or DSP code.
    Re-build the demo and the desired pre-compiled libs (e.g. drivers, DPUs) separately with the non-optimized configuration to enable debugging.
A note about DPUs: All DPUs are linked with the application as pre-compiled libs, so just re-building the application/demo code does not re-build the DPU libs automatically. Any DPUs that need to be debugged, should be re-built first with the new build options and then the applications code re-compiled to link with the new DPU lib(s). This applies to the SDK drivers as well.
Removing optimization may increase the memory requirements and/or break real-time behavior.
SDK Compile flags for Cortex R4F core
SDK Compile flags for C674x DSP core
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 44: MMWAVE-SDK Debugging
Disabling Real time asserts:
  If the DPC cannot complete the frame (or sub-frame) processing within the real-time deadline, it raises as assert causing the application to exit
  When step debugging a distributed DPC which runs on both R4F and DSP cores (e.g. in the 68xx point cloud detection chain), this assert should be disabled on both cores in DPC code as shown otherwise application would crash as shown in this CCS console log.
  NOTE: Make sure to re-enable the frame timing assert when running the DPC in non debug mode.
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 45: Understanding Error Codes: Datapath Errors
When demo runs into error conditions, an error code is generated and printed out on CCS console
The error code is a negative integer e.g. shown in the picture.
Can be from various sources such as Drivers, Control modules, DPC, DPU or demo (i.e. application)
Error code defined as: (Module error code base minus Module specific error code)
  The module error code base values are defined in packages\ti\common\mmwave_error.h.
  The base error codes for DPC and DPU are define in packages\ti\datapath\dpif\dp_error.h
  Individual DPU specific error codes defined in the DPU header files
Example: Parsing the error -30430 shown here
  The error code is from module with error base "-30000", which indicates it is DPU error
  Referring to dp_error.h, base "-30400" is from AOA Proc.
  Then find the error code in aoaprocdsp.h for error(-30) which is DPU_AOAPROCDSP_ESCRATCHSIZE
NOTE: In SDK demos, these error codes are not sent out on UART so the demo must be run in CCS debug mode to get the error code
Refer to SDK module documentation at the following location (in the SDK install directory) for more details:
  file:///C:/ti/mmwave_sdk_03_05_00_04/packages/ti/demo/xwr68xx/mmw/docs/doxygen/html/index.html#mmwave_error
Datapath Errors
-30000 = DPU Error base
-30430 = -30000 -400 -30
-400 = AOA Proc Error base
-30 = Insufficient Memory Error
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 46: Understanding Error Codes: mmWave Errors
Besides Datapath errors, there is another class of errors known as mmWave module errors.
These represent errors returned by the RF Front-End e.g. incorrect profile configuration.
Defined as a combination of mmWave error, Susbsystem error and error level as shown.
  mmwave errors defined in packages\ti\control\mmwave\mmwave.h
  Subsystem errors defined in packages\ti\control\mmwavelink for mmwavelink.h
  Error level represents WARNING or ERROR.
Example: The error shown in the log here indicates
  The error is from module(-3100 i.e. mmwave) with error -8 (MMWAVE_EPROFILECFG)
  The Subsystem (mmwavelink) error is 36 which is defined as RL_RET_CODE_PF_START_FREQ_INVAL_IN in mmwavelink.h, which indicates invalid start frequency specified in ProfileCfg API.
mmWave Link errors
Notes: DPM is the foundation layer that enables the "scalability" aspect of the architecture. This layer absorbs all the messaging complexities (cross core and intra core) and provide standard APIs for integration at the application level and also for integrating any "data processing chain". Application layer will be able to call the DPM APIs from any domain (MSS or DSS) and control the configuration and execution of the "data processing chain". The APIs offered by DPM will be available on both MSS and DSS. The various deployments that it can cater to (but not limited to) are:
Datapath control on R4F and datapath execution is split between R4F/HWA and DSP (Distributed)
Datapath control on R4F and datapath execution is on R4F using HWA (Local)
Datapath control on R4F and datapath execution is on DSP (with and without HWA) (Remote)
Datapath control on DSP and datapath execution is on DSP+HWA (Local)
Datapath control on DSP and datapath execution is on DSP (Local)

## Slide 47: Extending SDK architecture for advanced applications

## Slide 48: Developing a Custom Radar Processing Chain
Key considerations for developing a custom mmWave processing chain with SDK 3.x architecture
Understand the data processing chain for the target application and model it in terms of DPC and DPUs
Re-use the SDK Out of Box Detection Processing OR develop a new Detection Chain
  SDK Out of box DPC is a Range-Doppler based processing chain.
  Lower angular resolution as compared to Range-Azimuth (Capon Beamforming) chain
    SDK Detection Chain re-used for Long Range People Detection and Area Scanner Demos
    But a Higher resolution Capon Beamforming Detection Chain was developed for Indoor People Counting Demos
  Range Processing is still re-used irrespective of the rest of the Detection Processing
Additional processing requirements beyond the OOB point cloud detection
  Can the additional processing be added to an existing DPU or do we need to create a new DPU
    Object Tracking - new DPU
    Static Object Detection - new DPU
    2D AoA (Angle of Arrival) using DSP – Enhancement to existing AoA DPU
Enhancements needed at the DPC and Application level e.g.
  Tracking
  Beam-steering
  Static object detection
Memory and MIPS requirements for the additional processing

## Slide 49: Examples of Custom DPUs and DPCs
New DPUs and DPCs developed in mmWave Industrial Toolbox
TrackerProc DPU and ObjectDetectionAndTracking DPC
  2D/3D Object tracking using SDK 3.3 Out of Box detection chain
  Used in the following demos
    Long Range People detection
    Traffic Monitoring
    Area Scanner
    Automated Doors and Gates
TrackerProcCapon DPU and Capon3D DPC
  2D/3D Object Tracking using Capon beamforming detection chain
  Used in the following demos
    3D People Counting Demo – Side Mount
    3D People Counting Demo – Overhead Mount
    Sense and Direct HVAC Control Demo
StaticDetProc DPU and StaticObjeDet DPC
  2D/3D Object tracking using SDK 3.3 Out of Box detection chain with added Static detection capability
  Used in the following demos
    Area Scanner
    Automated Doors and Gates
Available in Industrial Toolbox 4.x download under C:\ti\mmwave_industrial_toolbox_4_x_x\labs\common

## Slide 50: Area Scanner and Automated Doors
Custom processing chain developed for Area Scanner and Automated Doors Demos.
Based on xWR68xx OOB Range-Doppler Detection Chain with addition of 2D AoA using DSP
Adds Object Tracking and Static Detection Capabilities

## Slide 51: Demo: Long Range Outdoor People Detection and Tracking

## Slide 52: 100m People Detection and Tracking
Features
  SDK 3.3 Range Doppler Detection Chain with Object tracking on R4F
  Tracker DPU developed on top of SDK 3.x
  Runs on IWR6843ISK ES2.0 and IWR1843BOOST
  Supports 2D and 3D tracking
  People tracking tested upto 100m with IWR6843ISK ES2.0 (3TX SIMO)
  Re-used for Traffic Monitoring Demo on IWR1843/6843
  Supports ISK, ODS and AOP antennas (for Indoor applications such as Area Scanner with Static Detection)
    DSP based AoA DPU modified to add 2D DoA for ODS/AOP
  Built on SDK 3.x OOB Demo
    Advanced features included for free e.g. Run time CFAR tuning, FoV filtering, ADC data streaming over LVDS.
Sub frame based TX Beam Steering
Overview

## Slide 53: 3D Long Range Tracker Chain
DSP
R4F
3D Tracker DPU
+ 2D DOA support
+ Spherical output
Tracking on R4F
Tracking on DSP
Point Cloud + Tracker output
Uses SDK gTrack Lib
×
×
×
×
R4F
×
×
Denotes Unused Datapath
Denotes new or modified components
Notes: Each of the mmWave device offers different processing nodes to realize the mmwave processing. xWR14xx has HWA engine, xWR16xx has DSP C674x core, xWR68xx and xWR18xx has HWA+DSP(C674x). For devices with multiple processing nodes, the mmWave detection processing chain can exploit them as needed for performance and scalable reasons. Shown here is an example of detection processing chain that uses various data processing units (DPUs) to perform the typical mmwave processing upto the point cloud. The mmwave data representation in mmWave device memory forms an interface layer between the various DPUs. Each DPU can be realized independently using HWA or DSP processing node - the choice is either driven by usecase or availability of that processing node on a given mmWave device.

## Slide 54
SLYP721