## Slide 1: Techniques for PIR-based motion detection
Miro Oljaca
Building Automation Systems

## Slide 2: PIR operation and limitation

## Slide 3: Infrared radiation (IR)

## Slide 4: Wien's displacement law
Mammals with a skin temperature of about 300°K emit peak radiation at around 10 μm in the far infrared. This is therefore the range of infrared wavelengths that pit viper snakes and passive IR cameras must sense.
Black-body radiation curve for different temperatures will peak at different wavelengths that are inversely proportional to the temperature

Credit: 4C, CC BY-SA 3.0, via Wikimedia Commons

## Slide 5: Indoor (TA = 72 °F) vs outdoor (TA = 94 °F)

## Slide 6: PIR sensor range is affected by: Environmental conditions including ambient temperature and light sources

## Slide 7: Pyroelectric infrared (PIR) sensor
300°K
(9.3 µm)
Part: IRA-S210ST01, courtesy Murata.com
Spectral response of window materials
Heat source movement
Sensor output voltage
Image source:
Murata.com

## Slide 8: PIR sensor operation, heat source movement
~ 3.6 mVpp
Pyroelectric Infrared Sensor IRA-S210ST01
(courtesy Murata.com)
Direction Distance Speed
Distance [inch] | Vpp [v]
30 | 3,14
70 | 1,42
90 | 0,92
130 | 0,42

## Slide 9: Noise reduction techniques

## Slide 10: PIR analog signal chain (from TIDA-00489)
Advantages
  Simple, low power
Disadvantages
  Gain/bandwidth are fixed in hardware
  Filter capacitors can act as noise sources (see next slide)

## Slide 11: Barium titanate (BaTiO3)

## Slide 12: SNR improvement with capacitor free design
Noise Source
Capacitor as noise source:
Ceramic - Microphonic
Tantalum - 1/f3
Bandpass Filter
Capacitor Free

## Slide 13: Single chip ultra-low power PIR solution
Advantages
Configurable gain and pass band  allows for optimizations for detecting targets at different distances and speeds
Low noise  Improved SNR in signal chain reduces false detections
Low average power consumption  long battery life
Fewer components  lowers BOM cost and simplifies layout

## Slide 14: MSP430 analog signal acquisition current
IAV = 5 µA @ 20 sps

## Slide 15: Battery life calculation
Assumptions (based on TIDA-00489)
  Current in low power mode: 5 uA
  Active-mode duration when event occurs: 60 s
  Additional current during active period: 645 nA
  Average current during wireless transmission: 1.12 mA
  Duration of wireless transmission: 104 ms
  Number of detection events per hour: 10
  Battery derating factor: 85%
Battery life
  CR2032 @ 240 mAh: 4+ years
  CR2450 @ 600 mAh: 10+ years

## Slide 16: Sub-1 GHz communication options
Option 1: MSP used to run simple Sub-1G protocol and interface to external transceiver
Option 2: Capacitor-less solution can be migrated to a wireless MCU (less integration of analog generally possible). Example below:

## Slide 17: Other topics to consider
Multiple PIR sensors and to reduce false triggering (e.g., due to pets)
Dual-mode detection techniques:
  PIR + optical ToF (improved sensitivity to longitudinal movement)
  PIR + ultrasonic
  PIR + discrete doppler
Tamper/masking resistance

## Slide 18: Advanced motion detection
Multiple PIR
PIR + camera
PIR + ToF
PIR + Ultrasonic
PIR + uWave

## Slide 19: Sensor and Fresnel lens combination
Image source: Murata.com

## Slide 20: Sensor and Fresnel lens combination cont.
The solutions consist to use three sensors with different lenses, in order to have different covered zone.
The first sensor will cover the whole area. This sensor will trigger the MCU and the rest of the circuit
The second sensor will cover the bottom and top vertical zone
The third sensor will cover the medium vertical zone
20
1,80m
Sensor 1
Sensor 2
Sensor 3
5m
0m
3m
3m
Sensor
height

## Slide 21: Advanced motion detection
Multiple PIR
PIR + camera
PIR + ToF
PIR + Ultrasonic
PIR + uWave

## Slide 22: PIR + camera system
Zone 1
Zone 2
For systems that combine PIR sensors with cameras (for example, home security systems, video doorbells), it is possible to use the PIR to trigger the camera.
Once activated, the camera can determine whether the motion occurs within specific user-defined zones.
This helps to reduce nuisance notifications (e.g., due to pedestrians on sidewalk/street, movement of trees, etc.).

## Slide 23: Advanced motion detection
Multiple PIR
PIR + camera
PIR + ToF
PIR + Ultrasonic
PIR + discrete Doppler

## Slide 24: PIR motion detection: False alerts
Motion is detected because PIR more sensitive to lateral motion compare to longitudinal)
PIR Sensor

## Slide 25: Motion detection using Time of Flight (ToF)
IR Tx/Rx
Distance is detected because:
Time between emitted and reflected wave is measured (ToF)
Motion is detected because:
There is difference in distance between consecutive measurements.

## Slide 26: PIR with ToF motion detector eliminating false alerts
Passive single of multiple PIR/s
Low Standby Current of 1.65 μA
Optimized for low-power battery operations
Motion sensitivity up to 30 ft
Generates interrupt
Great flexibility
Low cost
Active ToF with multiple Tx
Sleep Mode Current 10 - 20 μA
Interrupt driven low-power battery operations
Motion sensitivity 1.6 to 12 m
Registers: phase and amplitude
Great flexibility
Low cost

## Slide 27: TIDA-010021: Wide-range (120° FoV at 1.6 Meters) proximity sensing with immunity to sunlight
Features
Three NIR emitters support up to 3 zones of detection with a single OPT3101 device
Total system Field-of-View (FoV) of 120° is covered by three LED emitters and one photodiode
Detection range up to 1.6 meters without lens
Adaptive high dynamic range (HDR) feature enables the detection range of system very wide
ToF based sensing AFE (OPT3101) makes measurement insensitive to object color and reflectivity and supports operation under high ambient condition (outdoor and Indoor Conditions)
Proximity sensing and direct distance measurement output with accuracy of ±10%
Low power mode running at 1 sample per second with a power drain of 30 mW
Exempt group lamp classification LED as emitter

## Slide 28: Advanced motion detection
Multiple PIR
PIR + camera
PIR + ToF
PIR + Ultrasonic
PIR + discrete Doppler

## Slide 29: ToF measurement using PGA460
 | Standard | Advanced
Drive Mode | Half-bridge (direct) | Transformer
Recommended Supply Voltage | 6V | 9V
Minimum Distance | 30cm | 15cm
Maximum Distance | 3m (human sized target) | 6m (human sized target)
Power per 1s interval | 3.7mW | 7.8mW
Solution Cost (at high volume) | $1.50 | $2.00

## Slide 30: TIDA-060024: Ultrasonic proximity-sensing module (PSM) reference design

## Slide 31: Advanced motion detection
Multiple PIR
PIR + camera
PIR + ToF
PIR + Ultrasonic
PIR + discrete Doppler

## Slide 32: Doppler effect (Doppler Shift)
Ultrasonic
Sensor
Motion is detected because:
Reflected and emitted wave have different frequencies.
Ultrasonic, Microwave, mmWave and ToF can be used to measure Doppler shift.

## Slide 33: Doppler effect (Doppler shift)
The Doppler effect (or the Doppler shift) is the change in frequency or wavelength of a wave in relation to an observer who is moving relative to the wave source.
Relationship between observed frequency f and emitted frequency f0 is given by:
If the speeds vs and vr are small compared to the speed of the wave, the relationship between observed frequency f and emitted frequency f0 is approximately
where
c is the velocity of waves in the medium
vr is the velocity of the receiver relative to the medium
vs is the velocity of the source relative to the medium
Credit: Lookang, CC BY-SA 3.0, via Wikimedia Commons

## Slide 34: Intermediate frequency (IF)
Intermediate frequency (IF) is a frequency to which a carrier wave is shifted as an intermediate step in transmission or reception. The intermediate frequency is created by mixing the carrier signal with a local oscillator signal in a process called heterodyning, resulting in a signal at the difference or beat frequency.
Heterodyning is a signal processing technique that creates new frequencies by combining or mixing two frequencies. Heterodyning is used to shift one frequency range into another, new one, and is also involved in the processes of modulation and demodulation. The two frequencies are combined in a nonlinear signal-processing device. In the most common application, two signals at frequencies f1 and f2 are mixed, creating two new signals, one at the sum f1 + f2 of the two frequencies, and the other at the difference f1 − f2. These frequencies are called heterodynes. Typically only one of the new frequencies is desired, and the other signal is filtered out of the output of the mixer. Heterodyne frequencies are related to the phenomenon of "beats" in acoustics.

## Slide 35: Intermediate frequency (IF) cont.
Doppler frequency fd is proportional to the object speed v:
or

## Slide 36: Motion detector using Doppler Effect

## Slide 37: Motion detector using Doppler Effect cont.
For detecting Persons, BW is around 4Hz to 400Hz.

## Slide 38: Comparing different motion detector technologies

## Slide 39: Motion sensor technology comparison
 | PIR | Microphonics | Ultrasonic | Microwave | mmWave | Camera | TOF
Motion Detection Operating Principle | Difference between heat of object and background | Detect audible sound levels compared background | Measure frequency shifts in the reflected ultrasonic sound waves (Doppler Sonar). TOF measurements also used. | Measure frequency shifts in the reflected microwaves (Doppler Radar). TOF measurements also used. | Measure phase and frequency shifts in the reflected millimeter waves as well as TOF measurements (Doppler Radar) | Compares consecutive image frames through image processing to determine motion. Depending on sophistication of algorithm, can filter for human motion. | Modulated IR transmission and reflection. Time of flight for reflections measured to calculate distance. Processing required for background calibration and analysis to detect presence and motion
Cost | $ | $-$$ | $$ | $$-$$$ | $$$$ | $$-$$$$ (application dependent) | $-$$
Range | 10-12m | 10-20m | 10-12m | 10-30m | ~10m (fine motion) 50m+ (broad motion) | 30m+ | ~6m (with lens) <20m (narrow FOV, increased power)
Requires clear line of sight between object and sensor | Yes | No | No (Can be directive thru use of horn or transducer design) | No | No | Yes | Yes
Power Consumption | Lowest | Low | Medium | High | High | Medium - High | Med
Fine Motion Detection | No | Maybe (depends on sound level of fine motion relative to background noise) | No | Maybe (depends on field of view) | Yes | Maybe (depends on space, zoom capabilities, and camera resolution) | Maybe (depends on space and field of view)
Notes: - Rain will be detected by Microphonics, Camera, and TOF technologies. Can be filtered out in Microphonics as background noise.
- Glass constrains ultrasonic waves (ultrasonic barrier). Sound waves reflect off solid surfaces.
- For best range, ultrasonic transducer should be exposed to open air with flexible membrane to absorb vibrations

## Slide 40: Motion sensor technology comparison (cont.)
 | PIR | Microphonics | Ultrasonic | Microwave | mmWave | Camera | TOF
Major Performance Advantages | Lowest Cost Lowest Power (passive sensing) reasonable range | Passive sensing of sound waves With signal processing, capable of masking non-human sounds | Capable of measuring the speed of object’s motion Capable of detecting stationary objects Can “see” around corners | Capable of measuring the speed of object’s motion Capable of detecting stationary objects Can “see” through walls | Capable of measuring the speed of object’s motion Capable of detecting stationary objects Can “see” through walls Capable of measuring angle of approach and distance Carrier can be used to enable additional services | For systems with a camera, no additional sensors are required for motion sensing Motion events can be recorded and replayed | Capable of precise distance measurements Capable of detecting stationary objects
Major Performance Disadvantages | Sensitive to false triggering for anything creating changes in temperature or white light Long time constant | Loss of sensitivity (SNR) in environments with high ambient noise | Can detect motion of objects outside of the desired field of detection by reflection around corners Will detect motion of inanimate objects Can be harmful to pets | Can detect motion of objects outside of the desired field of detection (capable of penetrating walls) Will detect motion of inanimate objects Can be sensitive to certain fluorescent lighting | Can detect motion of objects outside of the desired field of detection (capable of penetrating walls) Will detect motion of inanimate objects | Cannot “see” in dark environments unless coupled with illumination and filtering for night vision Dust, dirt, moisture effect image quality | Cannot “see” through fog, dust, or smoke Will detect motion of inanimate objects Measurement errors for reflective or IR absorbing materials
Notes: - Rain will be detected by Microphonics, Camera, and TOF technologies. Can be filtered out in Microphonics as background noise.
- Solid surfaces such as Glass constrains ultrasonic waves (ultrasonic barrier). Sound waves reflect off solid surfaces and are absorbed by soft materials.
- For best range, ultrasonic transducer should be exposed to open air

## Slide 41: Motion sensor technology comparison (cont.)
 | PIR | Microphonics | Ultrasonic | Microwave | mmWave | Camera | TOF
Enclosure influence | Requires Fresnel lens which directly impacts shape and appearance of enclosure | Needs hole(s) for microphone input in enclosure No protrusions required | Vents needed in the enclosure to avoid attenuation of the transducer signals | Enclosure only needs to be large enough to house transducer Transducer can be concealed as long as material is transparent to carrier frequency | Enclosure only needs to be large enough to house transducer Transducer can be concealed as long as material is transparent to carrier frequency | Enclosure designed around camera lens | Enclosure needs to include IR transparent material to accommodate IR transmission and reception of reflected IR.
Direction of motion with highest sensitivity | Lateral | Omni | Longitudinal | Longitudinal | Longitudinal | Uniform in FOV of Camera Lens | Longitudinal
Notes: - Rain will be detected by Microphonics, Camera, and TOF technologies. Can be filtered out in Microphonics as background noise.
- Solid surfaces such as Glass constrains ultrasonic waves (ultrasonic barrier). Sound waves reflect off solid surfaces and are absorbed by soft materials.
- For best range, ultrasonic transducer should be exposed to open air

## Slide 42
SLYP722