## Slide 1: Getting started with the new PSpice® for TI design and simulation tool
Ian Williams
APP – LP – LDO

## Slide 2: About me – Ian Williams Business lead, Low-Voltage LDOs
Career
  BSEE University of Texas at Dallas, 2009
  TI since 2009, LDO since July 2020
Expertise
  11 years working with various types of amplifiers
  Co-creator of GWL amplifier SPICE model architecture
  Co-creator of TI Precision Labs – Op Amps
Fun fact
  Big music guy – have performed at festivals, DJ’d at clubs and on FM radio, and even met my wife at Coachella 2013

## Slide 3: Agenda
TI simulation tools overview – 10 min.
PSpice® for TI deep dive – 10 min.
  Features and limitations
  Built-in model library
Setup and simulation examples – 25 min.
  Operational amplifier: OPA211
  Power supply: TPS7A52
  Modeling Application: Power MOSFET
Additional resources
Please ask your questions in the chat!
?
?
?

## Slide 4
Part 1 TI simulation tools overview
Tip: SPICE stands for “Simulation Program with Integrated Circuit Emphasis”

## Slide 5: Time for some audience participation…

## Slide 6: Introducing PSpice® for TI
PSpice for TI will help engineers speed time to market and reduce development costs, delivering:
Full-featured simulation of entire systems.
  Advanced capabilities, including Monte Carlo and worst-case analysis.
  Synchronized library of >5,700 models and counting.
  No design size limitations.
  Easy transition to layout and prototype.
Integrated design resources.
  Quick access to TI product information.
  No need to manually upload new TI models.
Notes: PSpice for TI is based on the popular PSpice simulator that many of our customers know and love. This is an enterprise-level, full-featured tool that will enables design engineers to build a complete schematic and simulate at the system level with no design size limitations.
Advanced capabilities of this tool include automatic measurements and post-processing, as well as Monte Carlo and worst-case analysis, that will enable engineers to fully validate their designs over a wide range of operating conditions and device tolerances with just a few clicks.
With these features, users have access to one of the industry’s largest libraries of IC models. The built-in model library in PSpice for TI is synchronized with updates as TI releases new models, which means you no longer need to upload new models to your simulator as they become available.
There is an easy path to layout and prototype thanks to the tool’s OrCAD Capture framework. After a user completes validation of a simulated design, they can then open the design in any commercial version of the PSpice Designer product family, then transfer the design to their PCB tools like OrCAD/Allegro PCBO Designer without having to recreate their schematic.
As Ian will show in the demo, there are also many built-in design resources that TI offers that make it easy to get the product information you need in the tool. While you are simulating with an op amp, for example, you can easily access its data sheet, associated reference designs and other design resources for that part. We will also connect you to TI’s E2E support forums so you can get technical support with your design.

## Slide 7: Why is TI partnering with Cadence?
Growing demand
There is an increased need for simulation software to test new design concepts, accelerate product development and demonstrate regulatory compliance.
Short design timelines
Today’s design engineers must produce accurate designs on tight deadlines — in many cases, reducing the prototyping and evaluation phases of their designs.
Source: ABI Research
Desire for more advanced simulation
Existing simulation tools in the market lack advanced analysis capabilities, model portability and flexibility, and easy library synchronization.
“Tools that are intuitive and include system-level simulation capabilities can cut the development time and speed time to market.” – Kevin Anderson, Omdia
Notes: When we look at the current landscape of design tools that are available to design engineers, we see a few themes.
First, there is an increased need for simulation software to test new design concepts, accelerate product development and demonstrate regulatory compliance.
Second, we are increasingly seeing that the timelines for design engineers are getting shorter. In some cases, we are even seeing that they are reducing the prototyping and evaluation phases of their design and jumping straight to PCB layout. This is where the right design tool can make life easier for them. Now that working from home is more common, using simulation means that you can make progress on your projects without needing to wait for parts, PCBs or lab equipment.
Finally, we have seen a desire among engineers for more advanced simulation that helps them work more quickly and run advanced analyses to help them reduce the risk of circuit errors in their designs.

## Slide 8: Is PSpice for TI replacing other TI tools?
Design & simulation
Design
support
Fundamentals & skill-building
Investigation & brainstorming
Educational e-books
Technical articles
TI Precision Labs
Power Supply Design Seminars (PSDS)
Additional videos at training.ti.com
Easy part selection on TI.com
Reference designs for specific applications
Application notes and technical white papers
e2e.ti.com
Forums for expert answers to technical questions
Evaluation modules
WEBENCH® Power Designer
Filter Design Tool
Analog Engineer’s Calculator, Circuit Cookbooks & Pocket Reference
TINA-TI™
Notes: The reason that TI is so passionate about this is because it is our goal and our strategy to meet customers where they are and provide the very best resources at every stage of their design cycle.
We’ve been doing this for a long time – from providing e-books, articles and in-depth video content to help engineers build new skills – to making it as easy as possible to find parts and reference designs with design ideas on TI.com – to providing tools and calculators and references to be used throughout the design and simulation phase – and of course to providing dedicated support throughout a customer’s design.
We are excited to be adding PSpice for TI to our design & simulation portfolio as a complement to our other design resources.

## Slide 9: PSpice for TI vs. TINA-TI
 | PSpice for TI | TINA-TI
Analysis / simulation |  | 
AC, Noise, BIAS point, DC sweep, Transient, Fourier | Yes | Yes
Variable sweeps | Temperature, component, parametric | Temperature, component
Monte Carlo analysis | Yes | No
Worst case analysis | Yes | No
Libraries / components |  | 
Internal libraries | ~5700 | ~1300
Automatic library updates | Yes | No
Built-in modeling application | Yes | No
Schematics |  | 
Create hierarchical schematic | Yes | No
Multipage schematics | Yes | No

## Slide 10
Part 2 PSpice for TI deep dive
Tip: PSpice for TI runs offline!

## Slide 11: Software features and limitations FAQ
Q. Does PSpice for TI work offline?
  A. Yes, an internet connection is not required to run.
Q. Is there a maximum number of nodes?
  A. No, there are no design size limitations. You can also use multi-page schematics and hierarchical blocks.
Q. Are there any other limits to be aware of?
  A. Yes. The tool is designed primarily as a SPICE simulation environment for use with the built-in TI models. If third-party models are imported, then only three nodes can be probed simultaneously.

## Slide 12: Built-in TI model library
Matches the product tree on TI.com
Includes device-specific test benches
To accelerate your development

## Slide 13: How do I update the TI model library?
Updates to the model library are automatically detected and performed at software startup.
  The user can choose not to update.
The model library is installed locally on the user’s hard drive. Models can be copied and imported into other tools if desired.
  Location: C:\SPB_Data\cdssetup\pspTILibDir

## Slide 14: Are models editable?
Models are text files and may be edited with a text editor (I recommend Notepad++) from the library directory
  Note: editing TI models breaks their signature, causing the tool to treat them as 3rd-party
Some models have user- editable parameters. Editing these does not break signature.
If you edit a model and save it in the same location, it will get over-written during the next library update.
Model file example

## Slide 15: Modeling application
Used to add customizable, parameterized components to your design:
  Power MOSFETs
  Power diodes
  Passives with parasitics
  Independent sources
  Switches
  Transformers
Click Place  PSpice Component…  Modeling Application in the top menu bar
Note: these components do not trigger the probe limit

## Slide 16: Modeling application, cont.
A simple UI opens for each type of component with editable fields
Customize each parameter to your liking, then click Place to drop in schematic
  Note: Device parameters can still be edited from their properties once in the schematic
Power MOSFET window
Power NMOS in schematic

## Slide 17: Additional included model libraries
These standard PSpice libraries are also included:
Note: components from these libraries do not trigger the probe limit
Library | Description
ABM | Analog behavioral models for various math functions
ANALOG | Passives, dependent sources, switches, transmission lines
BREAKOUT | Customizable versions of many device types
DIG_MISC | Digital timing control, pull-up / pull-down resistors
DIG_PRIM | Logic gates, flip-flops
SOURCE | Independent voltage and current sources
SPECIAL | Parameters, simulation control, library management, utilities

## Slide 18: Importing third-party or custom models
With your project (.opj) selected, click Tools  Generate Part
Browse to your model file in the new window, make your selections, and click OK
The new model appears in your project’s library

## Slide 19: Types of models on TI.com
Type | Description
PSpice | Analog / mixed-signal model for use in PSpice-based simulators. Packaged in a way to be easy to import and use in PSpice / Cadence / OrCAD.
TINA-TI | Analog / mixed-signal model for use in PSpice-based simulators. Packaged in a way to be easy to import and use in TINA-TI.
HSPICE (uncommon) | Analog / mixed-signal model for use in HSPICE-based simulators. HSPICE is a branch of SPICE similar to PSpice, but models are not directly compatible.
SIMPLIS | Switch-mode power supply model for use in SIMPLIS.
IBIS | I/O Buffer Information Specification model, typically used for digital pin timing analysis. Compatible with a broad range of industry simulators.

## Slide 20
Part 3 Setup and simulation examples
Tip: Enabling AutoConverge in your sim profile can fix a broad range of convergence issues.

## Slide 21: Operational amplifier example – OPA211
Schematic capture
AC simulation result

## Slide 22: Power supply example – TPS7A52
Schematic capture
Transient simulation result

## Slide 23: Modeling Application – Power MOSFET
Schematic capture
DC simulation result

## Slide 24
Part 4 Additional Resources
Tip: Choose the “Last Plot” setting in your sim profile to preserve results display settings between runs.

## Slide 25: Additional resources
Self-guided, step-by-step tutorial that walks the user through the entire tool workflow
  Includes basic and more advanced content
  Includes debugging and troubleshooting
Available from the PSpice for TI start page:
  Click Training Course
Hands-on training manual

## Slide 26: Additional resources, cont.
Overview content
Technical training videos
TI.com/pspice-for-ti
How to simulate complex analog power and signal-chain circuits with PSpice® for TI
[Link]
PSpice for TI
overview video
[Link]
[Link to videos]
Notes: We have a number of resources that we can share with you, including a short article from TI that gives an overview of the features of PSpice for TI, and several overview videos. We will share a copy of this presentation and links to these resources after the presentation.

## Slide 27: “Trust, but verify” SPICE models
Series of articles that covers verifying parameters of amplifier models:
  Part 1: Output impedance
  Part 2: Small-signal bandwidth
  Part 3: Input-referred errors
  Part 4: Noise

## Slide 28: Direct support from TI
For tool-related support: Simulation, hardware & system design tools forum
For specific model or product support: post to that product’s forum
  i.e. For amplifier support, post to the Amplifiers forum
Note: these forums are all supported by TI applications engineers who are graded on responsiveness and quality of support. You should get an initial reply in 24h.

## Slide 29: SPICE tips – analysis parameters
Option | Default | Relaxed | Effect
AutoConverge | Off | On | Relaxes multiple parameters if needed to enable convergence
ABSTOL | 1e-12 | 1e-10 | Sets the absolute tolerance of nodal currents between DC iterations
RELTOL | 1e-3 | 3e-3 | Sets the relative tolerance of the nodal voltages at each DC iteration compared to the first
GMIN | 1e-12 | 1e-10 | Adds conductance parallel to every p-n junction
CSHUNT | 0 | 1e-15 | Adds capacitance from every node to ground
Notes: If you’ve followed the techniques I’ve shown but still have convergence issues, you can often “hack” the analysis parameters to relax the tolerances and be able to get better convergence at the cost of accuracy
The analysis options on this slide are standard in SPICE, but may have different names in different simulators
If you look in the help file of your simulator of choice, you will often see an explanation of each parameter with its standard SPICE name given for reference
Abstol – Sets the absolute tolerance of nodal currents between DC iterations. Increasing this tolerance means the solver can essentially “be lazy” with what it will accept as a correct answer
Reltol – Sets the relative tolerance of the nodal voltages between DC iterations, relative to the first iteration. As with abstol, increasing this lowers the accuracy requirements for each iteration
Gmin – Adds conductance parallel to every p-n junction, aiding with linearity and providing DC paths
Cshunt – Adds capacitance from every node to ground, helping to reduce the sharp edges/glitches in some nonlinear circuits that can cause problems for the solvers
Different simulators will also more options specific to that simulator which can also aid in convergence and should be explored if running into more issues.

## Slide 30: SPICE tips – DC path to GND
Ensure DC path to ground at every node
  Can force a path with large resistors (1T, etc.) that don’t affect electrical performance
  Try to use the smallest value possible
Notes: The first step to any simulation is finding an initial DC operating point
DC paths to ground are critical for finding this operating point, as all capacitances are considered to be open circuits in this case
If paths to ground are not provided, more complex solvers (such as Source Stepping and Pseudo-Transient) may be needed, which taken much more time than the simple solvers like Direct Newton and Gmin stepping

## Slide 31: SPICE tips – linear circuits
Design functional blocks with as linear behavior as possible
  Sharp transitions or discontinuities cause issues with convergence checks
  Use R-C filter networks to reduce bandwidth of subcircuits for smooth transitions
  Use voltage inputs and current outputs wherever possible
R-C filter slows edges of subcircuit output
Voltage inputs
Current output
Resistor converts current to voltage and provides DC path to GND
Notes: This is an example of a support circuit used to control switches in the model that is designed for good SPICE convergence.
H2 and H3 convert a current sensed elsewhere in the circuit to a voltage. When voltage inputs OLN and OLP are below a certain threshold, the subcircuit OL_SENSE is “off” and its output is 0A. When either input exceeds the threshold, the subcircuit turns “on” and its output transitions almost instantly to 1A. The output currents of 0A and 1A are converted to an output voltage of 0V and 1V by a load resistor.
Output R-C reduces the bandwidth of the output, and causes a smooth low-to-high transition with an exponential shape over many picoseconds, instead of a near-instantaneous step

## Slide 32: SPICE tips – bounded matrix
Keep matrix equations as tightly bounded as possible
  Place limits on gain and buffer stages
  Use only as much gain as required
  Scale resistances to keep node voltages and currents in similar ranges
Notes: This circuit is a gain block, using techniques to keep the overall matrix better (more tightly) bounded and easier to converge
In matrix equations that define the circuit, the range of all aspects (resistance, capacitance, voltages, currents, etc.) affects convergence
The tighter the range of values, the easier it is for the solvers to find an answer, since the relative values are much closer together and changes are not as drastic
VCCS_LIM_1 is a code-defined voltage-controlled current source used as a gain stage
The gain of the block is set to 1e-4, which is actually attenuation, but the output is a current and is converted to a voltage by the load resistance R44
Total gain = 1e-4*1e6 = 100V/V = 40dB
The subcircuit uses a limit function to set the maximum current output to ±0.5A

## Slide 33: SPICE tips – simplified components
Replace complex components with simple approximations if exact component modeling isn’t necessary
  Example: ideal diode  voltage-controlled switch
Diode equation:
Notes: For cases where the detailed modeling of the component is NOT critical, consider replacing the component with one that achieves a similar behavior
Step through desired operation of this example diode clamp circuit
Diodes are defined by a relatively complex exponential equation, and this is only for first-order behavior. Over a dozen additional parameters are used to compute secondary effects and behavior such as breakdown!
Switches are simpler, and are either equal to Roff, Ron, or a resistance between based on the voltage across its inputs set by a single equation
Switches also contribute no noise, unlike diodes, allowing very low noises to be tuned in, especially for input current noise that can be in the fA/√Hz

## Slide 34
Thank you!

## Slide 35
SLYP725