## Slide 1: A simple, robust, and low-EMI solution for inverter gate driver bias supplies
High Voltage Seminar
Bing Lu

## Slide 2: Agenda
Inverter and isolated gate driver bias supply architectures
Different ways of creating isolated bias supply
  Control method
  Topology
  Transformer
LLC based open-loop isolated bias supply
  Operation principles
  Circuit variations
  Voltage regulation
  Multiple outputs
Performance demonstration

## Slide 3: Inverters in different applications
Traction inverter
Motor drive
Onboard charger
UPS

## Slide 4: Example: inverter isolation boundaries
How to bias the isolated drivers?

## Slide 5: Different gate driver architectures
Centralized
Semi-Distributed
Distributed
Centralized system has lowest cost, but heavy and difficult to manage fault
Distributed system distribute the weight and fault, but more expensive
Semi-distributed is somewhere in the middle

## Slide 6: Output voltage control
Close loop
Secondary side feedback
Well regulated output
No need pre-regulator
More components
Less reliable due to the opto coupler
Close loop
Primary side feedback
Semi regulated output
  Determined by cross regulation
No need pre-regulator
Noise sensitive due to the output voltage sampling method
Open loop
No feedback
No control loop, robust operation
Less noise
  Coupling only through the transformer
Unregulated output, need pre-regulator
Open-loop control provides a robust solution

## Slide 7: Topologies used for isolated bias supply
Flyback
Push-pull
LLC

## Slide 8: Flyback converter topology
Flyback can easily create multiple outputs
  Voltage proportional to the turns ratio
  Suitable for centralized architecture
Can be controlled with opto feedback or primary side feedback
Need well coupled transformer

## Slide 9: Push-pull topology
With 50% duty cycle operation, in each half switching cycle, output is connected with input through the transformer
Filter inductor is needed if the duty cycle is less than 50%
Transformer needs to have low leakage inductance to avoid ringing and device over stress
Good for distributed and semi-distributed architecture

## Slide 10: Transformer parameter impacts to system EMI
High dv/dt couples through transformer parasitic capacitor to the primary side
Higher EMI noise
Extra loss
More noise to the controller, CMTI issue
It gets worse with SiC or GaN devices with higher dv/dt

## Slide 11: Transformer structure: less parasitic capacitance
The capacitance can be reduced by increasing the insulator thickness
Less effective due to the large surface area
Split bobbin reduces the capacitance by reducing the surface area and increasing the distance
Much smaller capacitance can be achieve
Increasing the distance reduces the capacitance while increasing the leakage inductance

## Slide 12: How topologies respond to leakage inductance
Flyback
Push-pull
LLC
Leakage energy can’t be transferred to secondary side
Leakage causes
  More EMI noise due to ringing
  More loss
  More device stress
Leakage needs to be minimized
Leakage is part of resonant circuit
Leakage energy is fully recovered
No extra ringing caused by the leakage
No limitations on the leakage inductance

## Slide 13: LLC converter
At resonant frequency, the impedance of resonant tank is equal to zero, input and output is shorted through the transformer. Fixed frequency open-loop control is possible
The leakage inductance of the transformer can be used as the resonant inductor

## Slide 14: Transformers for isolated bias supply
CPri-Sec
~20 pF
~20 pF
<2pF
~10 pF
CMTI
Worse than LLC
Much worse than LLC
>150V/ns
Worse than LLC
Cost
>1.3X
>1.18X
1X
>1.15
Regulation
Better
Best
Good
Good
Poor
Poor
EMI
Best
Good
LLC Transformer
Push-Pull Transformer
Three-winding Flyback
Two-winding PSR
Flyback
~20 pF
Much worse than LLC
>1.18X
Good
Poor
Half-Bridge
LLC converter provides an order of amplitude capacitance reduction

## Slide 15: LLC converter variations
Transformer variations
Two-winding
Center-tap
Multi-output
Rectification Variations
Full-wave
Center-tap
Voltage-doubler
Voltage-doubler

## Slide 16: Primary vs. Secondary side resonant
Primary side resonant
Secondary side resonant
Chart: Switching frequency (kHz)
| 400 | 410 | 420 | 430 | 440 | 450 | 460 | 470 | 480 | 490 | 500 | 510 | 520 | 530 | 540 | 550 | 560 | 570 | 580 | 590 | 600
no P R no S R | 23.606 | 23.618 | 23.612 | 23.626 | 23.615 | 23.634 | 23.616 | 23.633 | 23.636 | 23.626 | 23.646 | 23.63 | 23.632 | 23.651 | 23.665 | 23.66 | 23.645 | 23.621 | 23.589 | 23.551 | 23.506
Chart: Switching frequency (kHz)
| 400 | 410 | 420 | 430 | 440 | 450 | 460 | 470 | 480 | 490 | 500 | 510 | 520 | 530 | 540 | 550 | 560 | 570 | 580 | 590 | 600
no P R no S R | 25.135 | 25.071 | 24.995 | 24.944 | 24.868 | 24.827 | 24.753 | 24.712 | 24.68 | 24.604 | 24.576 | 24.553 | 24.474 | 24.45 | 24.436 | 24.412 | 24.371 | 24.322 | 24.266 | 24.205 | 24.14
Secondary side resonant is less sensitive to switching frequency error

## Slide 17: Open-loop LLC voltage regulation
The voltage regulation is determined by transformer turns ratio and resistive loss, as well as the diode drop
It is critical to keep the resistive loss low to get best load regulation
n:1

## Slide 18: Illustration of voltage regulation
 | Normal operation |  | Standby mode load | Vout |  | 
 | Min load | Max load |  | Min | Max | Standby max
Fixed Fre. | Iload_3 | Iload_3 | Iload_0 | Vmin_2 | Vmax_2 | Vmax_3
Var. Fre. | Iload_1 | Iload_2 | Iload_0 | Vmin_1 | Vmax_1 | Vmax3
For a fix switching frequency inverter, the gate driver load is fixed
  The output voltage regulation can be very tight
For a variable frequency inverter, the gate driver load varies
  The output voltage varies more
The standby mode load voltage tends to go up
  It could be too high that need extra help from a Zener diode
  It is mainly determined by the diode junction capacitor

## Slide 19: Split single output voltage into dual outputs
Zener split
Lowes cost
Unregulated outputs
Shunt Regulator
Higher cost
Regulated negative output
Unregulated positive output
Shunt Regulator & Linear regulator
Highest cost
Regulated output

## Slide 20: UCC25800-Q1 Low-cost LLC transformer driver with high performance
Features
Benefits
Operation from 9 V to 34 V (40 V Abs Max)
6 W from 24-V input, Up to 10 W from 34-V input
Integrated half-bridge MOSFETs
Programmable fixed switching frequency up to 1.2 MHz
  – 1.2 MHz default, resistor settable 100 kHz – 1 MHz
  – Frequency accuracy +/-6% maximum over temperature
  – External SYNC function
Drive multiple transformers with one UCC25800-Q1
Automatic dead time adjustment with programmable maximum
Integrated soft-start
Disable pin with fault code output
Two-level over current protection
  – Programmable via external resistor
  – UCC25800L is latched after over current
  – UCC25800R is retry after over current
Over Temperature Protection
  – 160°C Junction
  – 10°C Hysteresis
AEC Q100 Qualified
Low common mode noise due to minimal interwinding capacitance in transformer
Simple design, highly integrated, no bootstrap capacitor
High switching frequency for smaller size and more robustness
Sampling
[Disclaimer: Specs, features & pinouts subject to change without prior notice.]

## Slide 21: UCC25800-Q1 measurement data
UCC25800 EVM with LM5156 Pre-Regulator
1% Load Regulation
Predictable Startup of +/- rails
Surpasses CISPR 25 Class 5
EMI Standard
PARAMETER | SPECIFICATIONS
Input voltage range | 6V – 26V
Output voltage and current | +18V / -5V
Switching frequency | 2.2MHz and 500 kHz
Isolation | Yes, 2500 VAC (1 sec)
Topology | SEPIC + Open loop LLC transformer driver
UCC25800-Q1
LM5156-Q1
Optional components for 1% load regulation
+18V
-5V
Pass - LLC Board Only with Filter

## Slide 22: Multiple outputs
Driving one transformer with multiple secondary side windings
Driving multiple two winding transformers

## Slide 23: Example: driving multiple transformers
Single primary side power stage drives three transformers and secondary side circuits
Three matched output voltages are created

## Slide 24: EMI noise performance comparison
5-V push-pull
24-V Flyback
24-V LLC
LLC has much lower high frequency EMI noise
*No EMI filter added

## Slide 25: EMI noise when connected with inverter
Flyback
LLC
When connected with inverter and bias the isolated gate drivers, LLC solution provides a much lower EMI noise due to the less parasitic capacitance

## Slide 26: CMTI performance
Operation is not affected by >150 V/ns CMTI
165 V/ns
155 V/ns
Switch node
Strike voltage
Switch node
Strike voltage

## Slide 27: Transformer design considerations
Transformer design is simple
  Two windings
  Turns ratio is roughly the voltage ratio between the input and output voltage (plus the diode drop)
  Square voltage on primary side, setting up the volt-second rating
  Lowest Rac possible
  No airgap
Once the transformer is made, measure the leakage inductance from secondary side
  Short the primary side while measuring
Match the leakage inductance with resonant capacitor
Part number (Wurth) | Turn ratio | Leakage inductance | Input / Output
750319331 | 1:1 | 1.4 uH | 24 V/24 V
750319177 | 1.67:1 | 1.48 uH | 15 V/24 V
750319177 | 1:1.67 | 0.53 uH | 24 V/15 V

## Slide 28: Summary
Isolated bias supply is needed for biasing the isolated gate drivers in the inverters
  Open loop control provides a robust solution, less noise sensitive
LLC topology is able to utilize the transformer leakage inductance and minimize the transformer primary side to secondary side parasitic capacitance
  Less EMI noise
The open loop LLC converter provides a simple, robust solution
  Less EMI
  High CMTI
  Good voltage regulation
  Multiple output capability

## Slide 29
©2021 Texas Instruments Incorporated. All rights reserved.
SLYP760