## Slide 1: Printed circuit board layout for switched-mode power supply
High Voltage Seminar 2021
Ben Genereaux

## Slide 2: What will I get out of this session?
The purpose of this session is to introduce the concepts needed to successfully layout a printed circuit board (PCB) for a switched-mode power supply (SMPS)
This presentation is relevant to all SMPS PCB layouts, from 1 W to 10 kW
Part numbers mentioned:
  UCC28180
  UCC28742
  UCC28710
  UCC24612
  UCC24610
Reference designs mentioned:
  TIDA- 00443
Notes: This session will provide you with fundamental concepts for a successful PCB layout for a switching power supply.
These rules and techniques are applicable to all switching power supplies, regardless of power level.
We will look at various examples of layouts including the UCC28180 CCM PFC controller; the UCC28742 and UCC28710 QR flyback controllers, and the UCC24612 and UCC24610 synchronous rectifier controllers.

## Slide 3: Why is layout important?
The best controller in the world cannot work well if embedded in a poor layout
PCB layout for SMPS is extremely complicated!
Same principles govern low and high power layouts
  The difficulty is how to apply the principles in practice
The PCB is often the most complex component in a design
How to translate a schematic into working hardware
Notes: Why is layout important?
The PCB is arguably the most complex component in a design.
In switching power supplies layout is especially critical for success.
As we will see, parasitic elements in a PCB layout can wreek havoc in a power supply. A bad layout can truly ruin a perfectly good design.

## Slide 4: Agenda
The schematic
Parasitics
  Resistance
  Inductance
  Capacitance
EMI & safety
Grounding & signal routing
Thermal management
PCB layout example
Summary
Notes: This video is split into two parts.
In this first video, we will be focusing on parasitic elements, which include resistance, inductance, and capacitance.
We will look at the how these parasitic elements are manifested, their effects, and how to mitigate them.

## Slide 5: What are concerns for a power supply PCB layout?
Safety
EMI
Parasitic inductance
Parasitic capacitance
Parasitic resistance
Thermal performance
High dv/dt
High di/dt
Grounding
Noise

## Slide 6: The schematic
EMI
di/dt
Safety
Thermal
dv/dt
High current
Grounding
Understand the circuit, including the parasitic components!
TIDA-00443 using UCC28180 PFC controller
Notes: Layout begins with the schematic. A clean schematic makes it much easier to create a clean layout. Functional groups of components should be placed together on the schematic, as they will be on the actual layout.
This schematic from the TIDA-00443 reference design featuring the UCC28180 PFC boost controller is a good example.
For a successful layout, you, the engineer must completely understand the circuit. Items like:
Where are the high current paths
Where are there switching currents
What nodes have switching voltage waveforms with high dv/dt
How much power loss is in each component
What safety rules apply to the application
How to filter and reduce EMI

## Slide 7: You mean copper is not a perfect conductor?
Material | mΩ-cm | mΩ-in
Copper | 1.70 | 0.67
Gold | 2.2 | 0.87
Lead | 22.0 | 8.66
Silver | 1.5 | 0.59
Silver (plated) | 1.8 | 0.71
Tin -lead | 15 | 5.91
Tin (plated) | 11 | 4.33
ρ(Cu) = 0.67 mΩ-in at 25°C
Impacts?
  Regulation
  Efficiency
  Temperature rise
Parasitic resistance
Notes: Resistance of components is always a problem in power supplies because it degrades regulation and creates power loss which leads to decreased efficiency and excess heat.
Even though we pick devices based on their resistance, the resistance of PCB traces is often overlooked.
Resistance of a conductor is determined by its resistivity and physical dimensions, as shown here. Resistance is proportional to the length and inversely proportional to the cross sectional area. So, to minimize resistance, we would want to use short traces with a large cross-sectional area.
The table here lists the resistivity for some common materials used in power supply construction. It is interesting to note that many materials used in soldering and plating such as Tin and lead are not nearly as good conductors as copper.
It is also important to realize that the resistivity of copper increases with temperature at approximately 4000 ppm per degree C, or roughly 40% for a 100 deg C rise.

## Slide 8: Counting squares
Assume 1 oz. Cu
Parasitic resistance
Notes: A simple way to estimate the resistance of a PCB trace is to use a technique called counting the squares.
From the resistance formula, if the conductor’s length and width are the same, they cancel out, and the resistance of that square conductor is simply the resistivity divided by the thickness.
Once the resistance per square is calculated, the designer can estimate the number of squares in a PCB trace and multiply by the resistance per square to get the total trace resistance.
It is much easier to remember that one square of 1 ounce copper is approximately 0.5 milli ohms than to try to remember the resistivity of copper and measuring trace widths and lengths.
In the example shown here, on the left side of the current sense resistor there are two squares in series, with 1 ounce copper this results in 1 milliohm of total resistance.
On the right side there are two squares in parallel from the edge of the resistor to the ground connection, for a total resistance of around 0.25 milliohms.

## Slide 9: Vias have resistance too
Typical rule of thumb is 1 A to 3 A per via
Parasitic resistance
Notes: An often overlooked current path is through the board vertically. For example from the top of the board to the bottom through vias.
The figure here shows the calculation of the via resistance for an outer diameter of 20 mils and inner diameter of 18 mils. This results in around 0.67 milliohms.
This seems insignificant, but consider that 10A flowing through a single such via would result in 7mV of drop and 67 mW of loss.
High current paths require multiple vias and larger vias with more cross-sectional area. A good rule of thumb is to limit the current per via to 1 to 3A.

## Slide 10
How many mΩ between L2 and J3?
Sensing at output connector
Poor sense location
Parasitic resistance
Notes: Now let’s put this knowledge to use. Here we are looking at the output filters of two power supplies going to a common connector. Current flows on the red etch from L2 to J3. The blue traces are the connections to the feedback of the power supply.
How many milliohms of resistance do you estimate between L2 and J3? Assume 1 ounce copper.
Pause
If we count three squares, that is roughly 1.5 milliohms between our sensing location and the output connector. The output voltage will be regulated at the inductor, where the blue sense etch connects and the parasitic resistance will lead to a 15mV drop for a 10A output current at the connector.
- Next animation -
To fix this, we could reduce the resistance in the current path, but it is more important to move the sense location near the connector so that the output voltage is regulated after the parasitic resistance.
This provides a well regulated voltage at the connector, regardless of the trace resistance between the inductor and connector.
Both of these layouts electrically match the schematic, but the one on the right will provide much better load regulation.

## Slide 11: Switched current loops
I/P loop (green)
di/dt rates much lower
Stray inductance is less critical
CIN provides local low impedance source
O/P loop (blue/red)
Inductor current alternates between MOSFET and diode paths
Pulsating currents
Stray inductance will cause voltage spikes
Diode current
MOSFET current
Inductor current
I/P loop
O/P loop
High di/dt
Low di/dt
Simplified PFC boost schematic
Identifying high di/dt
Notes: Now, let’s discuss another parasitic element – inductance.
Parasitic inductance in high di/dt current loops can cause large voltage spikes that can cause EMI, circuit malfunction, and even device failure.
The first and most critical step when dealing with parasitic inductance is to understand your circuit and identify the current loops with high di/dt.
Here is a simplified schematic of the CCM PFC boost example that we introduced earlier.
There are three current paths with switching currents.
The highest di/dt occurs in the MOSFET shown by the blue waveform and in the output diode shown by the red waveform. Inductance in these paths can cause huge voltage spikes when the Fet turns on and off.
The input loop shown in green also experiences an AC current, but the di/dt rates are much lower. Parasitic inductance is less of a concern in this path. Intuitively you can see that any parasitic inductance in series with the power inductor will simply add.

## Slide 12: Reverse recovery
Occurs when:
MOSFET turns ON during CCM operation (nearly every topology)
Stray inductance will cause voltage spikes
Mitigation:
Minimize loop inductance
Use low QRR rectifiers –
SiC for high VOUT
Schottky or ultra-fast diodes
Sync rectifiers with low QRR
Simplified PFC boost schematic
Identifying high di/dt
Notes: Another source of high di/dt can occur due to reverse recovery of diodes in the switching paths.
In our CCM boost example, this occurs in the output diode when the FET turns on, while there is still current flow to the output.
As the stored charge is swept out of the diode junction, large current spikes can be created, which in turn can cause voltage spikes due to the parasitic inductance.
This is a concern in nearly every topology when operated in continuous conduction mode.
The first step to mitigating this problem is to minimize the parasitic inductance in this loop.
The other technique for mitigating this problem is to use rectifiers with low QRR.
In applications with high output voltages, like CCM PFC boost converters, SiC diodes are often used. Lower voltage applications like flybacks will often use schottky or ultra-fast diodes.
Even synchronous rectifiers will exhibit this problem, as the body diode of the synchronous FET will conduct during the dead time of the switching transition.

## Slide 13: Gate drives
VGATE
IGATE
Simplified PFC boost schematic
High di/dt in loop (yellow)
Stray inductance:
  Limits drive current
  Can cause ringing
Minimize loop inductance
High dv/dt on gate (blue)
Can couple to noise-sensitive nodes
Minimize capacitance
Identifying high di/dt
Notes: Yet another area where parasitic inductance can cause problems is in the gate drive path.
Here, a gate driver applies a square wave voltage across the gate the FET. During the turn on and turn off of the FET, large currents will occur in this path as the gate capacitance is charged and discharged.
Any inductance in this path limits the drive current and can cause ringing on the gate.

## Slide 14: Self inductance of PWB traces
Due to the natural logarithmic relationship, large changes in conductor width have minimal impact on inductance
W (mm/in) | T(mm/in) | Inductance (nH/cm or nH/in)
0.25/0.01 | 0.07/0.0028 | 10/24
2.5/0.1 | 0.07/0.0028 | 6/14
12.5/0.5 | 0.07/0.0028 | 2/6
Parasitic inductance
Notes: Now let’s look at how parasitic inductance is manifested in a PCB layout.
First, consider the self inductance of a PCB trace in free space.
An important note is that these equations are empirical, but are still good for large extremes of the variables. It provides a good rule of thumb of 6 nH per cm for a PCB trace or a wire in free space.
It is interesting to note that due to the natural log relationship, large changes in conductor width have minimal impact on inductance.
This shows that it is very difficult to reduce the inductance of an isolated trace.

## Slide 15: PWB traces over ground planes
Substantial inductance reduction
Inductance inversely proportional to width
Metric |  |  | English |  | 
h (cm) | w (cm) | Inductance (nH/cm) | h (in) | w (in) | Inductance (nH/in)
0.25 | 2.5 | 0.2 | 0.01 | 0.1 | 0.5
1.5 | 2.5 | 1.2 | 0.06 | 0.1 | 3.0
Parasitic inductance
Notes: Now let’s look at the impact of adding a ground plane.
The equations shown here are again empirical and are only good for large ratios of conductor trace widths to the separation from the ground plane.
Notice that the inductance is proportional to the spacing and inversely proportional to the conductor width. This means that there is much more control of the inductance compared to the isolated conductor.
Another important point, is that the inductance is proportional to the area enclosed by the conductors. This is true, even in the absence of a ground plane.
The significance of a ground plane can be seen by comparing the inductances shown here of 0.2 and 1.2 nH per cm with the 6 nH per cm self inductance of an isolated conductor on the previous slide.

## Slide 16
Low series inductance
High series inductance
How much inductance in series with C39? (total length ~ 2 cm)
Parasitic inductance
Notes: Now let’s put what have learned into practice.
Here, we are looking at the output filter of a power supply. You can see the output inductor L2, output capacitor C43 and output connector J1. What is wrong with this layout, and how can it be improved?
Pause
There is a fairly long etch run in series with the output capacitor and no ground plane underneath. This will lead to parasitic inductance in series with the output capacitor and limit its effectiveness at higher frequencies.
If the length of this etch is roughly 2cm, how much inductance is in series with the capacitor?
Pause
Using our 6nH per cm rule, this results in around 12 nH of parasitic inductance.
- Next animation -
The picture on the left shows a much better layout for the output filter. The inductor current flows past the output capacitors on the way to the connector. Using a ground plane underneath will help further reduce the parasitic inductance.

## Slide 17: Switched nodes
High dv/dt at switched node (blue):
Switched between 0V and VOUT
Stray capacitance can cause:
  EMI problems
  Noise injected to internal circuits
  Reduced efficiency
Mitigation:
Minimize VSW surface area
Keep sensitive etch and components away from VSW
Ground the heatsink!
VSW
The switched node paradox
Lower resistance
Increased surface area Lower inductance
Better cooling
Decreased surface area Lower capacitance
Simplified PFC boost schematic
Identifying high dv/dt
Notes: Now, we will investigate the third parasitic element – capacitance.
Parasitic capacitance on PCB etch with high dv/dt can create an EMI nightmare. It can also inject noise to internal circuitry, and even cause additional power loss.
Every switching power supply, by definition has at least one electrical node with a switching waveform. We often refer to these nodes as the “switched node”.
Here, in our PFC boost example, the switch node is at the junction of the inductor, FET, and diode.
To mitigate the effects of high dv/dt through the parasitic capacitance, we should try to minimize the surface area of the switched node, and keep noise sensitive etch and components away from the switched node etch.
It is also good practice to ground heat sinks to shunt stray currents back to ground.
- Next animation -
When laying out the power stage of a power supply, we often run into what I like to call the switched node paradox.
As we just said, we want to minimize the surface area of the etch in order to minimize the parasitic capacitance. However, we are at the same time incentivized to increase the surface area of this copper in order to reduce the resistance, lower the inductance and provide better cooling.
However, it is usually wise to choose smaller surface area for lower capacitance and find other ways to minimize resistance and inductance by shortening path lengths, and finding other ways to cool the devices.

## Slide 18: Sample capacitance calculation
Consider two 10 mil traces crossing with 10 mil PWB thickness
Not much capacitance but consider the area of all components connected to the feedback network
Parasitic capacitance
Notes: On this slide we will look at how parasitic capacitance is manifested on a PCB layout.
Capacitance is related to the permittivity, relative permittivity, area and thickness.
For typical PCB materials, the relative permittivity is around 5 F/m. The only variables the designer has control over are the area and spacing.
As shown here, two 10 mil traces crossing at 90 degrees results in very little capacitance. This is not usually where problems occur due to parasitic capacitance.
Issues tend to arise most commonly with planes, parallel conductors, or large pads on components.

## Slide 19: Chaos created by noise injection
Ten 0.05 x 0.02 in2 pads can increase parasitic capacitance to 2 pF
VSW
Cparasitic
Noise sensitive
Parasitic capacitance
Notes: Here we are looking at the example of a Quasi resonant flyback using the UCC28742.
There are two switched nodes in the flyback topology. One is connect to the drain of the primary FET. The other, highlighted in red in this example, is the drain of the synchronous rectifier, Q1.
One of the most noise sensitive areas in a power supply is the feedback and error amplifier, which are highlighted in green on this example.
Consider if these components were placed on an adjacent layer underneath the switched node. The ten 50mil by 20 mil pads would create 2pF of capacitance coupled to the switch node, injecting significant noise into one of your most sensitive circuits.
This is a great example of how important it is to completely understand your circuit and visualize how parasitic capacitance is manifested.

## Slide 20: At high frequency inductors turn into capacitors
Don’t route planes under common mode inductors!
Parasitic capacitance
Notes: Here we show the impedance of a common-mode inductor versus frequency. At low frequency, the impedance rises as expected, but at higher frequencies the inductor takes on a capacitive response. This is due to the internal winding to winding capacitance of the inductor.
This problem can be exasperated by a poor layout.
Consider if a ground plane were placed underneath the pads of the inductor, which have an area of 3 cm square. This creates a significant amount of capacitance from input to ground and then to output, and adds considerably to the 23pF of interwinding capacitance of the inductor.
For this reason ground planes should not extend underneath EMI filters.
High frequency, distributed capacitance and ur reduction

## Slide 21: Magnetic coupling
External fields couple between inductors
Can cause EMI issues
Consider alternate orientation of second inductor to minimize coupling
Use core shapes that provide better shielding
EMI considerations
Notes: In part one of this video series, we saw how parasitic capacitance due to routing a ground plane under an common mode filter inductor can decrease its effectiveness at higher frequencies.
This figure illustrates magnetic coupling between circuits. In this case, it is two toroidal inductors, but the same thing can happen with current loops in a PCB layout.
Because of the physical orientation, the flux lines generated by one inductor can induce currents in the other inductor.
This is yet another reason why it is critical to minimize loop area of switching currents.
To mitigate issues caused by magnetic coupling, filter inductors should be oriented such that the flux lines can not couple to the windings, or different core shapes can be used that provide better magnetic shielding.

## Slide 22: Input filter layout
Place components away from noise sources
Common mode inductor T2 input pins do not cross output pins
No GND plane under EMI filter
Wide, short etch used to minimize losses
Wide spacing between etches meets high-voltage requirements and minimizes coupling capacitance
EMI considerations
Notes: Here is a list of some tips when laying out an EMI input filter.
Don’t place components near noise sources
Avoid routing ground planes under the common mode choke
Be mindful of trace resistance
Adhere the applicable safety requirements for spacing between high voltage etches.

## Slide 23: Separate hazardous voltages from user accessible points
Consult your safety expert!
Create a very clear channel between primary and secondary
Spacing depends on:
  Type of insulation
  Pollution degree
  AC mains voltage
  Working voltage
Types of insulation:
  Functional
  Basic/supplementary
  Reinforced
Partial Clearance Dimensions (mm) from UL60950-1, Section 2.10.3, Table 2H
Safety
Notes: When it comes to safety in power supplies, we are primarily concerned with separating hazardous voltages from all user accessible points.
To accomplish this, we define two different spacing requirements, called creepage and clearance. A visual description of these two terms, as related to power supplies is shown here.
Clearance is the shortest path between two conductors through air. Creepage is the distance between two conductors along a surface. Techniques like barriers and air gaps can be used to increase clearance and creepage distances.
How much creepage and clearance spacing is needed for a particular application is dependent on many factors, like pollution degree, AC voltage, and working voltage. In addition, three different classes of insulation are defined: functional, basic/supplementary, and reinforced.
Saftey standards are complex and can vary by application, so a safety expert should always be consulted to ensure your layout has adequate spacing.

## Slide 24
  Ground planes provide:
    Low resistance return paths
    Low inductance return paths
    Lateral heat spreading across board
  General ground plane tips:
    Consider flooding empty areas with ground
    Avoid putting slots in GND planes
    Use jumpers on single layer boards to improve GND planes
    Place as much GND under the IC as possible

Ground planes
Notes: Ground planes are very beneficial to a power supply layout. They lower the resistance and inductance for ground currents.
They also serve as a heat spreader, allowing heat to transfer laterally through the board, reducing hot spots.
It usually good practice to flood empty areas with ground to make use of the empty space.
In multi layer boards, try to keep at least one internal layer as an unbroken ground plane, if possible.
In single layer boards, use wire jumpers to avoid cutting up the ground plane to much.
Flood ground under Ics as much as possible.

## Slide 25: Avoid coupling noise to sensitive nodes
Maximize the separation
  Move the source, reduce Cstray
Place capacitors and resistors near pins
Place GND vias near caps, resistors, and IC
Minimize the unfiltered track length
Good
Bad
VSW
VSW
Signal routing/placement
Notes: Placement of critical small signal components can be just as important as the layout of the power stage.
Consider the image shown here. This is the current sense signal from the PFC boost. It is filtered by Rf and Cf. If these components are placed far away from the pin of the IC as shown at left, noise from the switch node can capacitively couple into the signal.
By placing the components near the IC, the etch between Rf, Cf and the IC is shortened, reducing the parasitic capacitance. Additionally, ground vias should be placed near the ground pins of the IC and the ground connection of the capacitor to minimize inductive impedance on the ground connections.

## Slide 26
Data sheets normally contain
PCB layout guidelines
Signal routing/placement
Notes: Datasheets often contain useful guidelines for placement and routing of critical components and traces.
Many control IC’s recognize noisy/quiet circuit areas and pin out the IC accordingly
Some even provide separate pins for power and analog grounds
It is good design practice to plan the layout around the IC pin out, and keep high currents away from the noise sensitive components.

## Slide 27: PCB cooling strategy
Have solid ground planes to better spread heat across the layer
Avoid breaks in planes as they substantially degrade lateral heat flow
Use thermal vias to spread heat to other layers
Thermal pads help to get the heat out of the IC into the PCB
Use both sides of the board to cool
Maximize the thermal paths with partial pours wherever practical
DO NOT use switched node for cooling
Thermal management
Notes: It is also very important to consider how heat will flow from hot components through the board when you do the PCB layout.
Solid ground planes are very important to spread the heat across the layer and help the heat get out of components, including the IC.
The other thing that's important to include is thermal vias to spread the heat to other layers.
The image shown here highlights the flow of heat out of an IC.
Vias provide perpendicular conduction down to different layers, and then you have lateral conduction on the layers to spread the heat across the board.
Then the heat gets out of the board through convection and radiation.
Usually, in the data sheet, we include a recommended footprint with a thermal via pattern to get the best performance of the IC.

## Slide 28: Why is Board A hotter than Board B?
Traces on the bottom layer prevent heat from spreading effectively
Removing horizontal trace for a more solid bottom layer reduces IC temp on board B
Hottest component on B is the catch diode
TOP
BOTTOM
Board A
Board B
Max IC Temp: 86C
Max IC Temp: 66C
Max Temp: 62.6C
Max Temp: 52.2C
Thermal management
Notes: Now let’s see an example of proper and improper thermal management.
In these thermal images the same part is operating in a very similar layout in the same operating conditions.
Notice that on board A, the max temperature on the back of the board is 62.6 degrees C, where board B-- the max temperature on the back is 52.2 degrees C.
On the top side, the IC on board A is 22 degrees hotter than on board B.
So why is board A so much hotter than board B?
Remember the same part operating with the same operating conditions, and the only difference is the PCB layout.
--------- Pause ------------
-------- next animation --------------
Look very closely at board A, there is a trace cutting through the ground plane on the back of the board.
You can see this in the thermal image by the line that prevents the heat from spreading across the rest of the backside of the PCB.
So just adding this one trace on board A increases the operating temperature of the IC by 20 degrees C.
And actually, on board B, with a better layout, the Schottky diode is now the hottest component on the board. It's no longer the IC.

## Slide 29
Useful information:
  PCB size and (layers, layer spacing, material)
  Position of inlet and outlet connections
  Mechanical restraints (keep outs and height restrictions)
  Manufacturing process constraints
  Know the creepage and clearance requirements
Understand the circuit:
  High current paths
  High di/dt paths
  High dv/dt nodes
  Hot parts
Imagine a general ‘flow’
  Trunk packing algorithm
Gather information and place large components
DC out
AC in
UCC28710/UCC24610 PSR flyback with SR
PCB layout example
Notes: In this next section, we will walk through the typical process for laying out a power supply using a UCC28710 primary side regulated flyback with synchronous rectification as an example.
Assuming the schematic is complete, the first task is to gather all important information.
This includes:
Board size, shape and number of layers
What components need to be in fixed locations, like the input and output connectors
Are there any keep out areas or areas with restricted height?
What are your creepage and clearance requirements?
In addition to this, we’ll repeat it again, you must understand the circuit. Identify the
High current paths
High di/dt paths
High dv/dt nodes
Hot parts
Now, your ready to get started. Place all the larger components first. Imagine the flow of power and currents from input to output. Place components in the power stage such that loop inductance will be minimized on high di/dt paths, and switch node capacitance will be minimized. Reduce the length of high current paths.

## Slide 30
Place the large parts in the power path first
Reserve a ‘quiet’ location for the controller
  NOT under transformer or node with high dv/dt
  Place its associated parts nearby
Reserve an area for the input filter
  Keep filter input away from output
  Rotate, reposition, reassign pins, repeat
PWM controller
SR controller
Place remaining components
UCC28710/UCC24610 PSR flyback with SR
PCB layout example
Notes: Next finish placing any remaining power path components.
Followed by ICs, like the primary controller and the UCC24610 synchronous rectifier driver in this example. Make sure to put the controller in a quiet location, not under the transformer.
Then place the smaller components like resistors, capacitors, and small signal diodes and transistors.
Inevitably, you will need to shuffle some parts around in the process.

## Slide 31
Two layers:
  Bottom layer (red)
  Top layer (blue)
Route power path first
  Use wide etch and polygon pours
  Minimize high di/dt loop area
  Minimize high dv/dt surface area
Route signal etch last
  Keep away from high dv/dt nodes
  Keep noise sensitive etch short
  Shorten return paths
Input loop
Output loop
Route power and signal etch
UCC28710/UCC24610 PSR flyback with SR
PCB layout example
Notes: Now you are ready to start routing. In this picture, the top layer is shown in blue, and the bottom layer is shown in red.
Start by routing the power path.
Use wide etch for the higher current paths, like the output and return.
Minimize the copper tied to the switch nodes, both on the secondary and the primary.
Minimize loop area for the high di/dt paths. The high di/dt path on the primary is shown in yellow. The high di/dt path on the secondary is shown in red.
Next, route the signal etch. Keep them away from the switched nodes where high dv/dt is present, and keep noise sensitive etch runs short.

## Slide 32
Flood empty areas:
  Primary GND
  Secondary GND
Use vias to connect to GND planes
  Near caps/resistors
  Near GND pins of ICs
Check for blocked GND connections
  Move parts/etch as necessary
  Be mindful of parasitic resistance and inductance
Flood highlighted areas with GND
Pour ground planes
UCC28710/UCC24610 PSR flyback with SR
PCB layout example
Notes: The final step is to pour the ground planes.
Flood empty areas with ground. In this example, there are two grounds: one on the secondary and one on the primary.
Place ground vias near the ICs and critical components to minimize inductance on the ground paths.
Check the ground pours for blockages, and move etch and parts around to help clear ground paths as necessary.
Finally, get a buddy to review your work and revise as necessary.

## Slide 33
Understand your circuit: high current and di/dt paths, high dv/dt nodes
Understand how parasitic resistance, inductance, and capacitance are manifested
Understand how layout can significantly affect EMI
Understand the safety requirements for your product
Understand how heat is transferred through the PCB
Follow a logical procedure:
  Place large parts, place small parts, power routing, signal routing, pour planes
Have someone review your layout!
Summary: keys to a successful SMPS layout
Notes: In summary, we have discussed some the key things to consider when laying out your power supply.
It is critical that you must understand how your circuit operates, and where high current, di/dt and dv/dt are present.
You must now how the three parasitic elements, resistance, inductance, and capacitance are manifested so that you can mitigate them.
You must now how placement of your components and routing will affect EMI.
Know the safety requirements for your application before beginning the layout.
Understand how heat flows through a PCB.
A good procedure for layout begins by placing large parts, then smaller parts, routing the power paths, then the signal etchs, and finally pouring the ground planes.

## Slide 34
Constructing Your Power Supply - Layout Considerations; R. Kollman; 2004 TI Power Supply Design Seminar; www.ti.com/seclit/ml/slup230/slup230.pdf
Safety Considerations in Power Supply Design; B. Mammano and L. Bahra; 2004 TI Power Supply Design Seminar; www.ti.com/seclit/ml/slup227/slup227.pdf
Common Mistakes in DC/DC Converters and How to Fix Them; P. Shenoy and A. Fagnani; 2018 TI Power Supply Design Seminar; www.ti.com/seclit/ml/slup384/slup384.pdf
Grounding in Mixed-Signal Systems Demystified, Part 1 & Part 2; S. Pithadia and S. More; 1Q 2013, TI Analog Applications Journal; www.ti.com/lit/an/slyt499/slyt499.pdf; www.ti.com/lit/an/slyt512/slyt512.pdf
Why Should You Count Squares; Brigitte; 2016 TI Power House Blog; http://e2e.ti.com/blogs_/b/powerhouse/archive/2016/10/03/why-should-i-count-squares
Summary: references
Notes: Texas Instruments offers numerous resources for layout guidance. Some of the references used to generate this video are available on the TI website at the addresses shown here.

## Slide 35: Thank you
HVS content available for download at: www.ti.com/highvolt

## Slide 36
©2021 Texas Instruments Incorporated. All rights reserved.
SLYP762