## Slide 2: What will I get out of this session?
Brief Description of Silicon Carbide performance
Different short circuit current sensing and protection methods
How to turn off MOSFET under short circuit safely
Other diagnostics available to assist in ASIL designs
Relevant part numbers:
  UCC587x-Q1
  UCC2152x
Relevant reference designs:
  TIDA-01605
  TIDA-00917
Relevant applications:
  HEV/EV traction inverter, EV on-board charger
2

## Slide 3: Power transistor application positioning
3
EV charger: 3.3 kW-22 kW
Traction inverter: 15 kW-400 kW

## Slide 4: SiC MOSFET advantages over Si IGBT: conduction
1) No 0.5-1.0V knee voltage; 2) Has “body diode”; 3) 3rd quadrant operation mode
4
Q1 current

## Slide 5: SiC MOSFET advantages over Si IGBT: switching
Low switching loss:
MOSFET (unipolar) vs IGBT (bipolar)- fundamental difference
Switch loss less increase at elevated temperatures:
For 1000V SiC MOSFET, Esw@25˚C = Esw@150˚C
Low reverse recovery for the body diode:
Silicon PiN diode has significant reverse recovery which has reverse recovery loss and also adds more turn on loss
5
Typical switching waveforms

## Slide 6: Traction motor: system failure mitigation
X
Potential failure
TI’s isolated gate driver
Failure mode | Possible prevention
Motor Coil Shorted/Open | Monitor Current through FET , Shut off Power
FET Short/Open/Damaged | Monitor Current through FET, Monitor Gate-Source, Shut off Power
Motor Driver Damaged | Monitor Internal signals, Implement Self Test, Disallow operation
MCU Failure | Watchdog on Motor driver or PMIC , Reset MCU if WD fails
PMIC failure | Watchdog on Motor Driver. Reset MCU if MCU Browns Out
Incorrect IC configuration | Checksum on configuration setups
MCU Brownout | Monitor PMIC supply independently, Reset MCU for brownout
Motor Driver Logic Incorrect | Monitor Gate driver logic voltages, Self test of Gate driver

## Slide 7: Overcurrent protection

## Slide 8: Overcurrent/short circuit fault
Short circuit happens at t1
ΔVgs
ΔVds
8

## Slide 9: Overcurrent/short circuit fault mechanism: thermal limitation
IGBT self-limits the current increase with lower saturation current
  Shape transient from saturation region to active region, collector current is limited to a constant value in active region
SiC MOSFET has large linear region with high saturation current
  In the case of SiC, Id continues to increase with increase in Vds, eventually resulting in faster breakdown
For same rated current & voltage, IGBT reaches active region for significantly lower VCE as compared to SiC MOSFET
IGBT
SiC MOSFET
9

## Slide 10: Overcurrent/short circuit fault mechanism: thermal limitation
The short circuit withstand time, tsc, is determined by the critical energy
  Minimal dissipated energy leading to device failure for one short circuit pulse
  Vds is the DC link voltage, Id will be the device saturation current.
SiC MOSFET short circuit withstand time is shorter than IGBT due to smaller chip size, less thermal capacity
Vds:
100V/div
Ids:
50A/div
Vgs:
10V/div
Tsc:2.5µs
10

## Slide 11: Overcurrent/short circuit protection method: DESAT
  Desaturation circuit detects the Vds of MOSFET or Vce of IGBT, protection is triggered when detected voltage is above pre-set reference voltage
  Blanking time is needed to prevent false trigger during switching turn on transients
  DESAT threshold voltage varies between different devices due to the output characteristics, especially IGBT and SiC MOSFET
  Most common method for SiC where the IR drop is measured for current sense
Vdesat
11

## Slide 12: Overcurrent/short circuit protection method: SenseFET / current mirror
  SenseFET / current mirror is used to scale down main current, tens of mV voltage is measured on sense resistor
  Advantages
    Fastest protection speed
    Accurate for both AC and DC
  Challenges of SenseFET / current mirror
    Module needs to be customized to integrate SenseFET / current mirror
    Higher cost
    Not currently available in SiC modules
12

## Slide 13: Overcurrent/short circuit protection method: shunt resistor
  Advantages
    Accurate for both AC and DC
    Fast protection speed
    Low cost
  Challenges of shunt resistor
    High power loss in high power applications
    Weak noise immunity due to gate loop noise caused by parasitic inductance of shunt resistor and PCB trace
13

## Slide 14: Overcurrent/short circuit safe turn-off: avalanche limitation
Vds:
100V/div
Ids:
50A/div
Vgs:
10V/div
Tsc:2.5us
Voltage and avalanche limit: device avalanche can be caused by the overshoot voltage on Vds
Id
ΔVgs
+
-
+
-
ΔVds
ΔVds
ΔVds
14

## Slide 15: SiC MOSFET protection: soft turn-off (STO) & 2L turn-off
There are parasitic inductances in the power loop
Parasitic inductances together with di/dt cause voltage spikes
The di/dt rate is much higher under short circuit fault so a preventive turn-off measure needs to be taken in order to limit the loop inductance induced voltage spike
Effectively, there are two ways to slow down the turn-off process: reduce di or extend dt
15

## Slide 16: DESAT Timing
Gate Driver Parameters
  tLEB
  VDESAT
  ICHG
  tDSOFF
  ISTO
  Determined by the blanking capacitor CBLK
tSTO
(1) Detection time
(2) Shutdown time

## Slide 17: Short-circuit protection: hardware validation
Evaluation hardware
Isolated Power Supplies
DC Bus Caps
IGBT Half-bridge Module
Isolated Half-bridge Drive Stage
using ISO5852S-Q1 + 15A Buffer Driver
IGBT
Half-bridge Module
(FF450R12KT4)
High-side
Isolated Driver
(Up to ±15A)
Low-side
Isolated Driver
(Up to ±15A)
Schematic for double-pulse test setup
TOP
BOTTOM
17

## Slide 18: SC protection response time
VSC_PIN
FLT
VOUT
UCC5870-Q1 Response to SC event is 255ns
UCC5870-Q1
The response time incorporates any deglitch and propagation delays in the device
DESAT and OC features are designed to support SiC requirements, which also covers IGBT applications

## Slide 19: DESAT with Safe Shutdown: 2LTO
Programmable ISTO optimizes for the trade-off between shutdown energy and VCE overshoot for IGBTs/MOSFETs
PARAMETER | MEASURED VALUE
Shutdown Energy | 1.58J
VCE Overshoot | 140V
Soft Turn-off (STO): ISTO=0.3A, V2LOFF=9V, t2LOFF=1.0us
PARAMETER | MEASURED VALUE
Soft Turn Off Current | 1.68J
VCE Overshoot | 132V
Soft Turn-off (STO): ISTO=0.3A, V2LOFF=10V, t2LOFF=1.0us
ICE (1kA/div)
VGE (5V/div)
Time: 1us/div
VCE (200V/div)
ICEpeak ~ 3080A
∆V ~ 132V
Vdesat (5V/div)
ICE (1kA/div)
VGE (5V/div)
VCE (200V/div)
ICEpeak ~ 3080A
∆V ~ 140V
Vdesat (5V/div)
Time: 1us/div
UCC5870-Q1 Response

## Slide 20: DESAT Response with Safe Shutdown: STO
Programmable ISTO optimizes for the trade-off between shutdown energy and VCE overshoot for IGBTs/MOSFETs
PARAMETER | MEASURED VALUE
Shutdown Energy | 1.01J
VCE Overshoot | 248V
Soft Turn-off (STO): ISTO=0.6A, VDESAT_th=9V
PARAMETER | MEASURED VALUE
Shutdown Energy | 2.04J
VCE Overshoot | 148V
Soft Turn-off (STO): ISTO=0.3A, VDESAT_th=9V
ICE (1kA/div)
VGE (10V/div)
VCE (200V/div)
ICEpeak ~ 4340A
∆V ~ 248V
Vdesat (5V/div)
Time: 1us/div
ICE (1kA/div)
VGE (10V/div)
Time: 1us/div
VCE (200V/div)
ICEpeak ~ 4340A
∆V ~ 148V
Vdesat (5V/div)
UCC5870-Q1 Response

## Slide 21: SiC with UCC21750: Soft turn-off, VDC=800 V
Overcurrent fault test circuit
IN+ gives a long pulse to create Id ramp
DESAT detects the fault and takes action
Soft turn-off (STO): UCC21750
2µs/div
VGS (10V/div)
DESAT (5V/div)
VDS (200V/div)
IDS (100A/div)
t1 = ~600ns
∆V ~ 120V
IDpeak ~ 420A
PARAMETER | MEASURED VALUE
Shutdown Energy | ~0.1J
VDS Overshoot | 120V
With the same soft turn-off characteristics, the only difference in shutdown between the UCC21750 and UCC21750 will be the detection timing
UCC217xx Response
Notes: Programmable VOCTH
Propose value ofr VOCTH

## Slide 22: SiC with UCC21750: Soft turn-off, VDC=800 V
Short circuit fault test circuit
IN+ gives a long pulse to create Id ramp
DESAT detects the fault and takes action
Soft turn-off (STO): UCC21750
PARAMETER | MEASURED VALUE
Shutdown Energy | 0.24J
VDS Overshoot | 80V
VDS (200V/div)
VGS (20V/div)
DESAT (5V/div)
ID (500A/div)
1us/div
∆V ~ 80V
IDpeak ~ 1000A
t1 = 600ns
With the same soft turn-off characteristics, the only difference in shutdown between the UCC21750 and UCC21750 will be the detection timing
UCC217xx Response
Notes: Programmable VOCTH
Propose value ofr VOCTH

## Slide 23: DESAT using OC
Gate Driver Parameters
  VOCTH
  ICHG
  tOCOFF
  ISTO
f
tSTO
(1) Detection time
(2) Shutdown time
tOC_T

## Slide 24: Short circuit protection for SiC MOSFETs: with or without soft turn-off
Hard turn-off
Soft turn-off for hard SC
Soft turn-off for SC under load
VDS(100V/div), IC(1kA/div),
VGS(10V/div), VDESAT(5V/div)
VDS(100V/div), IC(1kA/div),
VGS(10V/div), VDESAT(5V/div)
VDS(100V/div), IC(1kA/div),
VGS(10V/div)
24
UCC217xx Response

## Slide 25: OC pin waveform
Normal switching
IDS (100A/div)
VDS (100V/div)
VGS (6V/div)
VOC: 1V/div
IDS (100A/div)
VDS (100V/div)
VGS (6V/div)
VOC: 1V/div
Soft turn-off after OC protection
This noise must be less than the threshold
UCC5870-Q1 response
IDS (500A/div)
VDS (100V/div)
VGS (6V/div)
VOC: 1V/div
Soft turn-off after SC protection

## Slide 26: Additional protection features

## Slide 27: Over and undervoltage lockout: adjustability
Measurements & specifications
System benefits
Flexible Supply Monitoring Across Platforms : Programmable OVLO and UVLO thresholds for primary and secondary supplies
Adjustable to Fit Power Switch Requirements: Monitor supply voltage to protect IGBT and SiC MOSFETs from undue stress
Gather Important Feedback: Configurable fault outputs nFLT1 and nFLT2 to report various faults and warnings
Supply | UVLO Options | OVLO Options
VCC1 | 3.3V, 5V | 3.3V, 5V
VCC2 | 16V, 14V, 12V, 10V | 23V, 21V, 19V, 17V
VEE2 | -3V, -5V, -8V, -10V | -5V, -7V, -10V, -12V
Thresholds can be optimized based on gate voltage of power switch!
IGBT vs. SiC MOSFET I-V characteristics vary with respect to gate drive voltage (VCC2) and conduction loss
Maintains VCC2 level to reduce conduction loss and protect power switch
Monitors VCC1 drop indicating system failure
Monitors VEE2 to indicate system failure and prevent undesirable effects

## Slide 28: VCE clamp: flexibility, protection
Measurements & specifications
System benefits
System Flexibility: Option between 3 communication modes (address-based, daisy-chain, regular SPI)
Ease of System Programmability: Simplify design time and engineering effort
Address-based SPI: Only requires 4 I/O pins and provides 6x shorter response time compared to daisy chain configuration
UCC5870-Q1 VCE Clamp Characteristics |  | Typ. Value
VCE Clamp Threshold | VCECLPTH | 2.2 V
VCE Clamp Threshold Hysteresis | VCECLPHYS | 200 mV
VCE Clamping Intervention Time | tVCECLP | 20 ns
VCE Clamping Hold Time | tVCECLP_HLD | Adjustable
High voltage clamping only active for a short time to prevent shoot-through |  | 

## Slide 29: Gate voltage monitoring: flexibility, protection
Measurements & specifications
System benefits
Enhanced System Safety: Ensure output follows the driver input as high or low to detect a system failure such as open resistor at gate or gate short
Real-Time Fault Monitoring: Dedicated fault output to feed information back to MCU
Size Reduction: Removes external components to monitor driver output voltage
UCC5870-Q1 Gate Voltage Monitor Characteristics | Typ. Value
Gate Voltage Monitor Threshold Value (reference to VCC2) | -3 V
Gate Voltage Monitor Threshold Value (reference to VEE2) | 3 V
Blanking Time (Programmable) | 500-4000 ns
Deglitch Time | 250 ns
Fault can be reported to nFLT1 or nFLT2, or report to state to nFLT2 | 
VBST voltage drop triggers Gate Voltage Monitor Fault
When Gate Voltage Monitor Fault is detected, the output is turned off
IN+
VGE
FLT
VBST
OUTL
OUTH
VGE

## Slide 30: Motor controller interface: flexibility, protection
Measurements & specifications
System benefits
System Flexibility: Supports 100% duty cycle operation (min 250ns input pulse, 30 kHz max frequency with ADC)
Shoot-through Protection: Interlocking with two drivers prevents shoot-through with programmable dead time and fault reporting
Noise Immunity: Minimum pulse width rejection on IN+ and IN-
100% Duty Cycle possible with integrated charge pump
Programmable dead time: 0ns, 105ns, 175ns…up to 4445ns in increments of 70ns
Noise rejection chosen based on programming input pulse width rejection ranging from 0ns to 210ns
OUT
IN+
IN-
STP Fault
Shoot-through prevented and STP Fault triggered

## Slide 31: Active Miller Clamp
[Disclaimer: Specs, features & pinouts subject to change without prior notice.]
Internal Miller Clamp
External Miller Clamp
Miller Clamp inside IC
5A peak pull-down current
Adjustable VCLMPTH (1.5V, 2V, 3V, or 4V)
Suitable for close connection of CLAMP pin to gate terminal of power switch
System challenges when connection from CLAMP pin to Gate terminal of power switch is too long (high inductance)
Miller Clamp outside IC: Discrete Si MOSFET switch
Flexible peak pull-down current + 5V signal w.r.t. VEE2 @ CLAMP pin
Adjustable VCLMPTH (1.5V, 2V, 3V, or 4V)
Suitable when CLAMP pin is far away from gate terminal of power switch
    Low inductance from clamp to gate terminal of power switch
Better technique for power module implementation
Notes: Programmable VOCTH
Propose value ofr VOCTH

## Slide 32: Active Miller Clamping
IDS (100A/div)
VDS (100V/div)
VGS (5V/div)
ON
As the SW node rapidly changes, coupling can turn on the External power FETs through the parasitic coupling
Miller clamp kicks in an pulls the gate to VEE with a low impedance path
Notes: Programmable VOCTH
Propose value ofr VOCTH

## Slide 33: 6-channel ADC: accuracy, integration, low noise
Measurements & specifications
System benefits
System Flexibility: Variety of configurations to measure temperature, current, or voltage
Higher Accuracy: Integrated 10-bit ADC and internal OR external VREF
System Cost/Size Reduction: Save ~$0.37 per channel by eliminating external ADC
ADC | MIN | TYP | MAX
Input Voltage Range (A1 to A6) | 0V | 3.6V | 3.636V
VREF (V) |  | 4 | 
INL, external ref (LSB) | -1.2 |  | 1.2
DNL (LSB) | -0.75 |  | 0.75
External ADC Reference Turn-On Delay (us) | 10 |  | 
NTC bias current (prog range, uA) | 100 |  | 1000
VAI* (V)
Total Channel Error (LSB)
-40C
25C
150C
VAI* (V)
Total Channel Error (LSB)
Precision reference can measure AI* to within +1/-2 LSB (+3.5/-7 mV)
Notes: System Flexibility: Variety of configurations to measure temperature, current, or voltage
Higher Accuracy: Integrated 10-bit ADC and internal OR external VREF
System Cost Reduction: Save ~$0.XX by eliminating external ADC
PCB Area Reduction: Reduce PCB Area by ~XXmm2
Reduced Noise Coupling: Sampling sequencing reads data at switching center
Configurable for Active Short Circuit (ASC)

## Slide 34: 6-channel ADC: use cases
Isolated switch temperature sensing: NTC/PTC/diode
Redundant Bus voltage measurement
Power switch junction temperature monitoring
Power switch over-temperature configurable warning and shut-down
Option for internal or external VREF to improve accuracy
HV Bus Sensing
Monitor DC link voltage
Referenced to low-side driver common
Example using thermal diode + external VREF
HV VCE Sensing
Monitor if phase open or closed
Option to reference to high-side or low-side common
VCE voltage measurement
Example using thermal diode + internal VREF
Notes: Programmable VOCTH
Propose value ofr VOCTH

## Slide 35: 6-channel ADC: sampling modes
Configuring ADC modes
Three modes available to ensure least amount of switching noise
Center sampling mode: samples in middle of switching cycle
Edge sampling mode: samples at start or end of each switching cycle
Hybrid sampling mode: samples mode samples in the center until a cycle is significantly longer then the one before it
Center sampling mode
Hybrid mode
IN+
Edge sampling mode
Notes: Programmable VOCTH
Propose value ofr VOCTH

## Slide 36: Power Switch VGTH Monitor: System Reliability
Measurements & Specifications
System Benefits
Integrated Health Monitor: Gate driver used to perform threshold voltage measurements over system lifetime
Help System Anticipate Failure: Works with MCU to provide critical power switch data
ΔVGTH is a precursor to IGBT failure
Click here to see more information about lifetime degradation of IGBT from Syed Huzaif Ali’s paper at IEEE
Early warning
TI Unique Feature
Operation of VGTH monitor and timing diagram
ADC measurement
VGATE
nFLT1
SCLK
DESAT
VGTH is accurate measure of health of external power switch
Test done with Cree SiC MOSFET C3M0065100K with voltage threshold of 1.8-3V

## Slide 37: Built-in self-test (BIST): enhanced reliability
Example & benefits
System and On-Demand Diagnostics: Ensures operation of critical driver functions at power up and on-demand using SPI programming
Enables Easier ASIL-D Implementation: Integrated diagnostics to support system-level functional safety requirements
BIST (built-in self test) mechanisms | 
UV/OV Comparators of Internal Regulator | Automatic on Power Up (Latent Fail Check)
UV/OV Comparators (VCC1, VCC2, VEE2) | Automatic on Power Up (Latent Fail Check)
Main Clock | Automatic on Power Up (Latent Fail Check)
Comparator for Thermal Shutdown | Automatic on Power Up (Latent Fail Check)
DESAT diagnostic | On-Demand (with SPI Command)
OCP, SCP and OTP comparator diagnostics | On-Demand (with SPI Command)
VCE clamping detection diagnostics | On-Demand (with SPI Command)
Gate Monitoring | On-Demand (with SPI Command)
CRC | On-Demand (with SPI Command)
SPI command sent to check VCE Clamp and fault reported showing functioning detection mechanism

## Slide 38: Other diagnostics and protection: reliability and flexibility
Measurements & specifications
System benefits
Data Protection: CRC (cyclic redundancy check) protects various registers against faulty data transmission when in the Active State
Communication Protection: CRC checks for SPI transfer are continuously updated as SPI data is sent/received
Flexible Feedback: Configurable fault outputs nFLT1 and nFLT2 to report various faults and warnings
Configuration Data CRC Check Timing
When the driver is in the ACTIVE state, the configuration and control registers are protected by the CRC engine (this can be disabled)
An error can be induced on the primary or secondary side
CRC checks on SPI transfers are continuously updated as traffic is sent/received and is updated with every 16-bits that are received
See the datasheet Detailed Description section for more information

## Slide 39
©2021 Texas Instruments Incorporated. All rights reserved.
SLYP764