## Slide 1: TI INDIA AUTOMOTIVE SEMINAR
LEANNE ZHANG, BOB MA
AUTOMOTIVE USB CHARGER CHALLENGES AND INNOVATIONS

## Slide 2
Contents
01
Automotive USB design challenges
Excellent thermals confronting a warm environment
02
Small solution size
03
Compatibility for different charging schemes
04
EMI optimization
05
How to choose: automotive USB products
06

## Slide 3
Contents
Excellent thermals confronting a warm environment
02
Small solution size
03
Compatibility for different charging schemes
04
EMI optimization
05
How to choose: automotive USB products
06
01
Automotive USB design challenges

## Slide 4: Automotive USB design challenges
Charging circuit thermal
50mm
40mm
100W with USB PD
5W
…
7.5W
12W
15W
Compatibility for max power charging
00
Small model, No airflow
Electromagnetic Compatibility EMC
Higher power density

## Slide 5
Contents
01
Automotive USB design challenge
Excellent thermals confronting a warm environment
02
Small solution size
03
Compatibility for different charging schemes
04
How to choose: automotive USB products
06
EMI optimization
05

## Slide 6
Excellent thermals confronting a warm environment
02
NTC smart thermal management
b.
a.
HotRodTM package contributes die heat dissipation
Good thermals with high efficiency
c.
Real-life thermal test results
d.

## Slide 7: Achieving good thermals with VQFN-HR
Good heat conduction through pin, wide copper planes
Thermal path for HotRod™
Flipped die on lead frame (HotRod™)
Thermal design for these packages
    Large pads connected to power devices are essential to distribute heat.
    Most of heat is through large pads because of metal routing but pins can also distribute heat
        PGND, GND, SW: most effective
~98%
<2%
~98%

## Slide 8: Innovation in packaging: VQFN-HR
Wirebond Cross Section
HR Cross Section
Notes: 传统封装技术是以bonding线的形式将die和Leadframe相连；FCOL（Flip Chip on Lead）- SOT封装技术则是将晶片倒扣，通过铜柱将die和Leadframe相连。
Bonding线的寄生电感和寄生电阻都比较大。FCOL - SOT技术则采用直径较大的通路避免了的寄生电感在开关节点上产生较大的振铃（Ring），从而避免开关管被击穿。同时减小寄生电感和寄生电阻的损耗，避免影响效率或产生热量。相似技术在FCOL – HotRod™ QFN封装中也有应用。

## Slide 9: Smart thermal management and load shedding
Phase | Description
Phase 1 | Normal operation; Charge at full load
Phase 2 | Temp Warm: Broad 1.5A type-C, reduce the current by half
Phase 3 | Temp Hot: Broad Default USB mode; Reduce the BUS voltage to 4.77V
Phase 4 | TDie rise to max Tj:Thermal shut down
ICHG
(/Port)
Max Tj
(165°C)
T2(Hot)
T1(Warm)
Phase 1
Phase 2
Phase 3
3A
TNTC
Phase 4
Customized
Customized
1.5A
VBUS
5.1V
4.77V
0.5/0.9A
VBUS
Charge Current

## Slide 10: Smart thermal management and load shedding
Temp Warm(T1)
VTS ➜ >50%
VTS ➜ >65%
Type-C Broad 1.5A @ CC1/2
Type-C Broad 0.5A @ CC1/2
SENSE voltage drop to 4.77V
Temp Hot(T2)
VCC1
(Type-C broad current)
VSENSE/BUS

## Slide 11: Good thermals with high efficiency
TPS25858-Q1
FSW = 400 kHz
Competitor
FSW = 400 kHz
95.4%
92.5%
Efficiency
I (A)
TPS25850-Q1
FSW = 2.2MHz
93.5%
Competitor
FSW = 2.2MHz
OTSD – Doesn’t support 6A.
Efficiency
I (A)
N/A

## Slide 12: TPS25850-Q1 thermal @2S2Pboard, 2 MHz
VIN=8V
PA=3A, PB=3A
Temp rise: 49.5°C
VIN=12V
PA=3A, PB=3A
Temp rise: 55°C
VIN=16V
PA=3A, PB=3A
Temp rise: 63.4°C
= 2.2MHz, VIN = 12V, TA = 25°C, Charge Current = 2*3A
As = 85°C, = 55°C
= +
= 85°C+ 55°C = 140°C, < 150°C (recommended max )
Support full load at 85°C ambient:

## Slide 13: TPS25858-Q1 thermal @2S2Pboard, 400 kHz
Temp rise: 32.4°C
Temp rise: 32.9°C
Temp rise: 34.2°C
VIN=8V
PA=3A, PB=3A
VIN=12V
PA=3A, PB=3A
VIN=16V
PA=3A, PB=3A
= 2.2MHz, VIN = 12V, TA = 25°C, Charge Current = 2*3A
As = 85°C, = 33°C
= +
= 85°C+ 33°C = 118°C, < 150°C (recommended max )
Support full load at 85°C ambient:

## Slide 14: TPS25858 thermal on compact board
TPS25858-Q1
VIN=12V, IBUS=2*3A
Max Temp = 68°C
Trise = 43°C
Competitor
VIN=12V, IBUS=2*3A
Max Temp = 88.7°C
Trise = 63.7°C
Competitor
EVM
TPS25858-Q1
EVM
50mm*50mm
45mm*45mm
Board size: 20% smaller
Board temp: 20°C cooler

## Slide 15
Contents
Small solution size
03
Compatibility for different charging schemes
04
01
Automotive USB design challenge
Excellent thermal confronting warm environment
02
EMI optimization
05
How to choose: automotive USB products
06

## Slide 16
Small solution size
03
a.
Small package size with HotRod™
High integration assists small solution size
b.
2MHz operation enable smallest solution size
c.

## Slide 17: TPS2585x small package size
TPS25850/8-Q1
3.5mm
4.5mm
TI’s smallest package size for dual USB-C charging
Benefits from HR package:
  High power density
  Good theta JA
  Low parasitic compare to bounding wire improve EMI
EMI friendly pinout
TPS25850/8-Q1
3.5mm x 4.5mm
Competitor 1
5.0mm x 3.5mm
Competitor 2
5.0mm x 5.0mm

## Slide 18: High integration, small solution size: PMP40731
35 mm
35 mm
15W
15W

## Slide 19: Operating frequency () setting: 400 kHz ~2.2 MHz
Recommended operating frequency
for TPS25850-Q1
2.2MHz
2MHz
450kHz
350kHz
Recommended operating frequency
for TPS25858-Q1
AM radio bands
49.9kΩ
8.45kΩ
400kHz
2.2MHz
Adjustable by selecting the correct

## Slide 20: Remarkable performance at 2.1-MHz operation
400 KHz operating, VIN=12 V, PA=3 A, PB=3 A
2.1 MHz operating, VIN=12 V, PA=3 A, PB=3 A

## Slide 21: 2-MHz operation enables smallest solution size
33 mm
24 mm
Inductor 0.68
6.8 mm * 6.4 mm
Input cap
3 * 10 + 0.1
Output cap (SENSE pin)
3 * 22
TPS25850-Q1
2MHz vs 400KHz comparison |  |  | 
Device |  | TPS25850 | TPS25858
 |  | 2.1MHz | 400KHz
BOM | Inductor | 0.68uH | 3.3uH
 | Cout | 3*22uF | 3*47uF or 10uF+10uF+330uF
 | Summary | - | L& C cost higher
Solution size | IC | 25mm² | 25mm²
 | Inductor | 43.5mm² | 168.96mm²
 | Capacitors | 121.28mm² | 152.16mm²
 | Others |  | 
 | Total | ~190mm² (~45%↓) | ~346mm²
2MHz vs 400KHz comparison |  |  | 
Device |  | TPS25850 | TPS25858
 |  | 2.1MHz | 400KHz
BOM | Inductor | 0.68uH | 3.3uH
 | Cout | 3*22uF | 3*47uF or 10uF+10uF+330uF
 | Summary | - | L& C cost higher
Solution size | IC | 25mm² | 25mm²
 | Inductor | 43.5mm² | 168.96mm²
 | Capacitors | 121.28mm² | 152.16mm²
 | Others |  | 
 | Total | ~190mm² (~45%↓) | ~346mm²

## Slide 22
Contents
Small solution size
03
Compatibility for different charging schemes
04
01
Automotive USB design challenge
Excellent thermal confronting warm environment
02
EMI optimization
05
How to choose: automotive USB products
06

## Slide 23
Compatibility
for different charging schemes
04
a.
USB BC1.2 overview
Apple® /Samsung® charging
b.
USB Type-CTM charging
c.

## Slide 24: USB battery charging 1.2
  BC 1.2 defines the type of charger, handshaking, allowable current draws, and PD decision-making flowchart that defines the interaction between PD and host charger.
BC1.2 Port Type | Definition | 5V Current Capability | Comments
Standard Downstream Port (SDP) | Compliant USB 2.0 port. No special charging capability | 100 mA until authenticated by USB controller, then 500 mA. (USB port controller handles this authentication – NOT the USB power switch.) | Most USB 2.0 ports provide 1A or more, but there is no absolute way for a USB2.0 client to know this. Most devices just assume the power is there and draw what they need.
Dedicated Charging Port (DCP) | Wall wart charger. No data communication capability | Up to 1.5 A current | Wall wart chargers don’t have a USB data transceiver or controller, but will need a small amount of handshaking, as defined by the BC1.2 standard, to let the client know “for sure” up to 1.5A of current is available.
Charging Downstream Port (CDP) | A USB 2.0 compliant port with intelligent charging capability | Up to 500 mA current if authenticated as SDP or up to 1.5 A current if authenticated as CDP. | CDPs can vary the amount of current available based on their power. For example, a notebook PC may limit power draw to 500mA on battery power (by responding to the PD as a SDP) – or allow 1.5A of draw when the AC adapter is present (by authenticating as a CDP). Data communications is allowed following the handshake as a CDP.

## Slide 25: Different charging schemes
Apple ® iPhone®
BC 1.2
Samsung®
2.7V
Apple ® iPad®

## Slide 26
USB Type-C channel configuration Simple way to accommodate flippable, symmetrical & reversible cable
Simple resistor divider network between host and device
DFP pulls up the CC pin with Rp
UFP pulls down the CC pin with Rd
DRD/P alternates between DFP and UFP
One CC wire in the cable
DFP(UFP) can detect attachment of UFP (DFP) if active CC line has a Rd (Rp) on the other side
DFP/UFP can detect plug orientation by monitoring which CC line is active
DFP uses different Rp (or current source) values to advertise its current provider capability. USB default, 1.5A or 3A
Data and power roles
By default DFP (host) is a power source and UFP (device) is a power sink
USB PD can be used to change these roles
VCONN power
DFP provides VCONN power (1W minimum) at the unused CC pin for electronics inside cable
Cable installs pull-down resistor Ra to request VCONN power
Type-C Data roles:
Downstream facing Port (DFP) - Host
Upstream facing Port (UFP) - Device
Dual-role port (dual-role data DRD and dual-role power DRP) switch between DFP and UFP
Type-C power roles:
Source - a provider of power when connected
Sink - a consumer of power when connected
Note only one CC wire through cable
DFP monitors for connection and orientation
UFP monitors for connection, orientation, and current

## Slide 27
USB Type-C can be used to deliver power via a number of different protocols:
Precedence | Mode of Operation | Nominal Voltage | Maximum Current
Highest | USB PD | Up to 20 V | Up to 5 A
 | USB Type-C current @ 3A | 5 V | 3 A
 | USB Type-C current @ 1.5A | 5 V | 1.5 A
 | USB BC1.2 | 5 V | Up to 1.5 A
 | USB 3.1 |  | 900 mA
Lowest | USB 2.0 |  | 500 mA
Port power roles
Following the introduction of USB PD, port power roles are now defined separately from the port data roles.
Provider: device can only provide power
Consumer: device can only receive power
Consumer provider: the device can act as either a consumer or provider. This is only possible for devices that support USB PD
Capable of delivering up to 100W over one USB Type-C port!
USB Type-C power modes Flexible and modular power-delivery methods

## Slide 28: Compatible with MFi OCP
Apple® MFi OC Test standard
Iout(A)
0A
*
*
* : nominal accessory/USB charger output current.
Test conditions | 
Type-C port | 
Type-A port | 
Lighting device power during testing | > 2 V
Test conditions | 
Type-C port | 
Type-A port | 
Lighting device power during testing | > 2 V
Real-life test result with TPS25850 (Type-C)
Port A
Port B
Port A in 3A charging
Condition: Port A in stable 3A USB charging; Apply MFi OCP to Port B.
Results: Otput 5V, 3A; Port B support 4.8A @2ms pulse current, VPB_BUS is stable.
PASS MFi certification
Port A stable charging
Port B Mfi OC testing start

## Slide 29
Contents
Small solution size
03
Compatibility for different charging schemes
04
01
Automotive USB design challenge
Excellent thermal confronting warm environment
02
EMI optimization
05
How to choose: automotive USB products
06

## Slide 30
EMI optimization
05
a.
EMI basics
Design / layout tips to optimize EMI
b.
Real-life example: TPS2585x EMI optimization
c.

## Slide 31: EMI in switch-mode power supplies
Supply
Switch Mode
Power Supply
Radiated EMI
Conducted EMI
Load
$$$
EMI noise generation
EMC noise compatibility
Goal:
Early EMC consideration helps reduce test and redesign effort and cost.

## Slide 32: Two EMI tests for CISPR 25
EUT
+
AN
-
Power Supply
EUT harness
  EUT is close to the measuring apparatus – the harness is short
  Measured quantity is voltage, dBµV
Conducted testing
Measures voltage ripple on input harness
  The EUT and harness are approximately 1 m from the antenna
  Measured quantity is electric field dBµV/ m
  Over most frequencies of interest for DC/DC conversion, this is not a far field measurement
Radiated testing
Measures electric field near the EUT and harness

## Slide 33: What can we do in PCB layout? TPS25850 example
Minimize critical path area: trace A, B, C, D
  Cin as close as possible to the VIN and PGND
  Inductor as close as possible to the SW node
To ensure no breaks in the power ground, make it short and wide

## Slide 34: Critical path area comparison
Critical path area reduction – Smaller loop area, better EMI (single Cin)
Average
Peak
3 times larger loop area
smaller loop area

## Slide 35: Critical path area comparison
Critical path area reduction – Smaller loop area, better EMI (single Cin)
3 times larger loop area
smaller loop area
VOUT ripple
SW ringing

## Slide 36: Layout consideration for ground
EMI mitigation by grounding PCB L\layout –
Unbroken ground plane, shortest return path, least impedance path, better EMI
Ground plane
Top layer
ITop
IReturn
ITop
IReturn
Top layer
Ground plane
Trace or cut on the ground plane
Enclose large area
Notes: Return current path in broken ground plane enclose much larger area since the direct path is blocked
Return current path in unbroken ground plane directly under path, Area minimized, B field minimized

## Slide 37: Differential-mode EMI filter design
EMI filter selection
for 2-MHz operating
EMI filter selection
for 400-KHz operating

## Slide 38: Recommended EMI optimized layout
TPS25850 2.1 MHz EMI: CISPR25 CLASS5 PASS
TPS25858 400 KHz EMI: CISPR25 CLASS5 PASS
https://www.ti.com/tool/PMP40723
https://www.ti.com/tool/PMP40680

## Slide 39
EMI reference design
Smart thermal management
Stable operating
2.1MHz
VQFN-HR
EMI standard : CISPR 25 Class5
PMP40723 FSW = 2.2MHz PASS PMP40680 FSW = 400kHz PASS

## Slide 40: TPS25850/8: Dual-3A USB Type-C charging ports controller
Low EMI and low switching noise meet CISPR25 class 5 standard
Direct-to-VBAT connection
Supports dual 3 A Type-C
Optimizes device charging
5.5-26 V Input operating voltage range
Maximum 36 V input voltage
Integrated high-power DC/DC Buck converter, power VCONN internally
FSW: 200 KHz~ 2.4 MHz FPWM with spread spectrum
  Total efficiency
    93.4% at 2.1 MHz, 2*3 A load, 13.5 V VIN (TPS25850)
    94.5% at 400 kHz, 2*3 A load, 13.5 V VIN (TPS25858)
Selectable output voltage: 5.1V, 5.17V, 5.3V, 5.4V
Cable compensation when VBUS set to 5.17 V
USB Type-C Charging Port Control & BC1.2 DCP schemes, support Divider3 and 1.2 V/1.2 V modes
Programmable USB short current limit: ±15% accuracy over temperature
Low EMI and low switching noise
Low dropout voltage to support 5.5V input with 5.1V output
Smart thermal management:
    Thermal management with adjustable threshold
    Thermal shutdown
Package: 3.5 mm-by-4.5 mm HotRod™-25
Features
Applications
Automotive Type-C USB charging ports
USB media hubs and remote ports
Benefits

## Slide 41: TPS25852/9: Dual-3A USB Type-C charging ports controller
Low EMI and low switching noise meet CISPR25 class 5 standard
Direct-to-VBAT connection
Supports dual 3 A Type-C
Optimizes device charging
5.5-26 V input operating voltage range (Max 36 V)
Integrates high power DC/DC buck converter and power VCONN internally
FSW: 200 KHz~2.4 MHz FPWM with Spread-Spectrum
  Total efficiency
    93.4% at 2.1 MHz, 2*3 A load, 13.5V VIN (TPS25852)
    94.5% at 400 kHz, 2*3 A load, 13.5V VIN (TPS25859)
Selectable output voltage: 5.1 V, 5.17 V, 5.3 V, 5.4 V
Cable compensation when VBUS set to 5.17V
USB Type-C Charging Port Control
USB ports ON/OFF control
Programmable USB short current limit: ±15% accuracy over temperature
Low dropout voltage to support 5.5 V input with 5.1 V output
Smart thermal management:
    Thermal management with adjustable threshold
    Thermal shutdown
Fault Detection:
    VBUS OC
    Thermal shutdown
Package: 3.5 mm by 4.5 mm HotRod™-25
Features
Applications
Automotive Type-C USB Charging Ports
USB Media Hubs & Remote Ports
Benefits
TPS25852-Q1
TPS25859-Q1

## Slide 42: TPS25850/2-Q1 typical application diagram
TPS25850-Q1
26V operating voltage;
Max 36V input voltage
Switching Frequency programming
Output voltage program input; Short to GND to set 5.17V VBUS with cable comp
USB charge current limit setting; Short to GND to set 3.55A for 3A charging
External/board temp monitor, connect to a NTC thermistor
Device Enable, 11V rating, connect to VSENSE directly for automatic startup
System
load
TPS25852-Q1
Fault indication, open-drain output, asserted during fault conditions
To control the USB port B channel load switch ON/OFF. Be tied to SENSE directly to automatically turn on USB port.

## Slide 43: TPS25850-Q1 family key features
Cable compensation
Short to Ground protection
4.1ms hiccup ON
524ms hiccup OFF
Chart: ILIM: Adjustable Current Limit
| 662.6899383983573 | 1689.6858638743454 | 2095.6493506493507 | 2602.6612903225805 | 2806.3478260869565 | 3386.463798530955 | 3550
RILIM | 48.7 | 19.1 | 15.4 | 12.4 | 11.5 | 9.53 | 0
USB port in Overload Hiccup

## Slide 44
Contents
Small solution size
03
Compatibility for different charging schemes
04
01
Automotive USB design challenge
Excellent thermal confronting warm environment
02
EMI optimization
05
How to choose: automotive USB products
06

## Slide 45: TPS2585x-Q1 family overview
TPS25850-Q1 | TPS25851-Q1 | TPS25852-Q1 | TPS25858-Q1 | TPS25859-Q1
TPS25860-Q1 | TPS25862-Q1 | TPS25868-Q1 | TPS25869-Q1
C+C
A+C
TPS25854-Q1 | TPS25855-Q1
C
TPS25864-Q1 | TPS25865-Q1
A+A
BC1.2 DCP/Divider 3 mode
Fault & EN for each Port
Fault & POL for each Port
2MHz
2MHz
2MHz
2MHz
2MHz
2MHz
2MHz
Recommend FSW= 2.2MHz
2MHz
*Short to GND to set the default 2.84-A current limit for Type A port
Notes: New RTM whole Focus family for Dual USB port opps
-13 parts
-2MHz/BC1.2 DCP moder/ Fault & EN/Fault & POL
15 >$1k customer , >18Mu Backlog. Looking forward to more DIN/DWIN for Focus family

## Slide 46: All-in-one USB-C and USB-A charging port products
PN | Port Type | BC1.2 Mode(s) Supported | Fault Indication | Short to Battery protection | IEC ESD | Thermal Mgmt. | MFi OCP | fsw | Package
TPS25830A | C | SDP/CDP | Yes | Yes | Yes | n/a | Yes | 300kHz to 2.2MHz | VQFN (32) 5mm x 5mm
TPS25832A | C | SDP/CDP | Yes | No | Yes | n/a | Yes | 300kHz to 2.2MHz | 
TPS25840 | A | SDP/CDP | Yes | Yes | Yes | n/a | Yes | 300kHz to 2.2MHz | 
TPS25842 | A | SDP/CDP | Yes | No | Yes | n/a | Yes | 300kHz to 2.2MHz | 
TPS25846 | A | SDP/CDP | Yes | Yes | Yes | n/a | Yes | 300kHz to 2.2MHz | 
TPS25831 | C / A | DCP | Yes | Yes | Yes | NTC Adj. | No | 300kHz to 2.2MHz | 
TPS25833 | C / A | DCP | Yes | No | Yes | NTC Adj. | No | 300kHz to 2.2MHz | 
TPS25854 | C / A | DCP | Yes | No | No | NTC Adj. | Yes | 200kHz to 800kHz | VQFN-HR (25) 3.5mm x 4.5mm
TPS25855 | C / A | DCP | Yes | No | No | NTC Adj. | Yes | 200kHz to 3MHz | 
Single USB-C and USB-A charging port solution (DCP & CDP, integrated sync buck DC/DC)
Dual USB-C and USB-A charging port solution (DCP, integrated Sync buck DC/DC)
PN | Port Type | BC1.2 Mode(s) Supported | Fault Indication | Short to Battery protection | IEC ESD | Thermal Mgmt. | MFi OCP | Fsw | Package
TPS25850 | C + C | DCP | No | No | No | Yes | Yes | 200 kHz to 3 MHz | VQFN-HR (25) 3.5mm x 4.5mm
TPS25858 | C + C | DCP | No | No | No | Yes | Yes | 200 kHz to 800 kHz | 
TPS25851 | C + C | No | Yes | No | No | Yes | Yes | 200 kHz to 3 MHz | 
TPS25852 | C + C | No | Yes | No | No | Yes | Yes | 200 kHz to 3 MHz | 
TPS25859 | C + C | No | Yes | No | No | Yes | Yes | 200 kHz to 800 kHz | 
TPS25860 | A + C | DCP | No | No | No | Yes | Yes | 200 kHz to 3 MHz | 
TPS25868 | A + C | DCP | No | No | No | Yes | Yes | 200 kHz to 800 kHz | 
TPS25862 | A + C | DCP | Yes | No | No | Yes | Yes | 200 kHz to 3 MHz | 
TPS25869 | A + C | DCP | Yes | No | No | Yes | Yes | 200 kHz to 800 kHz | 
TPS25864 | A + A | DCP | No | No | No | Yes | Yes | 200 kHz to 3 MHz | 
TPS25865 | A + A | DCP | No | No | No | Yes | Yes | 200 kHz to 800 kHz | 

## Slide 47: Automotive USB 2.0 short-to-battery protection
Part number | VBUS | D+/D- | Current limit fixed or adj. | ILIM accuracy | Flow-through layout | OTG/client mode | Package
TPD3S716 | 1-Ch 18V Short-to-Battery | 2-Ch 18V Short-to-Battery | Adj. 0.5 – 2.1A | 10% | Yes | Yes | SSOP-16 (DBQ)
TPD3S714 | 1-Ch 18V Short-to-Battery | 2-Ch 18V Short-to-Battery | Fixed 0.6A | 20% | None | None | SSOP-16 (DBQ)
TPD3S713 | 1-Ch 18V Short-to-Battery | 2-Ch 18V Short-to-Battery | Adj. 0.05A - 0.5A | 13.5% @ 200mA | None | Yes | WQFN -20
TPD2S703 | None | 2-Ch 18V Short-to-Battery | None | None | Yes | None | DGS-10 DSK-10
TPD2S701 | None | 2-Ch 7V Short-to-VBUS | None | None | Yes | None | DGS-10 DSK-10
More training video
End Equipment

## Slide 48: USB automotive collateral and design support
Competitive Cross Reference (~4000 crosses)
Online USB University
50+ TI Designs from SEM (TIDA) and PDS (PMP)
Reference Designs
50+ TI Designs from SEM (TIDA) and PDS (PMP) on Auto USB
showcases a system implementation of various single or dual port USB Type-C/A charger.
Video Series
Video series on Auto USB
Introduce the important technical factor to consider when designing auto USB charging port
Product Portfolio
All of Q100 devices for USB power solution
provides easy-to-use USB-A and USB-C/PD charging port solution with high efficiency, low EMI, and robust protection in Automotive application

## Slide 49: Platform vision: USB auto differentiators
Ease of Use, Tools, & Training
Robust
Security & Protection
Platform Approach
System Integration & Flexibility
VCONN support: 5V@200mA
Warm / Cold Crank Load Dump Protection
Smart Thermal Management
ROM Architecture
ESD & Vbat /VBUS Protection
VBUS Cable Droop Compensation
Dynamic Port Power Management policy
Image Authentication
ROM Architecture
USB AUTO
EEPROM for flexibility & Scalability
EVM’s & Ref Designs
E2E & Application Notes
USB Academy
Comprehensive Portfolio
USB-IF Member participating in next gen USB spec.
15 + Years of Automotive USB Experience.
> 50 Q1 Released Parts, Shipped >100Mu Parts in 2020
Leader in USB & Power Management Solutions

## Slide 50: Q&A

## Slide 51
SLYP834