## Slide 1: DM388 based SOM Reference Design
For Texas Instruments

## Slide 2: Introduction
Purpose
Purpose of this document is to propose a design of SoM Solution based on Texas Instrument’s DaVinci video processor DM388 and its Carrier Card
Scope
With respect to DM388 SOM and Carrier Card, this document captures the following
  Concept
  System Block Diagram
  Design Approach
  Design Features
  Mechanical Design Approach
  Schedule and Effort
Sep-16
Mistral Confidential
2

## Slide 3
Salient Features:
  Small Form factor
  Modular Design
  Mass manufacturing capability
  Expandability
  Additional Features can be added via Carrier Cards
SoM Features

## Slide 4: DM388 SoM – Concept Diagram
DM388
SOM

## Slide 5: DM388 SoM Block Diagram
Sep-16
Mistral Confidential
5
PMIC TPS659113
DM388
DEBUG
INTERFACE
CARRIER BOARD CONNECTOR
[Two FX11LA-140P-SV and One FX11LA-68P-SV]
DDR
MMC2, UART2, McASP1
Wi-Fi MODULE
WG78 31-D0
NAND /eMMC / SPI flash
[2Gb]
ANTENNA Connector
EXPANSION SIGNALS
JTAG
UART0
I2C
+5V, 3.3V
Level Translator
TWL1200ZQCR
DDR3L
MT41K256M16TW-107 [4Gb x 16]
GPMC/MMC1/SPI
DC/DC TPS51116
Enable
+1.35V
+1.8V, 1.2V

## Slide 6: Features of DM388 SoM
SoM shall have the following components:
  Processor: DaVinci Digital Media processor DM388
  Memory:
    Two x16 DDR3L memory of 4Gb each
    NAND/eMMC Memory for storing boot images 2Gb
  Wireless Connectivity:
    Wi-Fi + BT module from Jorjin/TI
    Level translator for converting 3.3V signals from DM388 to 1.8V signals of Wi-Fi module
    UFL connector for connecting external antenna
  Power
    5V +and +3.3V from Carrier card is input to SoM
    PMIC TPS659113 generates voltages 1.2V and 1.8V and enables 1.35v DC/DC regulator TPS51116
  Expansion Connectors:
    Additional signals shall be terminated at the expansion connector for Carrier Card Interface.
Sep-16
Mistral Confidential
6

## Slide 7: DM388 SoM Over All Dimensions
Sep-16
7
48mm
60mm
NAND
DM388
WiFi
DDR3L
DDR3L
UFL conn

## Slide 8: DM388 SoM Pre Placement
Sep-16
Mistral Confidential
8
TOP SIDE
DM388

## Slide 9: DM388 SoM Pre Placement
Sep-16
Mistral Confidential
9
BOTTOM SIDE

## Slide 10: Carrier Board Design Approach

## Slide 11: Carrier Board Block Diagram
BOARD TO BOARD CONNECTOR
VIDEO AMP
PPM & REGULATORS
TO SoM & PERIPHERALS
CAMERA
USB
uSD CARD
COMPOSITE
VIDEO OUT
VIDEO IN
DC IN
LED'S
PUSH BUTTON
SDDAC
CAM
USB
MMC
JTAG AND UART
GPIO
Expansion Connectors
Spare Signals
HDMI
HDMI
PCIE x1
PCIe
ETH PHY
ETHERNET
EMAC
AUDIO
CODEC
AUDIO IN/OUT
McASP

## Slide 12: Carrier Board Dimension
Sep-16
Mistral Confidential
12
90 mm
90 mm

## Slide 13
Carrier Board Features
The features supported on Carrier boards are
  Micro USB Connector to provide Debug Support (JTAG and UART) via FTDI Chip
  Composite Video Out
  Interface Support and Connector for TI Supplied Parallel Camera LI-AR-0331A
  Audio Codec with Line In and Line Out
  Micro USB OTG connector
  Micro SD card connector
  LEDs and switches
  Expansion Connector for GPIOs and spare interface signals like GPIO, SPI, I2C, PWM, ADC, 5VCC, GND.
  DC Barrel Jack Connector for 5V Input
  Wired LAN Connectivity via Ethernet Interface
  PCIe Interface and Mini PCIe Connector
  HD Video Out via HDMI Connector

## Slide 14: SoM + Carrier Board Dimension
Sep-16
Mistral Confidential
14
SoM Carrier Board
90mm
90mm
SoM
50mm
70mm

## Slide 15: Assumptions
The board size and placement can be optimized during design phase.
Carrier board feature list shall be provided by TI.
The board to board connector shall be selected from standard supplier for easy availability with different stackup height option.
SoM's shall be supporting UFL connector for interfacing different type of external antennas.

## Slide 16: Deliverables
SOM and Carrier Board
  Schematics
  Board File
  Gerber
  Tested Proto Boards – 10 Nos
  Diagnostic Software