## Slide 1: SAR ADC Power Scaling TIPL 4601 TI Precision Labs – ADCs
Created by Reed Kaczmarek and Peggy Liska
Presented by Peggy Liska
Notes: Hello, and welcome to the TI Precision Lab introducing SAR ADC Power Scaling.
Overall, this section will cover the basic ideas of power consumption for the SAR data converter and ways to minimize it.
In this video, we will define and explain analog supply power, digital supply power, and front-end driver power.

## Slide 2: Acquisition Phase vs. Conversion Phase
Notes: Let’s begin by covering the 2 basic stages of a SAR ADC. First, the acquisition phase is when the SAR ADC allows the input signal to charge the sample and hold capacitor. This happens by closing switch 1 while switch 2 remains open. Next, the SAR ADC will enter the conversion phase. The conversion phase is where the voltage on the sample and hold capacitor is translated into a digital code. The switches swap so that S1 is now open and S2 is now closed. A generic timing diagram is shown with the following signals: chip select (CS), serial clock (SCLK), and serial data out (SDO). The acquisition phase is a passive stage where there is very little internal activity for the SAR ADC. All of the conversion and communication happens during the conversion phase.

## Slide 3: Power: Acquisition Phase vs. Conversion Phase
“Zero Power”
The majority of the power is consumed during the conversion phase
Note that not all SAR ADCs will support power scaling
Notes: Now let’s relate the acquisition and conversion phases to SAR ADC power consumption. The vast majority of the power consumption comes from the conversion phase. The acquisition phase can be termed as a “zero power” stage because the power consumption comes only from the quiescent current. The conversion phase is where the SAR ADC will consume power in order to perform both the translation from analog voltage to digital code and the digital communication. The average power, or power per cycle, is the sum of the power consumed in the acquisition phase and the power consumed in the conversion phase divided by the cycle time. It is important to note that by extending the length of the acquisition phase the average power will decrease since the cycle time will increase. A longer acquisition time will lead to a lower average power. The length of the acquisition period also has important considerations in the selection of the external amplifier driver. In short, a longer acquisition period allows for the selection of a lower bandwidth amplifier driver which will help reduce system power further. Because understanding the acquisition and conversion period is important for low power design, we will look closely at how these periods are set in different SAR architectures. Note that not all SAR ADCs will support power scaling, so be sure to look in the device datasheet for the curve that shows this relationship.

## Slide 4: Acquisition Time: Internal Conversion Clock
Conversion time is fixed due to internal conversion clock
SCLK sets data output speed only, doesn’t effect conversion / acquisition time
Slower sampling rate directly adds more time for acquisition
Examples:
ADS8881
ADS8332
Notes: The acquisition and conversion time of a SAR ADC will differ depending on the internal device design. To understand what determines the acquisition and conversion time look at the timing diagram. First, we will look at the timing for a SAR ADC with an internal conversion clock. With an internal conversion clock, the SAR conversion cycle is always a fixed amount of time. The SCLK that the user applies will only influence the speed of the data communications, not the conversion time. In this type of SAR, a lower sampling rate will increase the acquisition time since the conversion time is fixed. The diagrams shown here highlight two different timing configurations for the same device. The configuration at the top is operating at a slower sampling rate than the configuration on the bottom. The transmission rate of the data is independent of the sampling rate. In fact, the maximum communication rate is bounded by the device and the minimum communication rate is only bounded by the total cycle time.
** CLICK **
Since the conversion time is always fixed, the acquisition time is longer for the slower sampling rate. Two examples of TI SAR ADCs that operate in this manner are the ADS8881 and the ADS8332. Note that most precision SAR converters use the internal clock method for setting conversion time. This is because the internal clock will ensure a clean, low-jitter clock for the more complex conversion process in a precision SAR converter.

## Slide 5: Acquisition Time: External Conversion Clock
SCLK sets data output speed and conversion time
Increasing SCLK frequency increases acquisition time for same sampling rate
Slower sampling rate with the same SCLK frequency increases acquisition time
Examples:
ADS7042 ADS7056
Notes: Next, let’s take a look at SAR ADCs with an external conversion clock. For this type of device, the SCLK provided by the user is also used for the conversion cycle. With this method, the conversion time is set to a fixed number of SCLK periods and therefore will expand and shrink with changes in the SCLK frequency. The timing diagrams show the same SAR operating at the same sampling rate but with different SCLK frequencies.
** CLICK **
It is clear that with a faster SCLK the acquisition time will increase as shown in the top example. Increasing acquisition time is advantageous because it will allow the input signal more time to settle, which decreases the bandwidth requirement for the front end driver. Decreasing the bandwidth requirement for the amplifier will result in further power savings. Thus, for the example shown the top timing diagram is preferable as it will give the maximum settling time to the amplifier. Two examples of TI SAR ADCs that use an external conversion clock are the ADS7042 and the ADS7056. Note that this method of setting the acquisition and conversion rate is typically used in lower resolution SAR converters, for example 8 to 14 bits. As mentioned previously, the higher resolution converters typically use the internal clock to set conversion time.

## Slide 6: Acquisition Time: Other
I2C
Fixed Acquisition
Always check the datasheet for timing diagram
Fixed Acquisition Time
Examples:
ADS7924 – I2C
ADS8321 – Fixed Acquisition
Notes: Not all SAR ADCs will fall into one of these two categories for conversion clocks. For example, devices with an I2C interface will operate very differently from the devices with a SPI interface. Some of the I2C devices will have registers that the user writes to in order to set the acquisition time. Also, some of the SPI devices will have a “fixed acquisition” window. This means the device will only acquire for a fixed number of SCLK periods. The timing diagram shown is for a fixed acquisition type of device. Two examples of TI SAR ADCs with other methods for timing are the ADS7924 and the ADS8321. Note that these exceptions are not common and most devices will fall into one of the first two categories. In regards to the different types of timing diagrams, it is best to always read the device datasheet in order to fully understand how the device will operate and how to determine the acquisition and conversion times.

## Slide 7: Power of a SAR ADC
Front-End Driver Power
Analog Supply Power
Digital Supply Power
Notes: There are three main contributors to the system power of a SAR ADC.
**CLICK**
First is the analog supply power, abbreviated as AVDD.
**CLICK**
Second is the digital supply power, abbreviated as DVDD.
**CLICK**
And lastly, is the front-end driver power. These three power consumption contributors will be further explained in terms of how each one is used as well as how to reduce the power consumption in a system.

## Slide 8: Analog Supply (AVDD) Power Consumption
ADS7042
Analog Supply Power
AVDD Example Calculation:
Notes: First we will look at the analog supply power consumption. The analog supply is used for the internal conversion circuitry of the SAR ADC. The average power consumption for the analog supply will increase as the sampling rate increases. This is due to the fact that as sampling rate increases, the acquisition time decreases which results in more frequent conversion phases. The datasheet supply current versus throughput graph for the ADS7042 is shown and the linear relationship is clearly visible. In order to reduce a system’s power consumption, lowering the sampling rate to the lowest acceptable throughput for the application will decrease the average analog supply power consumption.
Using the datasheet’s supply current versus throughput graph, let’s calculate the AVDD supply power consumption.
** CLICK **
For this example, the device is running at 600kSPS. On the graph we see the typical supply current for 600kSPS is 120uA. With a 3.3V AVDD, the analog supply power for this device is 396 micro-Watts.
Note that with some devices, there will be an additional source of power consumption on the reference pin. This can be calculated in the same way as the AVDD supply power and considered as an additional source.

## Slide 9: Digital Supply (DVDD) Power Consumption
Digital supply power consumption is a function:
    DVDD Voltage
    Sampling rate
    Digital output code
    Capacitance
      Trace + Pin + External
IDVDD is the DVDD supply current
Digital Supply Power
Notes: Next we will look at the digital supply power consumption. The digital supply for a SAR ADC is only used for the digital communication circuitry of the device. This means that the digital supply power consumption is related only to the SPI or I2C output. For a SAR device with SPI communication, the power is only consumed on the digital supply for the serial data output line (SDO) and not for the chip select, serial data input, or system clock since those are all powered by the master. The power consumption is a function of the DVDD voltage, sampling rate, digital output code, and capacitance. The capacitance is comprised of the SDO trace, the SDO pins on both the ADC and the Master, and any external capacitors added to the SDO line. The equation to estimate the average digital supply current is given as the capacitance multiplied by the DVDD voltage multiplied by the frequency of transitions on the SDO output. More output transitions from low to high or high to low on the SDO line will result in more current draw. The worst case scenario from a current draw perspective is if every other bit on the SDO output alternates. The maximum number of SDO transitions for a 12-bit SAR ADC is shown in the timing diagram graphic on the right.

## Slide 10: Minimizing Digital Supply Power Consumption
Use a lower digital voltage (ex. use 1.8V logic instead of 3.3V logic)
Run the device at lowest applicable throughput
Reduce the trace capacitance of SDO line
  Analog Engineer’s Calculator can be used to determine PCB capacitance
ti.com/tool/analog-engineer-calc
Notes: Since we now understand the factors that play into the digital supply power consumption, let’s look at methods to reduce this power. First, since the digital power is a function of DVDD, lowering the DVDD voltage will allow for a lower digital supply power consumption. If the system can operate with a 1.8V logic level, then switching from a 3.3V DVDD to 1.8V DVDD will drastically decrease power consumption. Next, digital supply power consumption is proportional to throughput. By running the SAR at the lowest possible sampling rate, the average digital supply power consumption will decrease because the frequency of SDO transitions will decrease. Lastly, reducing the trace capacitance of the SDO line on the printed circuit board (PCB) will decrease power consumption. Shorter traces will have less capacitance. TI’s Analog Engineer’s Calculator has a built-in tool to calculate trace capacitance by entering the characteristics of the PCB and the trace of interest. A link to this tool is provided at the bottom of the slide.

## Slide 11: DVDD Supply Power: Example Calculation
DVDD Voltage = 3.3V
Pin Capacitance = 3 pF for both ADC and Master
SDO Trace Capacitance (2.54 cm long, 0.254 mm wide) = 1.322 pF
Sampling rate = 1 MSPS
Frequency of SDO Transitions (12 bit transitions, 1µs cycle time)
Notes: Let’s walk through a digital supply power consumption example calculation. Using the equation for DVDD current we will need the DVDD voltage, capacitance of the SDO line, and the frequency of SDO transitions. First, the DVDD voltage is easy to determine since it will be the voltage that is supplied to the part. In this example we are using 3.3V. The pin capacitance is usually available in a device datasheet or it can be estimated as 3 pF. Next, the trace capacitance can be calculated using the Analog Engineer’s Calculator by entering in your PCB characteristics, trace length, and trace width. By entering these values into the calculator we determine the SDO trace capacitance to be 1.322 pF. Lastly, we need to figure out the frequency of SDO transitions. For this example, we have a 12-bit output and with 12-bits, the worst case scenario would be for the SDO line to transition on each bit, resulting in 12 SDO transitions. The frequency of SDO transitions is determined by taking the number of transitions and dividing it by time. Since the device is operating at 1 MSPS, the cycle time is 1 micro-second. To find the DVDD supply power, we simply multiply the DVDD current by the DVDD voltage. Entering these values into the equation will give us an estimated DVDD supply power of 956.8 micro-Watts.

## Slide 12: Front-End Driver Power Consumption
Front-End Driver Power
Amplifier | Bandwidth | IQ
OPA365 | 50 MHz | 5 mA
OPA211 | 45 MHz | 3.6 mA
OPA320 | 20 MHz | 1.45 mA
TLV313 | 1 MHz | 65 µA
LPV811 | 8 kHz | 450 nA
Notes: Moving onto the third contributor to SAR ADC power consumption, we will now focus on the front-end driver. Typically an operational amplifier (op amp) is used to drive the input of the SAR ADC. This amplifier consumes power due to the quiescent current of the op amp and the op amp power supplies. Choosing an op amp to drive the SAR ADC is described in detail in the “SAR ADC Input Driver Design” Precision Labs Videos. These videos describe how to determine the bandwidth required for the front-end driver. The bandwidth required depends on the throughput of the SAR ADC. At lower throughput less bandwidth is needed to drive the SAR. Generally with op amps, as the bandwidth specification decreases, the quiescent current (IQ) also decreases. The chart in the bottom left shows some example amplifiers comparing the bandwidth and quiescent current. In order to minimize front-end driver power consumption, operating the SAR at a lower sampling rate will allow for a lower bandwidth op amp to be used, which in turn will have less quiescent current. Note that the power is calculated by multiplying the total supply voltage by the quiescent current. The front-end driver power consumption will decrease with a lower quiescent current op amp. The TI Precision Labs Op-Amp series has a video series explaining op amp bandwidth in depth.

## Slide 13: Front-End Driver Tradeoffs
Large feedback resistors will act as a small load and result in less power consumption but add more noise
A good rule of thumb is to keep the Op Amp noise dominant
TI Precision Labs - Op Amps: Noise
Notes: Going to a lower powered front-end driver does not come without a cost. As op amp quiescent current decreases, the intrinsic noise of the op amp increases at a proportional rate of 1/sqrt(Iq). This is important to keep in mind because there is a tradeoff between power and noise – so depending on what is important in your system, the amplifier should be selected appropriately. Next, the feedback resistors of an op amp circuit will result in additional power consumption. Sometimes, in order to reduce power consumption, people will use large-valued resistors in order to decrease the load current but resistor noise increases with resistance. A good rule of thumb is to keep the op amp intrinsic noise dominant compared to the resistor noise from the feedback network. The TI Precision Labs Op-Amps series has a video series dedicated to noise that goes into much more detail on this topic. Also, as amplifier quiescent current decreases, typically the slew rate will also decreases.

## Slide 14: Driving a SAR ADC without a Driver Amplifier
Low frequency voltage inputs can be connected directly to the SAR ADC
Applicable for low sampling rates (<20 kSPS)
Chart: ADS7042 + LPV811 at 1 kSPS
| With Op Amp | Without Op Amp
Op Amp | 1.8 | 0
AVDD | 0.73 | 0.73
DVDD | 0.98 | 0.98
ti.com/lit/pdf/sboa206
Notes: While most applications require a front-end driver for the SAR ADC, in some cases the circuit can be designed without the driver. This applies to low frequency voltage inputs that the user can connect directly to the input of the SAR ADC as shown in the schematic on the left. This topology is effective only for low sampling rates and there is a TI Tech Note showing a specific example of this topology with accurate measurements for 20 kSPS and lower. The link for this is shown at the bottom of the slide. The main advantage to not using a driver amplifier is the power savings. The graph shows a measured example of system power and it is clear that the Op Amp is about 50% of the total power.

## Slide 15: Power Scaling Example
Power Level | Amplifier | Sampling Rate | Measured Amplifier Power | Measured Analog Power | Measured Digital Power | Total System Power
Low | LPV811 | 1 kSPS | 1.8 µW | 0.737 µW | 0.988 µW | 3.5 µW
Medium | TLV313 | 100 kSPS | 192.7 µW | 73.1 µW | 135.8 µW | 401.7 µW
High | OPA320 | 1 MSPS | 6386 µW | 708.3 µW | 655.2 µW | 7750 µW
ADS7042
AVDD = 3.3V, DVDD = 3.3V, Op Amp Supply = 4.5V
Chart: Sampling Rate
| 1 kSPS | 100 kSPS | 1 MSPS
Op Amp | 1.8 | 192 | 6386
AVDD | 0.73 | 73 | 708
DVDD | 0.98 | 136 | 655
Chart: Sampling Rate
| 1 kSPS | 100 kSPS | 1 MSPS
Op Amp | 1.8
AVDD | 0.73
DVDD | 0.98
Notes: On this slide, an example of measured results for power scaling is shown. For this example, the system used an ADS7042 with AVDD = 3.3V, DVDD = 3.3V, an op amp supply = 4.5V, and different op amps for each sampling rate. Different op amps were used because the bandwidth requirement changes with sampling rate. The table allows you to see three different power levels, the amplifier used, and the sampling rate. The power is broken down into the 3 contributors that were explained earlier in this video: front-end driver power, analog supply power, and digital supply power. The last column combines the 3 power components to give a total system power. The power scaling is shown in the graph and the difference between 1 kSPS, 100 kSPS, and 1 MSPS is clear and drastic.
**CLICK **
If we zoom in on the 1 kSPS power measurements you can now see the 3 contributors on a smaller y-axis scale.

## Slide 16: Thanks for your time! Please try the quiz.
Notes: That concludes this video – thank you for watching! Please try the quiz to check your understanding of this video’s content.

## Slide 17: ADC System Power Scaling TIPL 4601-L TI Precision Labs – ADCs
by Art Kay, Peggy Liska
Notes: Hello and welcome to the TI Precision labs hands-on experiment covering ADC System Power Scaling. In this experiment we will use hand calculations to predict ADC system power for different amplifiers and different sampling rates. Then we will measure the system power and compare to the hand calculations.

## Slide 18: Required/Recommended Equipment
Calculation
  Calculate power for the amplifier, digital communications, and analog ADC supply
Measurement
  Short description of current shunt measurement
  Measure power for different amplifiers and sampling rates
  PLABS-SAR-EVM-PDK
  http://www.ti.com/tool/plabs-sar-evm-pdk
  Download EVM software and purchase EVM
Notes: In the last precision labs lecture we described in detail the steps involved in calculating power for different amplifiers and different sampling rates. For this lab we will quickly review and summarize this procedure. We will use hand calculations to find power for six different configurations. We will have a short discussion describing the operation of the measurement circuit. And finally, we will measure power for these circuits and compare to the calculated results.

## Slide 19: Circuits under test
OPA320 Parameter |  | Test Conditions | MIN | TYP | MAX | UNIT
GBP | Gain Bandwidth Product | Unity gain |  | 20 |  | MHz
IQ | Quiescent current | Vs=5.5V, Ta=25⁰C |  | 1.5 | 1.75 | mA
TLV313 Parameter |  | Test Conditions | MIN | TYP | MAX | UNIT
GBP | Gain Bandwidth Product | Unity gain |  | 1 |  | MHz
IQ | Quiescent current | Vs=5.0V, Ta=-40⁰C to 125⁰C |  | 65 | 90 | µA
LPV811 Parameter |  | Test Conditions | MIN | TYP | MAX | UNIT
GBP | Gain Bandwidth Product | Unity gain |  | 8 |  | kHz
IQ | Quiescent current | Vs=3.3V, Ta=25⁰C |  | 450 | 540 | nA
Notes: For this experiment we will measure three different amplifiers. Keep in mind that quiescent current is inversely proportionate to the amplifiers bandwidth. Also, wide bandwidth amplifiers are required for high sampling rates. First we will use the OPA320 for sampling rates of 1Msps and 500ksps. This amplifier has a bandwidth of 20MHz and a maximum quiescent current of 1.75mA. Next we will use the TLV313 for sampling rates of 100ksps and 10ksps. This amplifier has a bandwidth of 1MHz and a maximum quiescent current of 90uA. Finally, we will use the LPV811 for sampling rates of 1ksps and 200sps. This amplifier has a bandwidth of 8kHz and a maximum quiescent current of 540nA. In the next slide we will use this information to calculate the system power.

## Slide 20: Expected results
Amp | Sampling Rate | IQ_Amp (µA) Max | PDVDD (µW) Max | PAVDD (µW) Max | PQ_Amp (µW) Max | PTOTAL (µW) Max
OPA320 | 1M | 1,750 | 1306.80 | 690.00 | 7875.00 | 9871.80
OPA320 | 500k | 1,750 | 653.40 | 345.00 | 7875.00 | 8873.40
TLV313 | 100k | 90 | 130.68 | 69.00 | 405.00 | 604.68
TLV313 | 10k | 90 | 13.07 | 6.90 | 405.00 | 424.97
LPV811 | 1k | 0.54 | 1.31 | 0.69 | 2.43 | 4.43
LPV811 | 200 | 0.54 | 0.26 | 0.14 | 2.43 | 2.83
Notes: The table shows the calculated maximum power for all the different test configurations that we will measure. The example calculation shown is for the OPA320 500ksps case. These calculations were covered in detail in the precision labs lecture on power scaling. Let’s review the calculation. First, we calculate the digital communications power, denoted PDVDD. The digital current is calculated as C * V * Nbits * fs. Where C is the digital output line capacitance, V is the digital signal level, Nbits is the number of ADC bits, and fs is the sampling rate. This equation is really just the charge multiplied by the maximum number of transitions per second on the digital output line. Multiplying the current by VDVDD converts to power. In this case the supply is 3.3V, digital output bus capacitance is 10pF, number of bits is 12, and sampling rate is 500ksps. The digital power is 653.4uW.
PAVDD is the analog power for the ADC. It is calculated by multiplying the AVDD supply voltage by the current. The current is calculated using information from the data sheet and the sampling rate. The data sheet provides the current measured at 1Msps, and this can be scaled by the ratio of the sampling rate to 1Msps. Plugging in the numbers, you can see that analog ADC power is 345uW.
Finally, let’s calculate the amplifier power. The amplifier power is calculated by multiplying the amplifier supply voltage by the quiescent current. Notice that the amplifier power is not dependent on the sampling rate. In this example 4.5V multiplied by 1.75mA gives a power of 7.875mW. These calculations were repeated for each amplifier and sampling rate. Later, we will compare these calculations to the measured results.

## Slide 21: Supply Current Measurement Circuit
Notes: This slide shows how the EVM measures current. The ammeter, circuit circled in red at the top of the page, is used to measure the current flowing into the analog, digital, and amplifier supply. The shunt resistor converts the supply current to a voltage. Note that the shunt is jumper selectable for different current ranges. Also notice that the calibration position shorts out the INA input to allow measurement of the system offset. In the example shown the digital supply current of 197uA flows through the 20 ohm shunt resistor to develop a 3.94mV input voltage. The INA gain of 823 increases this to 3.343V. The attenuator then scales this according to the ADS1220 input requirements. The ADS1220 delta sigma converter was used as it naturally averages the input signal. Also, the filter at the input of the INA averages out transients in the current measurement. Keep in mind that the ADC conversion current is not a constant value but rather is a series of transient currents that is averaged. The same circuit shown at the top of the page is repeated for the amplifier and ADC analog channel. Finally, note that the calculations to convert the ADS1220 measurements into power values is done automatically in software.

## Slide 22: 6a: Connect the hardware
Notes: For this experiment we will be using channel 3 on the precision labs hardware. First, set the jumpers as shown here. Connect the PSI to the PLABS board using the SMA cable, and connect the PHI to the PLABS channel 3 connector. Finally, connect the USB cables to the computer. Throughout this experiment we will test different amplifiers. Always be careful to install this amplifier right side up with the label at the bottom of the coupon card. For now you can leave the amplifier socket empty. Pause and connect the hardware.

## Slide 23: Start & Setup the Plabs-Power Scaling EVM Software
1. Select “Plabs-Power Scaling” from “start>All Programs”
2. The green hardware connected and teal PSI controls indicate that communication is established.
Notes: Now start the “Plabs-Power Scaling” software. If the hardware is connected correctly you should see the green “hardware connected” indicator, and the PSI controls should be colored teal. Pause and start your software.

## Slide 24: Calibrate system offsets
1. Set Jumpers as Shown. Remove coupon card from socket. Sampling rate will be adjusted automatically.
2. Press “continue” after the hardware is configured.
Notes: Before making any power measurements we need to calibrate the system. This calibration will eliminate the offset errors from the INA and ADC, so that we can get the best accuracy. To do this press the “calibrate” button. Once you do this you will see a window pop up that shows how the jumpers need to be positioned for this test. In this case the input is set to “AC_IN”, and the jumpers are in the “CAL” position. Also, make sure that no amplifier is in the socket during this test. Press “continue” after the hardware is configured. Pause and calibrate the system.

## Slide 25: Measure OPA320 at different sampling rates
Start by measuring system power at 1Msps and 500ksps. At these sampling rates we will use the OPA320.
Change the jumpers as shown. Install the OPA320_Good_filter2 device.
Press continue to measure power at the specified sampling rate.
Notes: Now we are ready to start measuring power. First we will measure the OPA320 and ADC at high sampling rates. Press the 1Msps button to begin. This will bring up a window that shows how to set the jumpers and indicates that you need to install the “OPA320 Good Filter 2” coupon board. Make these changes in the hardware and press continue. Follow the same procedure for the 500ksps sampling rate. Pause and make these measurements.

## Slide 26: Expected results for OPA320
Your power measurements should be in the same range as these. When running at full speed power is in the hundreds of µW to mW.
Notice that the amplifier current is constant and not dependent on sampling rate.
ADC current scales with sampling rate.
Note: the ADC sampling rate, number of samples, PSI controls, and calculations are all done automatically when the buttons are pressed.
Notes: This slide shows the expected results for the OPA320. The table shows the measured currents and powers for the amplifier, ADC analog supply, and ADC digital supply. When we have completed all the measurements we will compare this to the calculated results. For now, notice that the currents are in the hundreds of uW to mW. The graph shows current versus sampling rate. Notice that the current for the amplifier is constant and not dependent on sampling rate. The ADC current, on the other hand, scales with sampling rate. Finally, note that this test automatically controlled many different parameters. For example, sampling rate, number of samples, the PSI controls, and all the calculations are automatically done in the software.

## Slide 27: Measure TLV313 at 100ksps
Start by measuring system power at 100ksps. At these sampling rates we will use the TLV313.
Notes: Now let’s change the amplifier and measure power for 100ksps. Press the 100ksps button to begin. This will bring up a window that shows how to set the jumpers and indicates that you need to install the “TLV313 low power” coupon board. Make these changes in the hardware and press continue. Pause and make these measurements.

## Slide 28: Measure TLV313 at 10ksps
Press 10ksps for the second TLV313 experiment.
Change the jumpers according to the figure below.
Notes: Let’s continue measuring the TLV313 at 10ksps. Press the “10ksps” button. This will bring up a window that shows how to set the jumpers and indicates that you need to install the “TLV313 low power” coupon board and change the jumpers. Now the amplifier jumper is in the high position but the ADC analog and digital current jumpers are in the low position. Make these changes in the hardware and press continue. Pause and make these measurements.

## Slide 29: Expected results for TLV313
Your power measurements should be in the same range as these. When running at medium speed the power is in the tens to hundreds of µW.
ADC current scales with sampling rate.
OPA320 Current
TLV313 Current
Notice that the amplifier current is constant and not dependent on sampling rate.
Notes: This slide shows the expected results for the TLV313 and OPA320. Notice that the currents are in the tens to hundreds of micro watts. The graph shows current versus sampling rate. Notice that the current for TLV313 is significantly lower than the OPA320. Again, note that the amplifier current is not dependent on sampling rate. The OPA320 was used at high sampling rates because it has a wide 20MHz bandwidth so it can achieve good settling accuracy. The TLV313 has a 1MHz bandwidth and can achieve good settling accuracy at low sampling rates. Finally, notice that the ADC current scales linearly versus sampling rate.

## Slide 30: Measure LPV811 at different sampling rates
Start by measuring system power at 1ksps and 200sps. At these sampling rates we will use the LPV811.
Notes: Finally, let’s change the amplifier and measure power for 1ksps and 200sps. Press the 1ksps button to begin. This will bring up a window that shows how to set the jumpers and indicates that you need to install the “LPV811 low power” coupon board. Note that all the jumpers are in the LOW position to measure low current. Make these changes in the hardware and press continue. Follow the same procedure for the 200sps sampling rate. Pause and make these measurements.

## Slide 31: Expected results for LPV811
Your power measurements should be in the same range as these. When running at lowest speed the power is in the hundreds of nW to µW range.
ADC current scales with sampling rate.
OPA320 Current
TLV313 Current
Notice that the amplifier current is constant and not dependent on sampling rate.
LPV811 Current
Notes: Now we have completed all the experiments. At low sampling rates the power levels are in hundreds of nano-watt to micro-watt. This is thousands of times smaller then at full sampling rate. You can clearly see the linear current scaling versus sampling rate for the ADC. Also, you can clearly see that the current is constant for each different amplifier. Comparing the measured amplifier current to the data sheet, shows that this current is the expected amplifier quiescent current.

## Slide 32: Compare final test results to calculated values
Select the “Power” cells in the measured table. Right click and “Export Data to Excel”.
Notes: To compare the measured results to the calculate results you should export the data to Excel. To do this highlight the power cells in the GUI table and right click. Select “Export Data to Excel”. This will cause an Excel spreadsheet to pop-up with the measured data. Now we can paste this into our table for comparison. Pause and export the data to Excel.

## Slide 33: Measured vs Expected Results
Your results should show the same trend as the expected result but the specific values will differ.
 |  | Calculated |  |  |  | Example Measurements |  |  | 
Amp | Sampling Rate | PDVDD (µW) Max | PAVDD (µW) Max | PQ_Amp (µW) Max | PTOTAL (µW) Max | PDVDD (µW) | PAVDD (µW) | PQ_Amp (µW) | PTOTAL (µW)
OPA320 | 1M | 1306.80 | 690.00 | 7875.00 | 9871.80 | 639.57 | 645.08 | 6461.89 | 7746.53
OPA320 | 500k | 653.40 | 345.00 | 7875.00 | 8873.40 | 282.36 | 321.95 | 6468.08 | 7072.39
TLV313 | 100k | 130.68 | 69.00 | 405.00 | 604.68 | 57.75 | 64.10 | 177.09 | 298.94
TLV313 | 10k | 13.07 | 6.90 | 405.00 | 424.97 | 6.67 | 6.50 | 176.94 | 190.11
LPV811 | 1k | 1.31 | 0.69 | 2.43 | 4.43 | 0.38 | 0.64 | 1.81 | 2.83
LPV811 | 200 | 0.26 | 0.14 | 2.43 | 2.83 | 0.06 | 0.13 | 1.81 | 2.00
Notes: This table compares the calculated result to the measured results. Here the example measurements are pasted in. It is important to note that the calculated results use data sheet maximum values, so you should expect that the calculated results are larger than the measurements. A quick review of the data shows that the measurements are smaller than the calculated maximum as expected. Nevertheless, you can see that the calculated and simulated results are in the same range and the measured trends match the calculated trends. Also, notice that the amplifier current is only dependent on the amplifier type and not on the sampling rate. Finally, notice the profound impact that changing the sampling rate has on total power. At full sampling rate the total power is 7746uW, and at 200sps the power is 2uW.

## Slide 34: 6b: Measured vs Expected Results
 |  | Calculated |  |  |  | Your Measurements |  |  | 
Amp | Sampling Rate | PDVDD (µW) Max | PAVDD (µW) Max | PQ_Amp (µW) Max | PTOTAL (µW) Max | PDVDD (µW) | PAVDD (µW) | PQ_Amp (µW) | PTOTAL (µW)
OPA320 | 1M | 1306.80 | 690.00 | 7875.00 | 9871.80 |  |  |  | 
OPA320 | 500k | 653.40 | 345.00 | 7875.00 | 8873.40 |  |  |  | 
TLV313 | 100k | 130.68 | 69.00 | 405.00 | 604.68 |  |  |  | 
TLV313 | 10k | 13.07 | 6.90 | 405.00 | 424.97 |  |  |  | 
LPV811 | 1k | 1.31 | 0.69 | 2.43 | 4.43 |  |  |  | 
LPV811 | 200 | 0.26 | 0.14 | 2.43 | 2.83 |  |  |  | 
Notes: Now you can paste your measured results into the table. You should confirm that your results are in the same range as the hand calculations. Pause and paste your results into the table.

## Slide 35
Thanks for your time!
Notes: That concludes the hands-on experiment. I hope this was useful to you. Thanks for your time.