## Slide 2: Agenda
Introduction
  Autonomous Robots
  Functional Safety for Robotics
  TI technologies serving Autonomous Robots
Autonomous Mobile Robots (AMR)
  AMR sensing challenges
  TI mmWave sensors for AMR
  Accelerate sensor fusion with TI Jacinto™ 7 processors
Getting started
Notes: Welcome everyone. As Sam mentioned, I am a product marketing engineer with Jacinto Processors Business in Texas Instruments, responsible for all Edge AI applications, including Robotics.
In this presentation today, I will cover
  Introduction of Autonomous Robots, Functional Safety for Robotics, TI technologies serving Autonomous Robots
  Followed by that Jitin will cover challenges with AMR sensing need, and will introduce the differentiation TI mmWave sensors brings to AMR sensors, and after that I will introduce Jacinto Processors for accelerated vision and sensor fusion for safe, efficient robots.

## Slide 3: Autonomous Robots
Notes: An autonomous robot (AMR) is any robot that can navigate in an unstructured environment with a higher level understanding. While a relatively young technology, they have already branched off into a number of distinct varieties in factories, warehouse, cities and home helping with ease of human life.

## Slide 4: Autonomous Mobile Robots
Sense
Perceive & Plan
Act
Proximity
Visuals
Contact
GPS
Internal
Where Am I?
What are the objects around me?
How do I get there?
Motor Control, break, throttle
Sensors
Notes: Autonomy requires that the Robots are able to -
Sense the environment, perceive the environment to localize itself in the map, detect dynamic obstacles around, track them, plan the route to reach the goal and control the vehicle to follow that plan. Act only when it is safe to do so, avoiding situations that pose a risk to human safety, property or the autonomous system itself
Sense the environment and keep track of the system’s current state
Perceive and understand disparate data sources to localize itself in the map and detect dynamic obstacles around
Determine what action to take next and make a plan
Act only when it is safe to do so, avoiding situations that pose a risk to human safety, property or the autonomous system itself

## Slide 5: Autonomous Mobile Robots
Sense
Perceive & Plan
Act
Proximity
Visuals
Contact
GPS
Internal
Where Am I?
What are the objects around me?
How do I get there?
Motor Control, break, throttle
Sensors
Functional Safety
Functional Safety
Functional Safety
Notes: As these robots are working in closer proximity to humans than ever before, the need for them to be not only autonomous mobile, intelligent and energy-efficient, but functionally safe is critically important.

## Slide 6: Autonomous Mobile Robots
Sense
Perceive & Plan
Act
Proximity
Visuals
Contact
GPS
Internal
Where Am I?
What are the objects around me?
How do I get there?
Motor Control, break, throttle
Sensors
TDA4VM
AM6442
HerculesTM MCU
IWR6843
IWR1843
DRA821
Functional Safety
Functional Safety
Functional Safety
Notes: TI products ranging from sensing, processing and control need help system integrators meet the rigorous requirements of functional safety standards, such as ISO 26262 and IEC 61508

## Slide 7: TI Engineering expertise for functional safety
Decades of safety engineering expertise
Industry leadership as a participant in IEC 61508 and ISO 26262 standards organizations
R&D processes enabling up to ASIL-D and SIL-3 systems
Tools and expertise to simplify part selection
Functional safety-compliant products leverage our TÜV SÜD-certified hardware and software development processes.
Notes: Texas Instruments has been developing processors for functional safety in industrial and automotive applications for years with products such as our Hercules microcontroller line or TDA automotive processors. We have worked with industry leading safety experts to develop the internal processes necessary to achieve the highest safety integrity levels for systematic faults and have developed the types of features, diagnostics, and tools necessary to help system integrators implement all sorts of safety application. TI’s expertise extends beyond the processors we will be talking about here today to include power, analog, and signal chain components to enable functionally safe systems. We have leveraged this expertise to bake in safety from the ground up on the new families of radar and processors we’ll be discussing today.

## Slide 8: Autonomous Mobile Robots Sensing
Sense
Perceive & Plan
Act
Proximity
Visuals
Contact
GPS
Internal
Where Am I?
What are the objects around me?
How do I get there?
Motor Control, break, throttle
Sensors
TDA4VM
AM6442
Hercules
IWR6843
IWR1843
DRA821
Functional Safety
Functional Safety
Functional Safety

## Slide 9: Why sensors are so important for robots …and humans
!
!

## Slide 10: Autonomous Mobile Robot challenges
Stereo Camera or
3D TOF
TI mmWave Radar
Ultrasonic
LiDAR
  Safer human presence detection (LIDAR, Radar)
  Mapping and localization (Stereo camera / LIDAR / Ultrasonic/Radar)
  Collision avoidance (Stereo Camera / LIDAR / Ultrasonic / Radar)

## Slide 11: AMR Sensing with TI mmWave Radar Sensors
Complement or displace established sensor solutions with SIL 2 capable TI mmWave sensors that can solve the most challenging AGV and AMR sensing problems including safe human presence detection and autonomous navigation
TI mmWave features | Robotics Benefits
3D presence detection | True 3D information (range, velocity & angle) of objects vs. LIDAR/ToF used mainly for distance measurement Quickly detect and prevent possible collisions minimizing machine downtimes
IEC 61508 SIL 2 targeted | Enable safe human presence detection that has traditionally been solved by expensive safety certified LiDAR sensors
Accurate glass detection | Ensure reliable detection of glass walls/doors over existing sensors that “see” through them
Wide azimuth area coverage | Create 360 degree detection zones around the robot to prevent collisions with humans to minimize injury and reduce machine downtimes
Robust in challenging environments | Increase reliability over existing vision/LiDAR based sensors in conditions such as rain, dust, smoke, complete darkness or in the glare of sunlight
Sense and Avoid - Collision Avoidance
Detect humans/obstacles and navigate around them to avoid collisions
360° Safety Bubble - Safe Human Presence Detection
Slow down and stop the robot when human is detected within safety bubble. Robot resumes only when human is out of safety bubble

## Slide 12: TI mmWave Sense & Avoid Demo for AMRs
12
 | Sense and avoid [IWR6843] | Sense and avoid [IWR1843]
Tuning range | 60-64 GHz. | 77-81 GHz.
Offering | TIDEP – 01006 / TIREX Lab | TIREX Lab: Sense & Avoid
HW / EVM | IWR6843 ISK | IWR1843 BOOST
Field of View | 120° Horizontal, 30° Vertical | 120° Horizontal, 30° Vertical
Max Range (Resolution) | 10m (0.047m) | 10m (0.047m)
Get started with mmWave for Robotics
TIDEP- 01006: Autonomous Robotics using mmWave and Sitara processor
Discover mmWave offering for robotics here
Evaluate the performance
  IWR6843 ISK
  IWR1843 BOOST
  Sense and Avoid Lab [IWR6843 and IWR1843]
  Detecting walls of different materials experiment
3. Design custom boards with IWR6843 silicon
  Online datasheet & other technical documents
  Hardware design checklist
Enhanced workplace safety with collision avoidance even in the most challenging environmental conditions
  Watch AMR Collision Avoidance use case video

## Slide 13
 | 360 Degree Safety Bubble [IWR6843]
Tuning range | 60-64 GHz.
Offering | TIREX Lab
HW / EVM | 4x IWR6843 ISK
Field of View | 360° Horizontal, 30° Vertical
Max Range (Resolution) | 10m (configurable) (0.047m)
Warning Zone (Slow Down) | 2m (configurable)
Danger Zone (Stop) | 1m (configurable)
Discover mmWave offering for robotics
Evaluate the performance
  IWR6843 ISK
  360º Safety Bubble performance video
  360º Safety Bubble with ROS Lab
  360° Safety Bubble Lab FAQ
3. Design custom boards with IWR6843 silicon
  Online datasheet & other technical documents
  Hardware design checklist
Accelerate path to production with 3P solutions
  Industrial mmWave third-party search tool
TI mmWave 360° Safety Bubble Offering for AGVs/AMRs
Danger Zone (Stop)
Warning Zone (Slow down)
Ensure worker safety with 360° human presence detection and collision avoidance even in the most challenging environmental conditions
  Watch 360° safety bubble performance video
Get started with mmWave for Robotics
TIREX - Lab: 360° Safety Bubble with ROS using mmWave

## Slide 14: Which sensors should I use for my robot?
Good Fair Poor | Human | LIDAR | Radar | 2D Camera | 3D Camera | Sensor Fusion
Object detection |  |  |  |  |  | 
Object classification |  |  |  |  |  | 
Range of visibility |  |  |  |  |  | 
Distance estimation |  |  |  |  |  | 
Object edge precision |  |  |  |  |  | 
Detect transparent surfaces |  |  |  |  |  | 
Functioning in poor lighting |  |  |  |  |  | 

## Slide 15: Autonomous Mobile Robots Processing
Sense
Perceive & Plan
Act
Proximity
Visuals
Contact
GPS
Internal
Where Am I?
What are the objects around me?
How do I get there?
Motor Control, break, throttle
Sensors
TDA4VM
AM6442
Hercules
IWR6843
IWR1843
DRA821
Functional Safety
Functional Safety
Functional Safety
Notes: The benefits vision sensor provide to the table to solve this challenging problem of localization and obstacle detection & avoidance are
high resolution spatial coverage
Ability to not only detect the objects, extract features from it but also classify them. Advancement in vision based deep neural network technology makes it possible to solve such complex problems using neural network methods
One of the biggest benefit it brings to the table is they are cost-efficient, compared to other sensors like Lidar,
Down side is they are computation intensive. As these robots are energy constrained, and CPUs and GPUs are power hungry, desire is to keep CPU/GPU based processing to minimum.

## Slide 16
Safety MCU
CAN-FD
LIN
Boot Flash
SPI
DDR
Radar/ LIDAR
MCU
Ethernet Switch
PCIe
Image Sensor
Applications Processor
GPU (analytics)
General
compute
Typical Architecture
ISP
PCIe
GPU (analytics)
ISP
Ethernet Switch
General
compute
Safety MCU
MCU
disparity
JacintoTM 7 TDA4x Platform
Highly-integrated scalable family of processors: Purpose built for smart, safe, energy-efficient & cost-effective edge applications
LPDDR4
Multi-core A72
DSP
PCIe Switch
Deep Learning Accelerator
Ethernet Switch
Large internal memory,
High-BW bus
Imaging & Vision accelerators
ISP | LDC | MSC
Jacinto™ TAD4x
Depth and Motion accelerators
MCU
Safety MCU
Notes: That’s where we introduce you TI’s Jacinto 7 platform. Highly-integrated, scalable family of processors with heterogenous architecture purpose built for smart, safe, energy-efficient & cost-effective edge applications with vision processing and sensor fusion.
In a typical architecture, application processor comprises of CPU and GPU for compute. Rest all other components such as ISP, disparity, MCU and PCIe Ethernet switches are external to the processor, making it complex and unoptimized for system & cost. In Jacinto-7 TDA4x devic, we integrated all these components in one single SoC, along with class-leading deep learning accelerator, powerful computer vision accelerators and while doing all these, designing the SoC bottoms up keeping functional safety in mind .

## Slide 17
Main domain: SIL-2
Compute intensive task @ Low-power, low-latency
\
4x PCIe
2x USB
8p Eth Switch
2x CSI-2
32 virtual channels
TDA4VM Processor
Vision accelerators: VPAC, 720 MP/s
8x 2MP / 2x 8MP @ 30 fps
ISP
Image
Rectification
Multi-Scaling
Depth & Motion Accelerator: DMPAC
Multiple cameras, up to 2 MP
Stereo Depth Estimation
90 MP/s
Dense Optical Flow
150 MP/s
TI DSP: C66x
FFTs
Localization key-tasks
Image processing
Deep Learning C7x MMA: 8TOPS
Low-latency, high throughput
Higher level task
Dual-core Cortex-A72
25K DMIPS
Sensor fusion
Planning
ARM
Cortex A7x
48k/32K each
Arm
Cortex A7x
48k/32K each
1M shared L2
Mapping
Power & FFI Isolation
Robust processing
2x Dual-core R5
Lockstep 4K DMIPS
Arm
Cortex R5F
32K/32K L1
64KB RAM
Arm
Cortex R5F
32K/32K L1
64KB RAM
Lock Step
0.5 MB SRAM
Arm
Cortex R5F
32K/32K L1
64KB RAM
Arm
Cortex R5F
32K/32K L1
64KB RAM
Lock Step
0.5 MB SRAM
Robustness through redundancy
Safety
Dual-core R5
Lockstep 2K DMIPS
MCU domain:SIL-3
Arm
Cortex R5F
32K/32K L1
64KB RAM
Arm
Cortex R5F
32K/32K L1
64KB RAM
Lock Step
Hardware Diagnostics
CRC
RTI
ESM
DCC
BIST
1 MB SRAM
Robustness through redundancy
Jacinto TDA4x for Autonomous Robots
Notes: First processor in family, TDA4VM
Heterogeneous cores
efficient hardware accelerators
high-bandwidth memory architecture enable class-leading low-power performance

## Slide 18
TDA4x Processor enable smart, safe, energy efficient & cost-effective Robots
Efficient DL
More FPS/TOPS/W
&
Accelerated CV
Low-power, low-latency & robust hybrid vision perception
Localization
Obstacle detection
Mono Camera
Stereo Camera
Energy-efficient
Where Am I?
What, where and how far are the objects around me?

## Slide 19
TDA4x Processor enable smart, safe, energy efficient & cost-effective Robots
Efficient DL
More FPS/TOPS/W
&
Accelerated CV
Low-power, low-latency & robust hybrid perception & navigation
Localization
Obstacle detection
Mono Camera
Stereo Camera
Energy-efficient
Safer
SIl-3/SIL-2 complaint* SoC
Lock-Step R5s
Redundancy w/ CV & DL
Radar
Other sensors
Cost-effective
Highly integrated SoC, single DDR instance
e-stop
Lidar
* Final certification pending
Where Am I?
What, where and how far are the objects around me?
Navigate safely
Notes: Heterogeneous cores
efficient hardware accelerators
high-bandwidth memory architecture enable class-leading low-power performance

## Slide 20: Deep Learning programming with open source RunTimes
Model Compilation
Post-training quantization
Calibration
Accelerated Inference
Model Training
TI Model Zoo
Optional: Quantization Aware Training tool
Neural Network accelerator
Optimal DDR utilization
C++
Neo-AI-DLR
Now
Now
Mar-end
Accelerated inference for large number of popular models
Programming experience of CPU, system benefit of specialized accelerators

## Slide 21: Processor SDK Robotics developers tools
V4L2
Multimedia
Hardware Accelerated
Linux Sensor Drivers
CSI-2 V4L2 Capture
CAN-FD
EMAC
PCIe
…
Deep Learning
Hardware Accelerated
TIDL Lib
MMA Lib
Vision Library
Hardware Accelerated
MSC
LDC
ISP
SDE
DOF
NF
Graph-level library
Full Stack
Ubuntu Docker Container
Docker Engine
Middleware Framework
Facilitates hardware acceleration and heterogenous execution
TFLite RT
ONNX RT
TVM / Neo-AI-DLR
Deep Learning
Open source framework
OpenCV
Computer Vision
March-21
June-21
March-21
Foundational components
Developers environment

## Slide 22: Processor SDK Out-of-box Robotics applications
Object Detection
Image Classification
Hardware accelerated
Hardware accelerated
Semantic Segmentation
Stereo Disparity
SemSeg + Stereo Obj Detect
Visual Localization
Simultaneous execution of Multiple model
8x 2MP @ 30 fps image processing
Object Detection
(Resolution 512x512)
Object Detection
(Resolution 512x512)
Semantic Segmentation (Resolution: 768x384)

## Slide 23: Accelerated DL and CV based Localization demo
Feature detector and Descriptor
Mono camera Localization w/ accelerated DL & CV
DKAZE
Enc + Dec
n/w
Thresholding & 3x3NMS
PnP Pose Estimation
Post Filtering
2D – 3D matching
3D Sparse Map
Upsampling + Sparse Conv
High resolution
Score
Low resolution
Descriptor
High resolution Sparse
Descriptor
DL accelerator
DSP
TDA4VM Resource loading
A72: | 1% | C7x+MMA: | 12%
1xR5: | 6% | C6x: | 45%
5xR5s: | free | DDR BW: | 8%
Mono camera 768x384 @ 30 fps, localization average error 10.6 cm
DKAZE: Deep Learning based descriptor
Learn more about the demo in Processor SDK user guide
Input image
Notes: Two Way Descriptor Matching: Two direction matching between sparse 3D map and computed descriptors:
Sparse Up-sampling: up-sampling on the sparse points selected by key point detector using nearest neighbor resizing, applies 7x7 filtering on the resized data.
Recursive NMS: scores plane buffer thresholding, and then 3x3 NMS is performed on thresholded score buffer.
Perspective N Point Pose estimation, a.k.a. SolvePnP: 6 DOF camera pose

## Slide 24: Accelerated DL and CV based 3D Obstacle detection demo
VPAC
DMPAC
C7MMA
A72
C66
TDA4VM
Hardware-Accelerated Stereo pipeline
Disparity Refinement
(C71x)
Stereo HWA
(DMPAC)
ZED Stereo Camera YUV 422 1280 × 720 (L + R) @ 30 fps, USB 3.1
Stereo Rectification
(LDC Mesh)
L
R
Stereo Depth Engine (SDE) produces 192 disparities @ 80 MP/sec
VectorNav VN-200 GPS + IMU, UART-to-USB
Mapping & Obstacle Detection
3D Point Cloud Mapping
(ARM A72)
2D Occupancy Grid Mapping
(ARM A72)
Class-Aware Connected Component Analysis
(ARM A72)
Safety Bubble Establishes 4.5m safety perimeter surrounding robot
Ego-Centric Occupancy Grid Map
ROS PC
OG Map Display
(x86)
ROS Rviz Visualization
(x86)
Pre-Processing
Semantic Pixel Labeling
(x86)
3D Object Localization
(x86)
X86
Safety Bubble
Stereo Safety Hazard Detection
(ARM A72)
Fuse Deep Learning & Conventional Stereo Vision for Robust Detection
C7 DSP (80 GFLOPs) with MMA (8 TOPs) accelerates deep learning and signal processing
Semantic Segmentation
(C7-MMA)
Deep Learning Pipeline
NV12RGB (C66x)
Resize 
(MSC0)
Learn more about the demo building blocks here

## Slide 25: TI Processors unified software platform
100% code
compatibility
Safety
Security
System Performance
Common to all TI processors and hardware
Built on common foundation of drivers, frameworks, libraries/codecs, and development tools
Industries best mainline LINUX support
Quarterly updates to SDK
Enables customers and 3P partners on all operating systems
NRE-free and royalty-free software!
Extensive support on e2e.ti.com

## Slide 26: Explore Robotics Applications With TI Today
mmWave Radar
Evaluation Modules
Reference examples / Labs
Accelerate path to production with 3P
IWR6843 ISK (60 GHz)
IWR6843 AOP (60 GHz Antenna on Package)
IWR1843 BOOST (77 GHz)
Sense and Avoid Lab for Collision Avoidance
360º Safety Bubble with ROS Lab for Safe Human Presence Detection
Designing TI mmWave made easier using 3rd party ecosystem
Industrial mmWave third-party search tool
TDA4VM
Full development
Turn-key designs
Software development kits
http://www.ti.com/tool/TDA4VMXEVM
Automotive version of TDA4V Mid
http://www.ti.com/tool/D3-3P-TDAX-DK
TI Processor SDK – Seamlessly reuse and migrate Linux software across TI processors
http://www.ti.com/tool/PROCESSOR-SDK-DRA8X-TDA4X
Free Support on e2e.ti.com

## Slide 27: Getting started with DRA821
Product
Evaluation Module
Software development kits
https://www.ti.com/product/DRA821U
SOM: https://www.ti.com/tool/J7200XSOMXEVM
CP Board: https://www.ti.com/tool/J721EXCPXEVM
TI Processor SDK – Seamlessly reuse and migrate Linux software across TI processors
https://www.ti.com/tool/PROCESSOR-SDK-J7200
Free Support on e2e.ti.com

## Slide 28
Getting started with AM6442
GPNs
AM6442
2x A53, 4x R5F
Pricing
Starting at $6.95
AM6441
1x A53, 4x R5F
AM6421
1x A53, 2x R5F
AM6412
2x A53, 1x R5F
AM6411
1x A53, 1x R5F
Target Markets
Servo drives
PLCs
Remote I/O modules
Communication modules
I/O Link Master modules
Gateways
Industrial robots
Automated machinery
Key content
Motor control demo (AM64x + F2800x) (video link)
AM64x overview technical article here.
AM64x benefits in Remote IO technical article
Refreshed motor drives and TSN white papers
Evaluation boards
EVM
Part#: TMDS64GPEVM
Price: $299
Description: Designed for industrial networking & control and evaluating main device interfaces
On ti.com:1/29/21
Notes: File name: AM64x Family Overview.pptx

## Slide 29
Hercules™ MCUs
Scalable Platform For Functional Safety Applications
Production
External certification: ISO 26262, IEC 61508
Documentation: Safety Manual, FMEDA reports
Software: Drivers, libraries, RTOS, Autosar, tools, debug
Development Kits: LaunchPad, HDK, SafeTI CSP, SafeTI CQK
RM41L2
80MHz
128kB Flash
32kB RAM
100p QFP
RM42L4
100 MHz
384kB Flash
32kB RAM
100p QFP
RM46L8
220 MHz
1.2MB Flash
192kB RAM
144p QFP
337p BGA
RM48L9
220 MHz
3MB Flash
256kB RAM
144p QFP
337p BGA
RM57L
330 MHz
4MB Flash
512kB RAM
337p BGA
RM48L7
200 MHz
2MB Flash
256kB RAM
144p QFP
337p BGA
RM44L9
180 MHz
1MB Flash
128kB RAM
100p QFP
144p QFP
RM44L5
180 MHz
768K Flash
128kB RAM
100p QFP
144p QFP
570LS03
80 MHz
256kB Flash
32kB RAM
100p QFP
570LS04
80 MHz
384kB Flash
32kB RAM
100p QFP
570LS07
160 MHz
768kB Flash
128kB RAM
100p QFP
144p QFP
570LS02
80 MHz
128kB Flash
32kB RAM
100p QFP
570LS09
160 MHz
1MB Flash
128kB RAM
100p QFP
144p QFP
570LS12
180 MHz
1.2MB Flash
192kB RAM
144p QFP
337p BGA
570LS31
180 MHz
3MB Flash
256kB RAM
144p QFP
337p BGA
570LC43
300 MHz
4MB Flash
512kB RAM
337p BGA
Compatible 100-pin QFP package
Compatible 337-pin BGA, 144-pin QFP package
Notes: Family of safety MCUs built on more than 20 years of experience with automotive applications like braking and airbag controllers. Hercules MCUs provide a large scalable platform with devices starting at 128K of Flash up to 4MB of Flash and performance options from 80MHz up to 330MHz. Devices in the same package type are pin compatible and all devices based on the ARM Cortex-R CPU and use the same peripherals. In addition Hercules provides the necessary safety documentation, tools and software to make developing functional safety applications easier.

## Slide 30
Hercules Training – Online Resources
To access them : https://training.ti.com/hercules
Functional safety 4-part training series:
https://training.ti.com/functional-safety

## Slide 31: Hercules Support – Online Resources
Hercules Web Page: www.ti.com/hercules
  Data Sheets
  Technical Reference Manual
  Application Notes
  Software & Tools Downloads and Updates
  Order Evaluation and Development Kits
Engineer 2 Engineer Support Forum:
www.ti.com/hercules-support
  News and Announcements
  Ask Technical Questions
  Search for Technical Content

## Slide 32
©2021 Texas Instruments Incorporated. All rights reserved.
SLYP748